## Slide 1: How well can European radars detect supercells and tornadoes?
Bram van ‘t Veen
Pieter Groenemeijer
Tomáš Púčik

## Slide 2: Radars in Europe
* radar sites that ESSL has access to permanently or for case studies
*

## Slide 3: The ESSL Radar Displayer
Technical
Maplibre ensures quick GPU-based data rendering
Custom WebP-based data format for fast compression and decoding
Data requests in 1 or 2 hour chunks speeds it up further
VIDEO SHOWING CAPABILITIES AND SPEED COMES HERE

## Slide 4: Doppler quality in Europe
They can be varied by changing the Pulse Repetition Frequency
Using 2 PRFs (dual or staggered PRF) can extend vNyquist
A radar's range rmax and the maximum velocity it can measure vNyquist can be varied at each other‘s expense
Their product is a constant:
= C =
speed of light
radar wavelength

## Slide 5: Doppler quality of Europe's C-band radars
Radial velocity
Reflectivity
Different radar configurations in Europe
Varying doppler quality: “pretty good” to “unusable”

## Slide 6: Doppler quality of Europe's C-band radars
Radial velocity
Reflectivity
Different radar configurations in Europe
Varying doppler quality: “pretty good” to “unusable”
dual PRF with few errors

## Slide 7: Doppler quality of Europe's C-band radars
Radial velocity
Reflectivity
Different radar configurations in Europe
Varying doppler quality: “pretty good” to “unusable”
dual PRF with many errors

## Slide 8: Doppler quality of Europe's C-band radars
Reflectivity
Aliasing errors always occur for single & dual PRF configurations
Important corrections are possible, if number of errors is small
Radial velocity

## Slide 9: Doppler quality of Europe's C-band radars
Reflectivity
Aliasing errors always occur for single & dual PRF configurations
Important corrections are possible, if number of errors is small
Radial velocity
(corrected)

## Slide 10: Doppler quality of Europe's C-band radars
Reflectivity
Aliasing errors always occur for single & dual PRF configurations
Important corrections are possible, if number of errors is small
Radial velocity

## Slide 11: Doppler quality of Europe's C-band radars
Reflectivity
Aliasing errors always occur for single & dual PRF configurations
Important corrections are possible, if number of errors is small
Radial velocity
(corrected)

## Slide 12: Doppler quality of Europe's C-band radars
Reflectivity
Aliasing errors always occur for single & dual PRF configurations
Important corrections are possible, if number of errors is small
Radial velocity

## Slide 13: Doppler quality of Europe's C-band radars
Reflectivity
Aliasing errors always occur for single & dual PRF configurations
Important corrections are possible, if number of errors is small
Radial velocity
(corrected)

## Slide 14: Ranking of radar configurations for circulation detection
Used historical tornado cases
Subjectively ranked appearance on radar
Assigned grades (0 – 10) to 5 aspects:
  Time resolution
  Spatial resolution
  Presence of excessive filtering
  Available elevation angles
  Number of aliasing errors

## Slide 15: Main suggestions for improvement
Filtering:
Don’t filter velocity based on signal quality
Prevent too agressive clutter filtering
Reliable velocity data:
Use dual PRF, optimally with a 3:2 PRF ratio
Ensure the high Nyquist velocity = 15 m/s or higher
QR-CODE 2 COMES HERE
Our poster “Ranking the radars”

## Slide 16
Combines Z, ZDR, and CC ( = RhoHV )
Helps judging collocation of signatures
Polarimetric RGB
CC

## Slide 17: Polarimetric RGB: C-band
15 minutes before 19 cm hailstone in Italy
RGB
Data: ARPA-FVG
Reflectivity
Photo: Tornado in Italia – Marilena Tonin
Our poster on the RGB

## Slide 18: Thank you!
Acknowledgements:
The weather services that provided data as Open Data or for research/education use
ESWD volunteers to collocate the radar data with storm reports
Dr Matthew Kumjian (Penn. State) for assisting us with interpreting polarimetric radar data
All participants to Radar Workshop in Dec 2024 and the 2025 ESSL Testbeds for their feedback
Veillette et al (2023) for the their “Deep Learning–Based Velocity Dealiasing“ post-processing algorithm that we used in sequence with our own algorithm
Access to the Radar Displayer and Weather Data Displayer can be licensed from ESSL Services GmbH