## Slide 1
Gabriele Coccia(1)(2) and Ezio Todini(1)(2)
(1)University of Bologna, Bologna, Italy
(2) Idrologia e Ambiente s.r.l, Napoli, Italy
Probabilistic flood forecasts within a time horizon

## Slide 2
Emergency managers deal with a big uncertainty about the evolution of the future events,
This uncertainty must be quantified in terms of a probability distribution
  Developing Predictive Uncertainty Processors that try to answer to the emergency managers questions, providing them a basis on which take their decisions
THE NEED FOR PROBABILISTIC FORECASTS
WITHIN A TIME HORIZON

## Slide 3
Which is the probability that the river dykes will be exceeded within the next 24 hours?
Which is the probability that the water level will be higher than the dykes one at the hour 24th?
Which is the probability that the river dykes will be exceeded exactly at the hour 24th?
THE NEED FOR PROBABILISTIC FORECASTS
WITHIN A TIME HORIZON

## Slide 4
3) Predictive Uncertainty is obtained by the Bayes Theorem
4) Reconversion of the obtained distribution from the Normal Space to the Real Space using the Inverse NQT
1) Conversion from the Real Space to the Normal Space using the NQT
2) Joint Pdf is assumed to be a Normal Bivariate Distribution (or 2 Truncated Normal Distributions)
Todini, E.: A model conditional processor to assess predictive uncertainty in flood forecasting, Intl. J. River Basin Management, 6 (2), 123-137, 2008.
G. Coccia and E. Todini: Recent Developments in Predictive Uncertainty Assessment Based on the Model Conditional Processor Approach, HESSD, 7, 9219-9270, 2010
Image of the forecasted values
Joint and Conditioned Pdf
Image of the observed values
a
a
BI-VARIATE
UNI-VARIATE
UNIVARIATE
MODEL CONDITIONAL PROCESSOR: BASIC CONCEPTS

## Slide 5
THE BASIC PROCEDURE CAN BE EASILY EXTENDED TO MULTI-MODEL CASES
N+1-VARIATE
N-VARIATE
UNIVARIATE
N = NUMBER OF MODELS
MCP: MULTI-MODEL APPROACH

## Slide 6
Following Krzysztofowicz (2008), the procedure can be generalized including all the available forecasts within the entire time horizon.
A MULTI-VARIATE Predictive Distribution is so obtained, which accounts for the joint PU of the observed variable at each time step.
The basic and multi-model approaches, as most of the existing processors, juast answer to the question:
Which is the probability that the water level will be higher than the dykes one at the hour 24th?
Krzysztofowicz, R.: Probabilistic flood forecast: exact and approximate predictive distributions, Research Paper RK0802, University of Virginia, September 2008.
MCP: MULTI-TEMPORAL APPROACH

## Slide 7
Observ. at 12 hours
Observ. at 24 hours
T - VARIATE
(N+1) ∙ T - VARIATE
N ∙ T - VARIATE
N = NUMBER OF MODELS
T = NUMER OF TIME STEPS
MCP: MULTI-TEMPORAL APPROACH
With respect to the multi-model approach, the dimension of all the distributions involved in the Bayesian formulation is multiplied by the number of time steps.

## Slide 8
Within 12 h
Probability to exceed a water level a within the time horizon of T time steps
12 h
24 h
MCP: MULTI-TEMPORAL APPROACH
12 h
24 h
Within 24 h
Chart: P(yi>s) i=1,T
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
P(y>a) within t time steps | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.01 | 0.02 | 0.03 | 0.07 | 0.11 | 0.15 | 0.217 | 0.283 | 0.35 | 0.443 | 0.537 | 0.63 | 0.67 | 0.71 | 0.75 | 0.787 | 0.823 | 0.86
Cumulative Exceeding Probability

## Slide 9
MCP: MULTI-TEMPORAL APPROACH
Exact Exceeding time (T*) probability
Chart: P(T*)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Pdf of flood peak timing | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.004 | 0.008 | 0.012 | 0.023667 | 0.035333 | 0.047 | 0.057333 | 0.067667 | 0.078 | 0.088333 | 0.098667 | 0.109 | 0.088333 | 0.067667 | 0.047 | 0.045667 | 0.044333 | 0.043
12 h
24 h

## Slide 10
12 h
24 h
MCP: MULTI-TEMPORAL APPROACH
Which is the probability that the water level will be higher than the dykes one at the hour 24th?
RED + GREY
Which is the probability that the river dykes will be exceeded within the next 24 hours?
Which is the probability that the river dykes will be exceeded exactly at the hour 24th?
RED + GREY + YELLOW
RED
Can be obtained also with the basic and multi-model approaches since it does not depend on the state of the variable at 12 hours

## Slide 11
Forecasted hourly levels: forecast lead time 24 h.
Observed hourly levels
01/05/2000
20/01/2009
30/06/2004
MCP: CALIBRATION VALIDATION
PO RIVER AT PONTELAGOSCURO and PONTE SPESSA
Available data, provided by the Civil Protection of Emilia Romagna Region, Italy:
APPLICATION: MCP with MULTI-TEMPORAL

## Slide 12
Exceeding Time Probability
Cumulative Exceeding Probability
90% Uncertainty Band
Pontelagoscuro Station (24 h)
PROBABILITY FORECASTS WITHIN A TIME HORIZON
P(T*)
Deterministic Forecast

## Slide 13
Exceeding Time Probability
Cumulative Exceeding Probability
90% Uncertainty Band
Ponte Spessa Station (24 h)
PROBABILITY FORECASTS WITHIN A TIME HORIZON
P(T*)
Deterministic Forecast
P(T*)

## Slide 14
Ponte Spessa Station (24 h)
VALIDATION
CALIBRATION
VERIFICATION: If the probability value provided by the processor is correct, considering all the cases when the exceeding probability takes value P, the percentage of observed exceeding occurrences must be equal to P.
Red Line = Perfect beahviour
Computed with a 5% discretization
PROBABILITY FORECASTS WITHIN A TIME HORIZON

## Slide 15
Most of the existing Uncertainty Processors do not account for the evolution in time of the forecasted events.
The presented multi-temporal approach allows to identify the joint predictive distribution of all the forecasted time steps, recognizing and reducing the time errors.
Important information are added to the Predictive Uncertainty, such as the probability to have a flooding event within a specific time horizon and the exact flooding time probability.
The comparison of predicted and observed flooding occurrences verified that, a part small errors due to the unavoidable approximations, the methodology computes the flooding probability with good accuracy.
CONCLUSIONS

## Slide 16
THANK YOU FOR YOUR ATTENTION AND YOUR PATIENCE

## Slide 17
Ponte Spessa Station (18 h)
The information about the time allows systematic
time errors to be identified and corrected
PROBABILITY FORECASTS WITHIN A TIME HORIZON