## Slide 1: EGU 2012, Vienna Session NH1.1/AS1.16
Marc Velasco, CETaqua
Application of a rule-based system for flash flood forecasting taking into account climate change scenarios in the Llobregat basin

## Slide 2: Table of contents
Introduction
IMPRINTS project
Llobregat basin
Data used
Rule based system
Results and discussion
Conclusions

## Slide 3: Introduction
Generate future discharge series in two sub-basins of the Llobregat river, to assess the changes in terms of occurrence and intensity of flash floods
  An operational rule-based system
  Observations and hydrological data to calibrate it
  A downscaling of future climate scenarios as input data of the system
  A probabilistic assessment of the exceedances to study the future discharge series

## Slide 4: IMPRINTS project
IMPRINTS project
  IMproving Preparedness and RIsk maNagemenT for flash floods and debriS flow events
  EC 7th Framework Programme project
  19 partners
  42 months (it finishes next september)
  Objectives
    Improve preparedness and the operational risk management of FF & DF
    Produce methods and tools to be used by practitioners of the emergency agencies and utility companies
    Produce a prototype of the operational platform designed to be used around the EU

## Slide 5: IMPRINTS project

## Slide 6: Llobregat basin
Located in the NE of Spain
Area of the basin: 4958 km2
River length: 156,6 km
Maximum elevation: 1259 m
Mean discharge of ≈ 20 m3/s
Mediterranean climate
  Annual rainfall of ≈ 700 mm
  Rainfall events of 200 mm in 24 h
  Floods occur generally in autumn

## Slide 7: Data used
Precipitation
  Observations from local rain gauges
Discharge
  HBV hydrological model outputs using the precipitation series as an input
Precipitation
  SMC downscaling data corrected using ARCON historical database
    Scenarios A2 and B1
Control period (1980 – 2008)
Future scenarios (2011 – 2100)
Used for the calibration and validation of the RBS
Used as input of the RBS

## Slide 8: Rule based system
Forecasting system that allows to link real-time observed values with expected hazard in probabilistic terms
  Simplification of a hydrological model with shorter lead times
  Operational use: issue warnings
  Considering high percentiles to represent extreme events
Governing variables for FF
  Antecedent soil moisture
  Forecasted rainfall

## Slide 9: Rule based system
Calibration period
  1980 – 1999
Validation period
  2000 - 2008
Sub basin | a | b | c | R2
Alt Llobregat | 0.377 | 0.256 | 0.425 | 0.833
Anoia | 0.128 | 0.220 | 0.095 | 0.881
Calibration (blue) and verification (red) periods for the Alt Llobregat sub-basin, considering a 15 days backstep, 0.8 quantile and 20 years of calibration. In black, the HBV discharge values.

## Slide 10: Results and discussion
Methodology
  Running the RBS with future precipitation series
  Assessment of the discharge series, following a Peak Over Threshold approach
    Extremes occurrence
      Number of exceedances
    Extremes intensity
      Fitting a Generalized Pareto distribution to the exceedances, and plotting the discharge – return period relationships
  To compare the control and future exceedances, a fixed threshold is established
Sub-basin | Threshold (m3/s)
Alt Llobregat | 26.5
Anoia | 11.5

## Slide 11: Results and discussion
Alt Llobregat basin
  Occurrence
    High generalized increase
  Intensity
    A high extreme in the control makes it difficult to draw conclusions
Period | # POT per year (for each sub-period) |  |  | 
Control (1980-2009) | 0.86 | 2011-2040 | 2041-2070 | 2071-2100
Scenario A2 (2011-2100) |  | 1.23 | 1.63 | 1.07
Scenario B1 (2011-2100) |  | 0.53 | 1.20 | 1.10
GP distribution fitted to the POT discharge values of the Alt Llobregat sub-basin for the control (1980-2009) and future periods for the A2 (left) and B1 (right) scenarios.
Time series of the discharge values in the Alt Llobregat sub-basin.

## Slide 12: Results and discussion
Anoia basin
  Ocurrence
    Moderate increase
    Two exceptions
  Intensity
    Generalized increase
    Even for the exceptions
Period | # POT per year (for each sub-period) |  |  | 
Control (1980-2009) | 0.86 | 2011-2040 | 2041-2070 | 2071-2100
Scenario A2 (2011-2100) |  | 0.93 | 0.93 | 0.53
Scenario B1 (2011-2100) |  | 0.80 | 1.07 | 0.87
GP distribution fitted to the POT discharge values of the Anoia sub-basin for the control (1980-2009) and future periods for the A2 (left) and B1 (right) scenarios.
Time series of the discharge values in the Anoia sub-basin.

## Slide 13: Results and discussion
Comparing the results of the two sub-basins
  An increase in both occurrence and intensity of flash floods occurs
  The trends are slightly different in each sub-basin
    Alt Llobregat
      high increase in occurrence, no clear results in intensity
    Anoia
      Moderate increase in occurrence, high increase in intensity
  It is not possible to obtain a general trend for the whole Llobregat basin, in terms of spatial variability
    FF are very local hazards, and hence should be studied locally

## Slide 14: Conclusions
A RBS has been used to assess future scenarios
  Although its main use is operational, it allows to easily assess the future behaviour of flash floods
An increase in both occurrence and intensity of FF is obtained for the two sub-basins
  Discharge values strongly depend on the future precipitation scenarios
    Uncertainties associated to climate science are transferred to this study
Results should be used with care. Still, management strategies should take the wide range of plausible scenarios into account

## Slide 15: Questions?
Thank you very much for your attention!

## Slide 16: IMPRINTS project
Floods are the major natural hazard in Europe
Mountainous areas and Mediterranean regions have the following aggravating factors:
  Steep slopes
  High spatial and temporal variability
  Heavy rain intensities
  Highly torrential phenomena
Mediterranean and Alpine basins are the test-bed basins of the IMPRINTS project

## Slide 17
WP10 Project Management (UPC-CRAHI)
Activity 5: Dissemination and management
WP9 Dissemination of project results (UPC-CRAHI)
Activity 3:
Practitioners’ tools
WP6
Specifications for practitioners’ tools
(SCHAPI)
Activity 1: Probabilistic early warning systems
WP1
Improving
short-term rainfall forecasting
(MeteoSwiss)
WP2
Developing probabilistic FF & DF early warning systems
(JRC)
WP8 Testing the practitioners’ tools
(UPC-CRAHI)
Activity 4: Verification on the test-beds
Activity 2:
Advanced probabilistic forecasting systems
WP3
Integrated probabilistic FF & DF forecasting system
(ULanc)
WP4
Rule-based probabilistic FF & DF forecasting system
(UPC-GITS)
WP5
Assessing impact of future changes
(CETAQUA)
WP7
Developing practitioners’ tools
(HYDS)

## Slide 18: Antecedent soil moisture
PL360
  Weightning function

## Slide 19: SMC downscaling
Bias correction with ARCON database

## Slide 20: Data used
Control period (1980 – 2008)
  Precipitation
    Observations from local rain gauges
  Discharge
    HBV hydrological model outputs using the precipitation series as an input
Future scenarios (2010 – 2100)
  Precipitation
    SMC downscaling data corrected using ARCON historical database
Used for the calibration and validation of the RBS
Used as input of the RBS