## Slide 1
Collaborative Catchment-Scale Water Quality Management using Integrated Wireless Sensor Networks
Huma Zia, Nick R. Harris, Geoff V. Merrett
hz2g11@ecs.soton.ac.uk, School of Electronics & Computer Science, University of Southampton, UK
Summary
Water Quality Monitoring, Control and Management Framework (WQMCM)
Simulation Results
Conclusions and Future Work
Fig.1 – Collaborative catchment-scale management using integrated WSNs
The challenge of improving water quality is a growing global concern. Nutrient losses from land to water have accelerated due to agricultural and urban pursuits [1]. In many cases, the application of fertilizer can be reduced by 30-50% without any loss of yield [2]. Thus information about nutrient levels and trends in and around the farm can improve agricultural practices and thereby reduce water contamination. The use of sensor networks for monitoring water quality in a catchment is in its infancy[3]. These applications are focused on local requirements and are mostly limited to water bodies. They have yet to explore the use of this technology for catchment-scale monitoring and management decisions, in an autonomous and dynamic manner. For effective and integrated water quality management, we propose a framework that utilizes local monitoring networks across a catchment, with provision for collaborative information sharing. Results indicate that the proposed mechanism of information sharing can lead to significant reductions in nutrient losses (up to 50%) and better reutilization of nutrients amongst farms, which would have a positive impact on catchment scale water quality and fertilizer costs.
The objective of the WQMCM framework is to integrate sensor observation data with weather forecasts, runoff/drainage and nutrient loss models (Fig.2). This is intended to integrate the variety of data streams and modeling tasks into a decision making system for day-to-day water and nutrient management in agriculture.
LEARNING AND LINKING EVENTS: A machine learning algorithm enables individual network (on a farm or in a water body) to correlate catchment events to events within their zone of influence. Based on that, a network is then able to predict discharge rates for nutrients and runoff.
DECISION MODEL: Based on the predicted influx duration and rates, sampling rates of the sensors can be adapted to give accurate measurements. This enables longer battery life of the sensors. Finally, the information about possible water and nutrient discharges is fed into a decision making system to appropriately manage water and nutrient usage in farms.
Fig. 3 illustrates the event captured using various sampling rates. The rate can be adapted using the predicted flow rate calculated from the shared information from neighbour networks. This is important because long sampling intervals tend to miss peak discharge values and reduces the precision of sensed discharge rate (Fig.4), but constant high-speed sampling depletes the sensor board’s battery in just 4 days. Thus adaptive sampling has the capacity to accurately capture events and still maintain long sensor lifetime. Figure 5 illustrates the results of a case study based on a rice crop, (which is a wetland crop and requires 200-300Kg/ha fertilizer), which is prone to nutrient losses (NL) through runoff. Based on the WQMCM framework, the runoff information is shared among farms with the result that fertilizer usage can be reduced by 30-50%.
Results indicate that the proposed mechanism for information sharing enables a network to learn its environment and correlate catchment events to events within its zone of influence. This can inform better decision making and therefore improve agricultural practices. Furthermore, results indicate that the proposed framework can lead to significant reduction in nutrient losses (up to 50%) and better reutilization of nutrients amongst farms, which would have a positive impact on catchment scale water quality and fertilizer costs. Future work involves extending simulations to represent improvements in water quality based on the WQMCM framework by various stakeholders in the catchment over a long period of time. Events would be introduced in the catchment to simulate resource and performance optimization of the deployed networks.
The authors would like to acknowledge the kind support extended by our Australian collaborators at the University of Western Australia, Mark Rivers and Prof. Neil Coles, together with the support of the World University Network.
[1] Rivers, M., K. Smettem, and P. Davies. Estimating future scenarios for farm-watershed nutrient fluxes using dynamic simulation modeling–Can on-farm BMPs really do the job at the watershed scale? in Proc.29th Int. Conf. System Dynamics Society, 2011. 2010. Washington
[2] Liu, C., et al., On-farm evaluation of winter wheat yield response to residual soil nitrate-N in North China Plain. Agronomy Journal, 2008. 100(6): p. 1527-1534.
[3] Kotamäki, N., et al., Wireless in-situ sensor network for agriculture and water monitoring on a river basin scale in Southern Finland: Evaluation from a data user’s perspective. Sensors, 2009. 9(4): p. 2862-2883.
Based on the framework of WQMCM, this system of networks is modeled which shares information about critical events, such as rain or flooding (Fig.1). Sharing information on critical parameters among networks of water bodies and farms can enable identification and quantification of the contaminant sources, enabling better decision making for agricultural practices and thereby reducing contaminants fluxes.
Chart: Fertilizer usage (kg N/ha)
| June | July | August | Sept | Oct | Nov
NL with conventional fertilizer i/p | 15 | 30 | 45
NL with modified fertilizer i/p | 15 | 5 | 0
conventional fertilizer i/p | 50 | 100 | 150
modified fertilizer i/p | 50 | 70 | 100
Fig. 3 – Runoff discharge measured using various sampling rates
Fig. 5 – Fertilizer usage with and without nutrient reuse in the runoff water
Fig. 2 – Model based on WQMCM Framework
Chart: Time (hr)
every 30 mins | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.067415 | 0.84504 | 3.2122 | 6.6799 | 11.1532 | 17.5476 | 26.0196 | 36.1879 | 48.9461 | 70.2521 | 116.3882 | 358.9795 | 1082.5447 | 1213.2846 | 795.3869 | 498.4835 | 333.1318 | 234.6506 | 178.5717 | 145.8963 | 125.0404 | 112.7816 | 103.9761 | 96.5564 | 89.2609 | 81.623 | 76.9081 | 74.4724 | 69.6898 | 62.7885 | 58.7921 | 57.0718 | 56.0858 | 55.7609 | 55.9701 | 55.3677 | 46.7344 | 27.6587 | 12.554 | 5.4506 | 2.4051 | 1.0181 | 0.42208 | 0.14692 | 0.024981 | 0
every 1 hour | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.84504 | 6.6799 | 17.5476 | 36.1879 | 70.2521 | 358.9795 | 1213.2846 | 498.4835 | 234.6506 | 145.8963 | 112.7816 | 96.5564 | 81.623 | 74.4724 | 62.7885 | 57.0718 | 55.7609 | 55.3677 | 27.6587 | 5.4506 | 1.0181 | 0.14692 | 0
every 2 hours | 0 | 0 | 0 | 0 | 6.6799 | 36.1879 | 358.9795 | 498.4835 | 145.8963 | 96.5564 | 74.4724 | 57.0718 | 55.3677 | 5.4506 | 0.14692
every 6 hours | 0 | 0 | 358.9795 | 96.5564 | 55.3677
Fig. 4 – variation in sensed peak discharge values and sensor board lifetime with sampling rate
Chart: Sampling Rate (hr)
| 1.6666666666666666E-2 | 0.5 | 1 | 2 | 6
peak discharge precision | 100 | 95.3154 | 95.3154 | 39.1608 | 28.2014
sensor board lifetime | 4.8 | 144 | 288 | 576 | 2304
Integrated Modeling with WQMCM Framework