## Slide 1: Air-quality in the mid-21st century for the city of Paris. From the regional to the local scale.
Konstantinos Markakisa
Myrto Valaria
Augustin Coletteb
Olivier Sanchezc
Olivier Perrusselc
EGU General assembly 2013
Session: Climate: Past, Present, Future
8 April
aLMD (Laboratoire de Meteorologie Dynamique), IPSL
Ecole Polytechnique, 91128 Palaiseau Cedex
bInstitut national de l’environnement industriel et des risques (INERIS), Paris, France.
cAIRPARIF, Surveillance de la qualité de l’air en Île-de-France, Paris, France
7-12 April 2013
Vienna, Austria
Notes: -Thank hospitality
-introduce yourself
-name of talk, why this title
-word “parametarisation”=boring

## Slide 2
Meleux et al., 2007 AE
Hedegaard et al., 2008 ACP
Katragkou et al., 2011 JGR
Manders et sl., 2012 ACP
Langner et al., 2012a ACP
Langner et al., 2012b ACP
Wild et al., 2012 ACP
ACHIA
Background in AQ-climate research in Europe
Climate effects on AQ
Climate – GHG’s changes
Ozone increases
Climate + emissions projections (reductions)
RCP’s: Compensation
Developed for GCMs (range of radiative forcings)
Not developed for AQ studies
GEA: Climate + AQ co-benefits
Europe - Ozone decreases
Hotspots – Ozone increases
2030
2050
Europe - Ozone decreases
Colette 2012 ACP
Colette 2013 ACPD
LOCAL SCALE
Health impacts are a major concern
The only available information originates from global/regional applications employing global/regional inventories
Exploring AQ in the city of Paris performing a 10yr run for the mid-21st century employing a bottom-up inventory and a CTM in 4km resolution
Bridging the gap (ACHIA project)
Notes: -Why this dates (to know where we are in time)
-Why start from 1991. nothing before (small pieces that where far from creating a solid parametarisation)
-all these from specific tree species

## Slide 3
ACHIA
Modelling framework
GCM: IPSL-CM5A-MR (2.5ºx1.25º)
GCTM: LMDz-INCA (3.75ºx2.5º) (Szopa et al., 2012)
Forcing: RCPs: 2.6-MIT and 8.5-REF (Riahi et al., 2011)
Offline coupling
RCM: WRF (0.5o) (Menut et al., 2012; Vautard et al., 2012)
CTM: CHIMERE in 0.5o (~50km) with 8 VL (Colette et al., 2012a)
GEA emissions: MIT, REF (Colette et al., 2012b)
Offline coupling
RCM: WRF (0.1o)
CTM: CHIMERE in 4km with 12 VL
Continuous 10 year simulation (1995-2004 and 2045-2054)
Airparif inventory: 2 consistent scenarios
MIT (more optimistic, AQ legislation + climate policy).
REF (less optimistic, AQ legislation, no climate policy).
1km resolution, explicit quantification of more than 50 anthropogenic activities in the region, 600 point sources
Notes: -Why this dates (to know where we are in time)
-Why start from 1991. nothing before (small pieces that where far from creating a solid parametarisation)
-all these from specific tree species

## Slide 4
Laboratoire de Meteorologie Dynamique
ACHIA
Rationale
1) Using the Regional and the Local scale applications we intent to investigate the differences that arise in mid-21st century AQ projections when implementing bottom-up emissions and a higher resolution.
quality of the emission inventory
limitations of the projection approach
modelling effects (e.g. resolution)
2) How will air-quality look like at 2050 in Paris?
Notes: -Why this dates (to know where we are in time)
-Why start from 1991. nothing before (small pieces that where far from creating a solid parametarisation)
-all these from specific tree species

## Slide 5
ACHIA
Emission inventory: Regional vs. local
Emissions inventories developed in global/regional scale can be erroneous when describing emission hotspots (Butler et al., 2008 AE and 2012 ACP; Colette et al., 2012a ACP)
Notes: -Why this dates (to know where we are in time)
-Why start from 1991. nothing before (small pieces that where far from creating a solid parametarisation)
-all these from specific tree species

## Slide 6
Laboratoire de Meteorologie Dynamique
ACHIA
Emission inventory: Projections
1st element Short term: Local experts REF for 2020
2nd element
Long term: coefficients extracted from the MIT / REF GEA national totals for France
Future Emissions for Paris:
2 pathways
Emission projections developed for global/regional applications maybe also unrepresentative for a city
We use a hybrid methodology to project the local scale emissions to 2050
Notes: -Why this dates (to know where we are in time)
-Why start from 1991. nothing before (small pieces that where far from creating a solid parametarisation)
-all these from specific tree species

## Slide 7
Chart: Annual emissions of one 50km GEA cell covering Paris
| NOx | NMVOC | PM2.5
Present | 56.8061 | 122.9483 | 7.5253
2050_REF | 2.5178 | 15.0406 | 0.2999
2050_MIT | 1.1493 | 0.667 | 0.0503
Laboratoire de Meteorologie Dynamique
ACHIA
Emission inventory – projections
Chart: Annual emissions of one 50km GEA cell covering Paris
| NOX | NMVOCs | PM2.5
Present | 32.8673 | 66.6926 | 6.4577
2050_REF | 18.7148 | 31.8606 | 1.8183
2050_MIT | 8.2305 | 24.6958 | 0.95532
Climate policy benefit
Climate policy benefit
We use the national totals because GEA uses a spatial algorithm to distribute future emissions for which emissions in urban centers are reduced more rapidly than in rural areas.
This produces a very clean Paris
Notes: -Why this dates (to know where we are in time)
-Why start from 1991. nothing before (small pieces that where far from creating a solid parametarisation)
-all these from specific tree species

## Slide 8
Evaluation O3 – daytime (April - August)
Lower NOx
NOx dilution
ACHIA
-18.2% bias in ozone during episodes
Episodically produced ozone is more sensitive to meteorology
Notes: -Why this dates (to know where we are in time)
-Why start from 1991. nothing before (small pieces that where far from creating a solid parametarisation)
-all these from specific tree species

## Slide 9
Laboratoire de Meteorologie Dynamique
ACHIA
Evaluation PM2.5
Notes: -Why this dates (to know where we are in time)
-Why start from 1991. nothing before (small pieces that where far from creating a solid parametarisation)
-all these from specific tree species

## Slide 10
Laboratoire de Meteorologie Dynamique
ACHIA
Rationale
How will air-quality look like at 2050 in Paris?
Notes: -Why this dates (to know where we are in time)
-Why start from 1991. nothing before (small pieces that where far from creating a solid parametarisation)
-all these from specific tree species

## Slide 11
50km: -4.5 ppb
Laboratoire de Meteorologie Dynamique
ACHIA
Mid-21st century in Paris – O3 “reference” scenario
In the 4km simulation Paris stays strongly VOC-limited.
REF scenario of GEA shows very large reductions of NOx but also for VOCs. It uses the spatial algorithm leading to large reductions in the cities
SOMO35 increases by 70% in the city
T2: +0.9 K
isop: +16%
4km:+7 ppb
4km:-3 ppb
50km: -5.6 ppb
Ozone increases
2020: Roustan et al., 2011 AE
2030: Colette et al., 2012 ACP
Notes: -Why this dates (to know where we are in time)
-Why start from 1991. nothing before (small pieces that where far from creating a solid parametarisation)
-all these from specific tree species

## Slide 12
Tarasson et al., 2003
Beekmann and Vautard, 2010
Laboratoire de Meteorologie Dynamique
ACHIA
Mid-21st century in Paris – O3 “mitigation” scenario
4km shifts to more NOx limited environment but apparently too late.
MIT scenario of GEA shows very large reductions of NOx but also for VOCs. It uses the spatial algorithm leading to large reductions in the cities
SOMO35 decreases by 83%.
T2: -0.6 K
isop: -24.5%
4km: -2.9 ppb
4km:-14.3 ppb
50km: -16 ppb
50km: -10.7 ppb
More NOx sensitive
Notes: -Why this dates (to know where we are in time)
-Why start from 1991. nothing before (small pieces that where far from creating a solid parametarisation)
-all these from specific tree species

## Slide 13
Laboratoire de Meteorologie Dynamique
ACHIA
Mid-21st century in Paris – PM2.5
Notes: -Why this dates (to know where we are in time)
-Why start from 1991. nothing before (small pieces that where far from creating a solid parametarisation)
-all these from specific tree species

## Slide 14: Thank you for your attention!
Laboratotie de Meteorologie Dynamique
ACHIA