## Slide 1
A new method of quantifying discharge of small rivers into lakes and inland seas
Shirshov Oceanology Institute Moscow, Russia
A. Osadchiev, P. Zavialov

## Slide 2: Motivation
1. Importance of river discharge estimates:
Continental discharge is an important component of the global hydrological cycle (about 10% of the input part of the water budget of the ocean);
Buoyant inflow usually causes surface density stratification at the large shelf areas, and plays a significant role in physical, chemical, and biological processes there;
For the inland seas and certain shelf areas, fluvial discharges can play much more significant role.
2. Complexity of river discharge estimation:
Direct measurements of discharge are expensive and laborious;
Indirect methods of river discharge estimation require ancillary ground-based information (e.g., gauge measurements, bathymetry, etc.) and are prone to uncertainties ;
There is a lack of discharge data for most of rivers in a global scale

## Slide 3
Schematic of a plume interaction with ambient environment
River plumes can be
recognized and identified
using satellite imagery
River Discharge = River Plume + Dissipation

## Slide 4
Application of the method for the Mzymta River

## Slide 5
Principal scheme of estimating river discharge
The initial satellite image. Suspended sediment concentration is used as a plume tracer.

## Slide 6
The initial satellite image. Suspended sediment concentration is used as a plume tracer.
Identification of border and spatial structure of the plume.
Principal scheme of estimating river discharge

## Slide 7
The initial satellite image. Suspended sediment concentration is used as a plume tracer.
Identification of border and spatial structure of the plume.
Prescribing river discharge and external forcing model
configuration
Q
τ
Principal scheme of estimating river discharge

## Slide 8
The initial satellite image. Suspended sediment concentration is used as a plume tracer.
Identification of border and spatial structure of the plume.
Prescribing river discharge and external forcing model
configuration
Modeling river plume under
prescribed conditions
Q
τ
Principal scheme of estimating river discharge

## Slide 9
Schematic of the forces applied to
an individual particle of the plume
interpolation
vertical
friction
wind stress
pressure gradient
force
Coriolis force
lateral friction
salinity diffusion
particle velocity
particle acceleration
modeled particle distribution
interpolated
river plume
STRiPE ‒ Lagrangian model of a river plume
Transport equation for a particle
vertical
friction
lateral friction
wind
stress
Coriolis force
pressure gradient force
More details at: A. Osadchiev and P. Zavialov. Lagrangian model of a surface-advected
river plume. Continental Shelf Research. 58: 96-106. 2013.

## Slide 10
Details
High variability of river plume is caused by variability of external forcing conditions, mainly, wind stress and discharge => we need to perform big number of model runs to simulate river plume under external forcing conditions with high resolution to determine the exact discharge;
The main advantage of STRiPE comparing to widely used Eulerian models (e.g., POM, ROMS, etc.) is its low computational cost, which enabled us to perform about 2000 simulations of the Mzymta River plume under various forcing and discharge conditions. The simulation results were organized as a data base, so the most similar river plume among the modeled results could be quickly found for every satellite image of the plume.
…
…
…
…
…
…
Data base of river plumes
simulated under various conditions

## Slide 11
Principal scheme of estimating river discharge
The initial satellite image. Suspended sediment concentration is used as a plume tracer.
Identification of border and spatial structure of the plume.
Prescribing river discharge and external forcing model
configuration
Modeling river plume under
prescribed conditions
5. Comparing the modeled and the
observed plumes.
Q
τ

## Slide 12
Details
In most cases there is no complete coincidence of the satellite plume image and best-fitting model result. Therefore similarity between satellite and modeled plumes is evaluated in two ways, comparison of their areas and comparison of their contours (e.g., normalized contour-vectors).
plume area =
N km2

## Slide 13
Principal scheme of estimating river discharge
Q
τ
river discharge = Q m3/s

## Slide 14
Validation for the Mzymta River

## Slide 15
Summary and conclusions
A method of estimating river discharge using satellite imagery and numerical modeling is developed. This method is an alternative for the expensive and laborious direct measurements of the river discharge.
This method was applied to the Mzymta River plume and was used to estimate the discharge rate of Mzymta River during the trial period (June-December, 2011). The method was verified against the in situ gauge measurements and showed good ability to produce realistic results.
Future work
The future improvement of the quality of satellite imagery on the one hand, and increasing of the computer performance on the other hand will result in growth of efficiency and accuracy of this method.
We are looking forward for applying the method to the whole Black Sea shore to estimate total river discharge to the Black Sea and evaluate the role of numerous small rivers and watersheds in the total discharge.
We plan to use several river plume tracers (e.g., temperature, chlorophyll, dissolved organic) for estimating borders of river plumes with low sediment concentration.

## Slide 16
Thank you for your attention!