## Slide 1: Comparison of ground-based FTIR measurements and EMAC model simulations of trace-gases columns near St. Petersburg (Russia) in 2009-2012
Yana Virolainen (1), Maria Makarova (1), Dmitry Ionov (1), Alexander Polyakov (1), Oliver Kirner (2), Yury Timofeyev (1), Anatoly Poberovsky (1), and Hamud Imhasin (1)
St.Petersburg State University, St. Petersburg, Russian Federation, (2) Steinbuch Centre for Computing, Karlsruhe Institute of Technology, Karlsruhe, Germany
Instrumentation | solar FTIR-spectrometer Bruker 125HR
Spectral resolution | ~0.005 cm-1
Location | Peterhof - St. Petersburg (59.88 N, 29.82 E)
Time series | 2009-2012
Gases | Spectral windows, сm-1 | Random error of measurement | Influenced gases
H2O | 1110.00-1113.00 1117.30-1117.90 1120.10-1122.00 1196.00-1200.40 1220.50-1221.50 1251.75-1253.00 | 0.9-1.3% | N2O, CO2, CH4, O3
O3 | 991.25-993.80 1001.47-1003.04 1005.00-1006.90 1007.35-1009.00 1011.15-1013.55 | 1-2% | H2O, CO2 , C2H4
ClONO2 | 779.0-779.8 780.0-780.3 780.3-781.3 | 15-20% | H2O, CO2, O3, HNO3, C2H2
HNO3 | 867.00-869.60 872.80-875.20 | 1-2% | H2O, CO2, NO2
HCl | 2925.75-2926.00 2727.73-2727.83 2775.70-2775.80 2925.80-2926.00 | 2-5% | CH4, H2O
CH4 | 2613.7-2615.4 2921.0–2921.6 2835.5-2835.8 | 0.3-0.5% | H2O, HDO, CO2, NO2
CO | 2057.7-2058.0 2069.56-2069.76 2157.5-2159.15 | 1.1-1.4% | O3,CO2,OCS,N2O,H2O
NO2 | 2914.590-2914.707 | 8-12% | CH4, HDO
The EMAC model is a numerical chemistry and climate simulation system that includes sub-models describing troposphere and middle atmosphere processes and their interaction with oceans, land and human influences. The simulation includes a comprehensive atmospheric chemistry setup for the troposphere, the stratosphere and the lower mesosphere. We applied the EMAC (ECHAM5 version 5.3.01, MESSy version 1.10) in the T42L39MAresolution, i.e. with a spherical truncation of T42 (corresponding to a quadratic Gaussian grid of approximately 2.8 by 2.8 degrees in latitude and longitude) with 39 vertical hybrid pressure levels up to 0.01 hPa.
Gas (number of days) | Method | Mean ± variability, cm-2 | Bias ± SD, % | Correlation coefficient
H2O (191) | FTIR | (4.49±2.99) × 1022 | -3.1 ± 21.5 | 0.95±0.01
 | EMAC | (4.62±2.79) × 1022 |  | 
O3 (189) | FTIR | (9.25±1.24) × 1018 | -12.5 ± 8.2 | 0.91±0.01
 | EMAC | (10.4±1.7) × 1018 |  | 
ClONO2 (89) | FTIR | (1.12±0.50) × 1015 | -0.7 ± 32.5 | 0.70±0.06
 | EMAC | (1.13±0.41) × 1015 |  | 
HNO3 (89) | FTIR | (2.39±0.51) × 1016 | +33.2 ± 16.8 | 0.65±0.06
 | EMAC | (1.60±0.44) × 1016 |  | 
HCl (309) | FTIR | (4.36±0.60) × 1015 | +22 ± 8.1 | 0.81±0.02
 | EMAC | (3.40±0.44) × 1015 |  | 
CH4 (232) | FTIR | (3.83±0.06) × 1019 | +1.4 ± 1.0 | 0.82±0.02
 | EMAC | (3.77±0.04) × 1019 |  | 
CO (452) | FTIR | (2.12±0.33) ×1018 | +14.0 ± 5.7 | 0.93±0.01
 | EMAC | (1.82±0.31)×1018 |  | 
NO2 (233) | FTIR | (3.32±1.10) × 1015 | +14.1 ± 13.2 | 0.92±0.01
 | EMAC | (2.85±1.05) × 1015 |  | 

## Slide 2: Comparison of ground-based FTIR measurements and EMAC model simulations of trace-gases columns near St. Petersburg (Russia) in 2009-2012
Seasonal cycle

## Slide 3: Comparison of ground-based FTIR measurements and EMAC model simulations of trace-gases columns near St. Petersburg (Russia) in 2009-2012
Distribution of gases total columns