## Slide 1: Development of High Precision Tsunami Runup Calculation Method Coupled with Structure Analysis
Taro Arikawa (1&2), Katsumi Seki (1),
Yu Chida (2), Tomohiro Takagawa (2), and Kenichiro Shimosako (2)
Chuo University
Port and Airport Research Institute
European Geosciences Union
General Assembly 2017
Vienna | Austria | 23–28 April 2017

## Slide 2: Direction of Research
In order to evaluate the damage due to giant tsunamis, influence of destruction of structures, debris, etc. is required.
The power of the tsunami is greatly different depending on the place and the condition
3 dimensional numerical simulator should be required to analyze overflow, scour, flood into buildings and so on.
The system which connects tsunami propagation simulator and 3-D numerical simulator should be developed.

## Slide 3: Multiscale and Multiphysics Tsunami Simulator
波源域
Inundation
Epicenter
Tsunami Propagation
Structure destruction
STOC-ML
STOC-IC
CADMAS
CADMAS-2F
STR
Nonlinear Long wave equations
Three dimensional NS equations
with continuity surface model
Structure and geo analysis by FEM or DEM
Three dimensional NS equations
with VOF model
Three dimensional two phase NS equations
with VOF model
STOC-ML
STOC-IC
STR
CADMAS

## Slide 4: Multiscale analysis
Coupled with wave propagation simulation

## Slide 5: The STOC-CADMAS system
STOC-ML
Tsunami source
STOC-IC
3D model Calculates the free water surface with a vertically integrated continuity equation
Computation load: moderate
Quasi-3D model (multi-level model)
Assumes hydrostatic pressures at each level
Computation load: light
CADMAS-SURF/3D
3D model Estimates the free water surface with the VOF method
Computation load: heavy
Coupled with DEM/FEM
STOC system (Tomita et. al., 2005)
CADMAS system (Arikawa et. al., 2005)
(Arikawa and Tomita, 2016)

## Slide 6: STOC(Storm surge and Tsunami simulator in Oceans and Coastal areas)
STOC-IC
3-d variable density RANS model with Eddy Viscosity closure and Integrated Continuity eq. for free-surface tracking
STOC-ML
3-d Multi-Level constant density RANS model with Eddy Viscosity and hydro-static pressure
gv : porosity
gx gy gz : transmissivity in each direction of “x”, “y” and “z”
p=ρg（η- z）
Equation of Free Water Surface
Equation of Motions
(Tomita et. al.,2005)
Equation of Continuity
Integrate in the z direction

## Slide 7: CADMAS-SURF (SUper Roller Flume for Computer Aided Design of MAritime Structure)
(For 3D version, Arikawa et. al.,2005)
This numerical code is based on the VOF method, and is applicable to not only wave transformation but also interaction of wave, current, structure and foundation. Namely, this numerical flume is replaceable with the laboratory flume, and applicable to the practical works of maritime structure design against wave action.
Equation of Motions
Equation of Continuity
Equation of Free Water Surface (VOF Method)
Volume of Fluid
implies the ratio of fluid volume to cell volume

## Slide 8: Connections between simulator calculations
STOC-ML
STOC-ML
STOC-IC
CADMAS-SURF/3D-MG
STOC-ML
STOC-IC
CADMAS-SURF
/3D-MG
Communication by MPI
Communication by MPI
Must not touch
All connections are made using MPI communications.
Although all three models are capable of segmenting their respective areas of interest, when different calculation methods are used in the same area (for example, STOC-IC calculations are used in an STOC-ML area), the parent area containing the different calculation methods is regulated to prevent segmentation.
Consequently, when a CS3D area is made sufficiently large, the STOC-IC area that contains it ultimately becomes larger as well, as a single area.

## Slide 9: Verification of Accuracy of the system
Domain for CADMAS-SURF
Domain for STOC-IC
Image of calculation at Onagawa

## Slide 10: Information of each domain
No. Layer | Grid Size(m) | Ratio of Grid size | Number of grid (X) | Number of grid (Y) | Number of grid (Z) | Number of grid | Code Name | Number of Core
1 | 2,916.0 | － | 500 | 365 | 1 | 182,500 | STOC-ML | 1
2 | 972.0 | 3 | 510 | 390 | 1 | 198,900 | STOC-ML | 1
3 | 324.0 | 3 | 405 | 387 | 1 | 156,735 | STOC-ML | 1
4 | 108.0 | 3 | 900 | 600 | 1 | 540,000 | STOC-ML | 1
5 | 36.0 | 3 | 930 | 930 | 1 | 864,900 | STOC-ML | 1
6 | 12.0 | 3 | 1,020 | 780 | 1 | 795,600 | STOC-ML | 1
7 | 4.0 | 3 | 870 | 627 | 1 | 545,490 | STOC-ML | 1
8 | 4.0 | 1 | 390 | 285 | 13 | 1,444,950 | STOC-IC | 3
9 | 1.0 | 4 | 600 | 800 | 32 | 15,360,000 | CADMAS-SURF/3D | 32
Tsunami Source:
Fujii-Satake ver. 4.0 model with scaling adjustments to match the tsunami waveform obtained with GPS wave sensors off the southern Iwate coast.
Fujii-Satake ver. 8.0
Central Disaster Prevention Council(2011)
Takagawa and Tomita (2012)

## Slide 11: Domain 01, ML
Tsunami Source; Takagawa and Tomita 2012

## Slide 12: STOC-IC to CADMAS-SURF/3D Domain 07 to 08
Tsunami Source; Takagawa and Tomita 2012

## Slide 13: Domain 08, CADMAS-SURF/3D

## Slide 14
Comparison of Maximum Inundation height (Tsunami Source: Takagawa andTomita (2012)
measured

## Slide 15: Comparison of Flow depth
Fujii, Satake –ver 4.0
Central Disaster Prevention Council

## Slide 16: Multiphysics Simulation
Coupled with Structure Analysis

## Slide 17: Outline of CADMAS-SURF/3D-STR
Main program
CADMAS-SURF/3D
(VOF method)
STR3D
(FEM)
calculation step
calculation step
Data on pressure
Data on displacement
call subroutine
call subroutine
Images of CADCADMAS-SURF/3D
(Arikawa et al., 2009)

## Slide 18: Breakwaters
Numerical Conditions
CADMAS
dx=dy=dz=0.10 m
STR
Young's modulus ： 2.35e11
Poisson's ratio ： 0.333
Density
test body ： 2135
dummy caisson ： 2349
Coefficient of friction
static ： 0.6
dynamic ： 0.2
dummy

## Slide 19: Breakwaters
Physical Experiment
Sea side
Harbor side

## Slide 20: Breakwaters
Animation

## Slide 21: Breakwaters
Water Level Difference
62.4cm
The result of the Water Level Difference of the physical experiment is 60.8cm

## Slide 22: Kamaishi Tsunami Breakwater
Suga
Hirata
Izumi
Mouth of Port
Kamaishi Port
Tsunami Breakwaters
North part
South part
Sea Side
Harbor Side

## Slide 23
Inside of Port
Outside of Port
Failure of Breakwater at North Part
深部
浅部
TOHOKU REGIONAL BUREAU MINISTRY OF LAND , INFRASTRUCTURE AND TRANSPORT
Shallow Region
Deep Region

## Slide 24
Calculation Domains
▼ STOC-ML Domain 1 -3
▼ STOC-ML Domains 4 -6
▼ STOC-ML Domain 7
STOC-IC Domain 8
CADMAS Domain 9
Example of Kamaishi Bay

## Slide 25
Example of Kamaishi Bay
CADMAS-STR Domain
Outer Region is by using STOC-ML
Model of Breakwater (All)
Magnification
South
mouth
S1-3
D1-3
D4
D2,3
D1
S3-2
S3-1
S2-2
S2-1
S1-2
S1-1

## Slide 26
CADMAS-STR
Animation
The average of dt is around 0.005s. If 1 hour calculation would be required, it takes around 10 to 20 days

## Slide 27: For evacuation
Coupled with Multiagent simulator

## Slide 28: Coupling with Evacuation Simulation
Coupling STOC, CADMAS-SURF and PARI-AGENT
STOC
CADMAS-SURF
Arikawa and Tomita (2015)
PARI-AGENT

## Slide 29: For inhabitants
Courtesy of Nakatosa town in Kochi Prefecture
Begin to evacuate 10 minutes after the seismic motion
Begin to evacuate 20 minutes after the seismic motion

## Slide 30: Thank you for your attention!!
Let’s study Tsunami together!!
Please come to Japan!!