## Slide 1: How much water is used for irrigation? A new approach exploiting satellite soil moisture observations
Luca Brocca (1), Angelica Tarpanelli (1), Paolo Filippucci (1), Wouter Dorigo (2), Felix Zaussinger (2), Alexander Gruber (2,3), Diego Fernandez Prieto (4)
National Research Council, Research Institute for Geo-Hydrological Protection, Perugia, Italy (luca.brocca@irpi.cnr.it)
CLIMERS – Research Group Climate and Environmental Remote Sensing, Department of Geodesy and Geoinfomation, Vienna University of Technology, Vienna, Austria
Department of Earth and Environmental Sciences, KU Leuven, Heverlee, B-3001, Belgium
European Space Agency, ESA-ESRIN, Frascati, Italy
European General Assembly, Vienna 10th April, 2018
http://hydrology.irpi.cnr.it/people/luca-brocca http://hydrology.irpi.cnr.it

## Slide 2
The irrigation problem
Soil moisture anomalies in Europe in 2017
Copernicus Climate Service (C3S)
CNR Press Release by
Luca Brocca and Wouter Dorigo (1st July 2017)
Water scarcity is a current issue in many parts of the world, and particularly in Europe in the recent and current period. Climate changing is expected to exacerbate the problem.
We currently do not have information about the water used for irrigation, except for statistical inventories available for specific and small regions and/or at multiannual temporal scale
 Accurate information on irrigation water are desperately needed
Irrigated agriculture accounts for about 70 percent of water withdrawn worldwide being the greatest human intervention in the hydrological cycle.

## Slide 3
The IDEA: using soil moisture for irrigation
From soil moisture to irrigation
Modelling (climate/hydrology)
Satellite observations
Irrigation
Detection of irrigated areas
Quantification of irrigation water
SM2RAIN is a new “bottom-up” approach (Brocca et al., 2014 JGR) for estimating the ACCUMULATED RAINFALL from satellite (and in situ) soil moisture observations
SM2RAIN: From soil moisture to rainfall
https://www.linkedin.com/pulse/do-you-know-sm2rain-read-here-its-short-story-luca-brocca
http://hydrology.irpi.cnr.it/research/sm2rain
ORAL TOMORROW Rainfall estimation from soil moisture observations, SM2RAIN: recent advances and future directions Brocca, L. et al; Wed, 11 Apr, 15:30–15:45, Room B

## Slide 4
WACMOS-IRRIGATION project
Understanding of the potential of satellite soil moisture data to obtain irrigation information on a global scale

## Slide 5
WACMOS-IRRIGATION project
DETECTING IRRIGATION THROUGH COARSE RESOLUTION SATELLITE SOIL MOISTURE PRODUCTS ON A GLOBAL SCALE
QUANTIFYING IRRIGATION THROUGH IN SITU SOIL MOISTURE DATA
QUANTIFYING IRRIGATION THROUGH COARSE RESOLUTION SATELLITE SOIL MOISTURE PRODUCTS
QUANTIFYING IRRIGATION THROUGH HIGH RESOLUTION SATELLITE SOIL MOISTURE PRODUCTS
not shown!
4 slides
4 slides
1 slides

## Slide 6
THE adapted “sm2rain” METHOD
precipitation
surface runoff
evapotranspiration
drainage
soil water capacity
relative soil moisture
= soil depth X porosity
Z*ds(t)/dt=p(t)+i(t)-r(t)-e(t)-g(t)
e(t): evapotranspiration
p(t): precipitaition
i(t): irrigation
SOIL LAYER
g(t): drainage = deep percolation + subsurface runoff
r(t): surface runoff
Inverting the water balance equation for i(t), assuming:
g(t)=as(t)b
r(t)=0
e(t)=ETpot(t)s(t)
i(t)=Z* ds(t)/dt+a s(t)b+ETpot(t) s(t)-p(t)
1 equation
3 parameters (Z*,a, b) + knowledge of s(t), p(t) and ETpot(t)
irrigation

## Slide 7
SYNTETHIC DATA
We apply 600 mm per year from June to September
We have soil moisture data affected by irrigation, i.e., synthetic satellite soil moisture (red line)
We apply SM2RAIN to satellite soil moisture to obtain SM2RAIN-derived rainfall+irrigation (magenta)
We subtract observed rainfall (green) from SM2RAIN-derived rainfall+irrigation to obtain irrigation
The method theoretically works

## Slide 8
CANIZAL station
Application of SM2RAIN in non irrigated periods
R=0.78
Spain
IN SITU SOIL MOISTURE DATA
Green=observed
Red=SM2RAIN-derived
SOIL MOISTURE
PRECIPITATION

## Slide 9
To be compared with actual observations 
Spain
IN SITU SOIL MOISTURE DATA
SOIL MOISTURE

## Slide 10
…finally the first irrigation + soil moisture observations last week!!!
GOAL: study the soil water content measuring the attenuation effects on gamma rays emitted by terrestrial radionuclides during a tomato crop season.
Soil moisture, precipitation and irrigation are measured!!!
Courtesy by F. Mantovani, V. Strati, and M. Baldoncini (UNIFE)
Italy
IN SITU SOIL MOISTURE DATA

## Slide 11
We apply the adapted SM2RAIN algorithm to gamma-ray soil moisture observations. Parameter values are calibrated against precipitation observations only.
The validation with irrigation data (in green) shows good performance of the proposed approach (agreement between red line and green bar) !!!
The method works if forced with in situ soil moisture observations (good quality)
Italy
IN SITU SOIL MOISTURE DATA

## Slide 12
URMIA LAKE (Iran)
STUDY AREA Southern part of Urmia Lake  Miandoab plain in West Azarbayjan province of Iran.
DATASETS | AGENCY PRODUCER | SPATIAL EXTENSION | PERIOD | SPATIAL/TEMPORAL SAMPLING
GLEAM | ESA | Global | 2011-2015 | 0.25-degree/1-day
AMSR2 | JAXA | Global | 2012-continuing | 0.25-degree/~1-day
MSWEP | European Commission, Joint Research Centre (JRC) | Global | 1979-2015 | 0.25/3 hours
In-situ Precipitation | Meteorological Organization | - | 1980-continuing | 1-day
In-situ irrigation | WRM organization | - | 2012-2015 | 1-day
COARSE RESOLUTION SATELLITE SOIL MOISTURE

## Slide 13
ORAL (THIS MORNING !) Estimation of Irrigation Water Using Satellite Soil Moisture Data in a Semi-Arid Area
Hashemi et al; Tue, 10 Apr, 09:45–10:00, Room 2.15
For a very large irrigated area, AMSR2-JAXA soil moisture product is able to detect irrigation, the proposed approach provides reliable irrigation estimates
COARSE RESOLUTION SATELLITE SOIL MOISTURE

## Slide 14
CALIFORNIA
NEBRASKA
MISSISSIPPI
MURCIA
ANDALUSIA
CASTILLA Y LEON
YANCO
ROMAGNA
MARRAKECH
a)
b)
c)
PILOT SITES
USA: California, Nebraska, Mississippi
AUSTRALIA: Yanco
SPAIN: Andalusia, Castilla Y Leon, Murcia
ITALY: Romagna
MOROCCO: Marrakech
COARSE RESOLUTION SATELLITE SOIL MOISTURE

## Slide 15
CALIFORNIA
Results for the different pilot sites are encouraging, but the unavailability of a benchmark (i.e., observed irrigation) does not allow to test properly the method… GROUND OBSERVATIONS OF IRRIGATION ARE NEEDED!
COARSE RESOLUTION SATELLITE SOIL MOISTURE
SMOS
SMAP
ASCAT
AMSR2-JAXA
AMSR2-LPRM

## Slide 16
HIGH RESOLUTION SATELLITE SOIL MOISTURE
ROMAGNA (ITALY)
IRRIGATED PIXEL
NON-IRRIGATED PIXEL
Different high-resolution satellite soil moisture products (e.g., SMOS 1km, SMAP and AMSR2 9km) are used in Italy and Spain, where we have in situ data. Only with Sentinel-1 satisfactory results are obtained, so far!
Sentinel-1 sees irrigation over small areas !!!
Courtesy by B. Bauer-Marschallinger (TUWien)
Simulated SM with IRRIGATION
Simulated SM without IRRIGATION
ASCAT
Sentinel-1

## Slide 17
TAKE HOME MESSAGES
QUESTIONS?
http://hydrology.irpi.cnr.it/people/luca-brocca http://hydrology.irpi.cnr.it
We can use in situ soil moisture observations for quantifying irrigation through the adapted SM2RAIN
Coarse resolution satellite soil moisture products have shown some potential
High resolution satellite soil moisture products are more appropriate for irrigation quantification