## Slide 1
Evolution of the Viennese Urban Heat Island caused by expected Reduction of Vegetation Fraction in favour of Built-up Land until 2030/2050
Project: URBANIA - Influence of the development of outlying districts and urban growth on the urban heat island of the city of Vienna in the context of climate change
ACRP 8th call: KR14AC7K11944
Project team:
Institute of Meteorology, University of Natural Resources and Life Sciences (BOKU):
BOKU-Rad: Philipp Weihs, Heidelinde Trimmel, Sandro Oswald
BOKU-Klim: Herbert Formayer, Imran Nadeem
BOKU-Biomet: Erich Mursch-Radlgruber, Christian Gützer
Environmental Agency of Vienna (MA22): Jürgen Preiss, Christian Härtel
CNRS-Météo-France: Valéry Masson, Robert Schoetter, Aude Lemonsu, Stéphanie Faroux
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
EGU 2018-7927
CL.18
11/4/2018

## Slide 2
Von Lodp - Eigenes Werk, Statistischen Mitteilungen der Stadt Wien (Heft 4/2000)Statistik Austria. Statistisches Jahrbuch 2009. http://www.statistik.at/web_de/static/bevoelkerung_zu_jahresbeginn_seit_1981_nach_bundeslaendern_031770.xlsx http://www.statistik.at/web_de/static/bevoelkerung_zu_quartalsbeginn_seit_2002_nach_bundesland_023582.xlsx
http://www.statistik.at/web_de/statistiken/menschen_und_gesellschaft/bevoelkerung/bevoelkerungsstand_und_veraenderung/bevoelkerung_zu_jahres-_quartalsanfang/023582.html , CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=29606863
Breakdown of Austrian-Hungarian Empire
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
Vienna‘s population is growing ...
- > will reach 1900 level again 2028
-> but 1971:22.9m²/person, 2014:44.7m²/person (trend stabalizing)
-> amount of population growth uncertain (parameters: fertility, life expectancy, migration (national and international))
Motivation
EGU 2018-7927
CL.18
11/4/2018

## Slide 3
1844 - Description of urban heat island by A.Stifter
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
Motivation
-> increased demand and supply of residential and other urban areas
-> increased urban heat island
Problem? Lets have EGU in summer to discuss...
EGU 2018-7927
CL.18
11/4/2018

## Slide 4
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
Population is growing in widespread around city borders
Greater Vienna: 2030: max +15.15% per district
2060: max +29.30% per district
-> main growth in „stadtregion+“ (see: PGO 2010)
How much + where?
within city borders: 2030: max +27.2 % per district
2060: max +55.2 % per district
EGU 2018-7927
CL.18
11/4/2018

## Slide 5
-> Tmax >= 35°C since observation started (Wien Hohe Warte)
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
Year
Number of days Tmax >=35°C per year
2015
Selection of reference period
EGU 2018-7927
CL.18
11/4/2018

## Slide 6
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
NEST1
NEST2
NEST3
NEST4
Lateral boundary conditions:
9km ECMWF analysis data (6h)
Static: Topography- SRTM1Arc:30m)
Landcover-USGS Classes (1 urban class)
WRF v3.9.1
EGU 2018-7927
CL.18
11/4/2018

## Slide 7
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
-Spatial distribution fits
good to gridded
interpolated observations
data set (INCA1)
- Spatial patterns are represented
even better (rivers and lakes, urban area )
-Absolute values fit good <1°C on average
- WRF slightly underestimates air temperature
Comparison with observation data
1 Haiden et al. 2011
EGU 2018-7927
CL.18
11/4/2018

## Slide 8
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
Comparison WRF, WRF/SURFEX offline and ground stations
EGU 2018-7927
CL.18
11/4/2018

## Slide 9
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
Model runs:
- WRFv3.9.1 using USGS classes (US)
Comparison WRF, WRF/SURFEX offline and ground stations
Bias
EGU 2018-7927
CL.18
11/4/2018

## Slide 10
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
Model runs:
- WRFv3.9.1 using USGS classes (US)
SURFEXv8 offline runs forced by WRF:
WRF/S using ECOCLIMAP (EC)
Comparison WRF, WRF/SURFEX offline and ground stations
Bias

## Slide 11
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
Model runs:
- WRFv3.9.1 using USGS classes (US)
SURFEXv8 offline runs forced by WRF:
WRF/S using ECOCLIMAP (EC)
- WRF/S high resolution maps (PM)
Comparison WRF, WRF/SURFEX offline and ground stations
using: highres. building height, surface fractions, UrbanAtlas,CORINE,...
Bias
EGU 2018-7927
CL.18
11/4/2018

## Slide 12
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
Model runs:
- WRFv3.9.1 using USGS classes (US)
SURFEXv8 offline runs forced by WRF:
WRF/S using ECOCLIMAP (EC)
- WRF/S high resolution maps (PM)
- WRF/S (PM)S forced by first sigma level (~40m)
Comparison WRF, WRF/SURFEX offline and ground stations
Bias
EGU 2018-7927
CL.18
11/4/2018

## Slide 13
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
-> WRF tends to underestimate maxima
-> WRF/SURFEX tends to overestimate maxima
-> both overestimate minima
-> clouds are not predicted well
Comparison WRF, WRF/SURFEX offline and ground stations
EGU 2018-7927
CL.18
11/4/2018

## Slide 14
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
observed land use change
people within Vienna city borders:
2001: 1.550.123
CORINE 2000
EGU 2018-7927
CL.18
11/4/2018

## Slide 15
CORINE 2012
people within Vienna city borders:
2014: 1.766.746 (13J: +216.623) +14% ref. to 2001
2030: 2.077.300 (16J: +310.554) +18% ref to 2014
2050: 2.286.094 (36J: +519.348) +30% ref to 2014
Change of „Mobilitätsreserve?“
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
observed land use change
EGU 2018-7927
CL.18
11/4/2018

## Slide 16
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
S1
STQ
Diurnal circle of air temperature on day Tmax>30°C („heißer Tag“)
Max: +0.3 °C
S1-STQ
0UTC
6UTC
18UTC
@ 2UTC+ @ 13UTC:
Tmax_urban- Tmin_rural = 8°C
12UTC
WRF/S (PM)
2050+ Scenario 1) increased built area >85% +10%
„DENSER“
EGU 2018-7927
CL.18
11/4/2018

## Slide 17
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
„LARGER“
 |  | 2012 „STQ“ | 2050+ Scenario 2 „scattered“ extrapolated current growth | 2130+ Scenario 3 „structured“ development following traffic axes
Simulation input Nest3 | „Built-up land“ fraction [km²] | 9 02 (100%) | 1 113 (123%) | 1 449 (161%)
 | „Nature“ fraction [km²] | 3 284 (100%) | 3 073 (94%) | 2 736 (83%)
Real Stadtregion+ | actual urban area [km²] | 1 080 (100%) |  | 
New urban areas:
Lower buildings -> more space demand
EGU 2018-7927
CL.18
11/4/2018

## Slide 18
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
S3
S2
STQ
new urban area set uniform
as first test:
BLT=0.5
GARDEN=0-2
BH=10
WALL_O=0.5
WRF/S (PM-XUNIF)
Diurnal circle of air temperature on day Tmax>30°C („heißer Tag“)
EGU 2018-7927
CL.18
11/4/2018

## Slide 19
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
S4
S3
STQ
North
East
West
South
Center
13UTC Tair | C | W | N | E | S
STQ | 29.0 | 24.6 | 23.8 | 25.1 | 26.6
S4 | 29.3 | 25.2 | 24.3 | 25.4 | 27.0
Diff | +0.3 | +0.6 | +0.6 | +0.3 | +0.4
Regions:10x10points-> 11km²

## Slide 20
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
S4-STQ:
increased built area + insolation
0 UTC
6 UTC
12 UTC
18 UTC
Min: -0.5 °C
Max:+0.3 °C
S2-STQ: increased isolation
 | 2012 | 2130+ Scenario 4)
Heat capacity wall [J/m³K] Commercial High and low density residential | 0.975 *106 1.520 *106 | 0.975 *106 1.496 *106
Heat capacity roof [J/m³K] (all categories) | 1 554 000 | 1.496 *106
Thermal conductivity wall [W/mK] (all categories) | 1.7 | 0.1
Thermal conductivity roof [W/mK](all categories) | 1.4 | 0.1
Values of this table calculated using spatial data sets of Vienna and absolute values from: Amtmann M and Altmann-Mavaddat N (2014) Eine Typologie österreichischer Wohngebäude, Austrian Energy Agency, TABULA/EPISCOPE; Berger T et al. (2012) Auswirkungen des Klimawandels auf den thermischen Komfort in Bürogebäuden, Berichte aus der Energie- und Umweltforschung |  | 
„TOWARDS SOLUTIONS“
WRF/S (PM)
EGU 2018-7927
CL.18
11/4/2018

## Slide 21
First conclusions - possible relativ changes of air temperature (derived only from surface energy balance changes):
Densification of built up area
  -> maximum +0.3 °C within actual urban areas.
  -> Largest increases in the evenings.
Urban sprawl -> maximum +2°C in the new urban area
-> spatial average: 0.6°C.
-> also the actual urban structure will be affected.
Countermeasures as ambitioned insolation
-> -0.5°C within the actual urban area during night
-> even under increased building density
-> also at noon in the inner districts air temperature
could be reduced even when the built area is increased
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
EGU 2018-7927
CL.18
11/4/2018

## Slide 22
Next steps:
Effects of urban densification and expansion on temperature including roughness modified wind field, change of urban boundary layer using WRF:
WRF-TEB coupling ongoing!
Szenarios will be run with:
3 land use categories (simplified from LCZ categorization according to WUDAPT Methodology – Steward and Oke 2012, presented EGU2017)
PBL-Scheme: Yonsei University Scheme
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
EGU 2018-7927
CL.18
11/4/2018

## Slide 23
Lots more to do:
In depth spatio-temporal analysis of observed heat waves
Analyze effect on thermal comfort within urban canopy
-> see poster: EGU2018-9582 Oswald et al. 2018
today, 11 Apr, 17:30–19:00
Search for key factors and more effective urban szenarios (together with city authorities):
Change of spatial distibution of new building areas
Change of building morphology
Building properties (roof albedo, new materials, latent heat, ...)
Climate change 2030/2050 for RCP4.5 and RCP8.5
Role of anthropogenic heat (spatio-temporal patterns)
website launch July 2018: http://urbania.boku.ac.at
1 Viennese Growth
2 Models
4 Conclusion and outlook
3 Urban Szenarios
EGU 2018-7927
CL.18
11/4/2018

## Slide 24
Thank you for your attention!