## Slide 1: The geomorphic and hydrological responses to flood embankment lowering on a medium sized gravel-bed river.
Addy, S. and Wilkinson, M.E.
Aberdeen, Scotland, UK

## Slide 2: Background
Naturally functioning floodplains are important for river ecosystem integrity (e.g. Tockner and Stanford, 2002).
Floodplain reconnection is needed to restore functions but case studies remain rare.
River Dee: good ecological status but morphology often unnatural due to engineering. Flooding is also an issue.
Upper River Dee, NE Scotland

## Slide 3: Study site
Restoration site
River Dee
18th C. embankment
18th C. drainage network
Aerial imagery: Corpyight Getmapping plc. 2010 DSM map courtesy of Aberdeenshire Council.
Upstream catchment area: 370 km2
BRAEMAR

## Slide 4: Restoration project and research aims
Project aims
To reduce flooding and erosion, improve water supply during low flows, and diversify riverine habitats.
Removal of waste and visual impact.
Research questions
How does the morphology of the main channel, floodplain and backwater change through re-connection?
How does the floodplain hydrological connectivity and water storage compare pre- and post barrier removal?
Aug. 2015 (pre-reconnection)
Sept. 2015 (during works)
2 m
Anke Addy

## Slide 5
Mar Lodge SEPA gauging station 3 km upstream
ML1 (ditch WL sensor)
ML2 (floodplain WL sensor)
ML3 (backwater WL sensor)
Time-lapse camera
XS surveys
Backwater
River Dee
Monitoring (2013-onwards)
XS surveys
2016 (post-restoration)

## Slide 6
Hydrology (2013-2018)
ML2 (floodplain WL sensor)
Median annual peak Q
30/12/2015 ‘Storm Frank’ (post-restoration)
Joanna Dick, River Dee Trust
Reconnection
site
RESTORATION

## Slide 7: Morphological responses: floodplain & backwater
2014 (pre-restoration)
2016 (post-restoration)
2015-2018 Σ volumetric response: 477.2±24 m3
Δ Cross section area: -8.5 m2 (-26%)

## Slide 8
Chart: Chainage (m)
Sept-2014 | 324.4464 | 324.5786 | 324.5884 | 324.5887 | 324.8208 | 324.8998 | 324.8998 | 323.1771 | 323.178 | 323.1724 | 323.1547 | 322.7891 | 322.746 | 322.7208 | 322.719 | 322.7325 | 322.7673 | 322.8255 | 322.8656 | 322.921 | 323.1702 | 323.2066 | 323.3318 | 323.3827 | 323.4542 | 323.5323 | 323.5395 | 323.5634 | 323.6441 | 323.6561 | 323.9324 | 323.9588 | 324.0944 | 324.2494 | 324.5792 | 324.43 | 324.1434 | 324.1298
May-2017 | 324.4455 | 324.2242 | 324.1502 | 324.1501 | 324.1489 | 323.9159 | 323.9129 | 323.6882 | 323.6187 | 323.5215 | 323.5076 | 323.3692 | 323.3641 | 323.3629 | 323.2985 | 323.296 | 323.2618 | 323.2721 | 323.2738 | 323.3159 | 323.3149 | 323.3194 | 323.3713 | 323.3911 | 323.3924 | 323.3943 | 323.4 | 323.4094 | 323.5293 | 323.5358 | 323.5394 | 323.815 | 325.1924 | 325.204 | 324.8665 | 324.5206
XS
Morphological responses: channel
2015-2018 Σ volumetric response: 1030±51 m3
ΔCross section: -5.4 m2 (-13%)
EMBANKMENT

## Slide 9: Floodplain hydrology annual responses
Chart: Median river discharge (m3/s)
| 9.2010000000000005 | 8.6189999999999998
Pre restoration | 323.3393 | 323.3633
Post restoration | 323.4063 | 323.359 | 323.3985
ML2 (floodplain WL sensor)
ML2
2013/2014 vs 2015/2016
Mann-Whitney U-test: p= 0.000

## Slide 10: Event response magnitudes
Chart: Peak discharge (m3/s)
| 376.79500000000002 | 170.41399999999999 | 153.6 | 136.30199999999999 | 129.15600000000001 | 126.52200000000001 | 111.511 | 109.256 | 100.786 | 91.647000000000006 | 85.641999999999996 | 257.64299999999997 | 200.542 | 179.27099999999999 | 178.7 | 165.685 | 162.43199999999999 | 156.39099999999999 | 145.72200000000001 | 143.541 | 127.411
 | 324.6683 | 324.0443 | 323.9063 | 323.9763 | 323.9343 | 324.0123 | 323.9753 | 323.8193 | 323.6563 | 323.6433 | 324.3813 | 323.8283 | 324.0103 | 323.8687 | 324.0203 | 324.0383 | 323.9293 | 323.8693 | 323.8913 | 323.8613
 | 324.7953 | 324.5623 | 324.5556 | 324.4933 | 324.4726 | 324.4864 | 324.4355 | 324.4453 | 323.5618 | 323.8584 | 323.6526 | 323.604 | 323.5903 | 324.396 | 324.43 | 324.303 | 323.831 | 323.711 | 323.733 | 323.87 | 323.643 | 323.705 | 323.675 | 324.45 | 324.445 | 324.387 | 324.384 | 324.273 | 324.046 | 324.034 | 324.004 | 323.88 | 323.857 | 323.486
Chart: Water surf. elev. (m.a.s.l.)
| 376.79500000000002 | 170.41399999999999 | 153.6 | 136.30199999999999 | 129.15600000000001 | 126.52200000000001 | 111.511 | 109.256 | 100.786 | 91.647000000000006 | 85.641999999999996 | 257.64299999999997 | 200.542 | 179.27099999999999 | 178.7 | 165.685 | 162.43199999999999 | 156.39099999999999 | 145.72200000000001 | 143.541 | 127.411
Pre-restoration | 324.672 | 324.207 | 324.206 | 324.124 | 323.944 | 324.021 | 323.849 | 323.694 | 323.622 | 323.612 | 324.36 | 324.248 | 324.208 | 324.2639 | 324.161 | 324.121 | 324.055 | 324.046 | 324.057 | 323.864
Post-restoration | 324.767 | 324.498 | 324.4663 | 324.485 | 324.3984 | 324.4076 | 324.3768 | 324.432 | 323.3634 | 324.0318 | 323.5711 | 323.6234 | 324.422 | 324.392 | 324.351 | 324.331 | 324.275 | 324.182 | 324.014 | 324.104 | 323.422 | 323.712 | 323.6 | 324.421 | 324.358 | 324.319 | 324.199 | 324.419 | 323.8 | 324.303 | 324.404 | 323.534 | 323.534 | 323.765
Chart: 
| 376.79500000000002 | 170.41399999999999 | 153.6 | 136.30199999999999 | 129.15600000000001 | 126.52200000000001 | 111.511 | 109.256 | 100.786 | 91.647000000000006 | 85.641999999999996 | 257.64299999999997 | 200.542 | 179.27099999999999 | 178.7 | 165.685 | 162.43199999999999 | 156.39099999999999 | 145.72200000000001 | 143.541 | 127.411
 | 324.9643 | 324.4573 | 324.4263 | 324.3523 | 324.1623 | 324.2263 | 324.1853 | 324.0813 | 323.8903 | 323.7263 | 324.6883 | 324.4573 | 324.4663 | 324.4803 | 324.3633 | 324.3163 | 324.3143 | 324.2453 | 324.3203 | 324.1873
 | 325.507 | 325.2072 | 325.0272 | 325.0372 | 324.9532 | 324.802 | 323.5343 | 324.4732 | 323.8802 | 323.8352 | 323.7972 | 324.8088 | 324.754 | 324.6258 | 324.5488 | 324.4418 | 324.3058 | 324.3378 | 324.017 | 324.1618 | 324.1458 | 324.807 | 324.775 | 324.7 | 324.644 | 324.632 | 324.612 | 324.492 | 324.313 | 324.278 | 324.67
Pre-rest bank level | 324.5 | 324.5
Post-rest bank level | 324.3 | 324.3
ML1 (ditch)
ML2 (floodplain)
ML3 (backwater)
Distance
from river: 400 m 250 m 70 m

## Slide 11: Event response times
Chart: Response time (min)
| 376.79500000000002 | 170.41399999999999 | 153.6 | 136.30199999999999 | 129.15600000000001 | 126.52200000000001 | 111.511 | 109.256 | 100.786 | 91.647000000000006 | 85.641999999999996 | 257.64299999999997 | 200.542 | 179.27099999999999 | 178.7 | 165.685 | 162.43199999999999 | 156.39099999999999 | 145.72200000000001 | 143.541 | 127.411
Pre-restoration | 15 | 30 | 75 | 60 | 75 | 90 | 75 | 165 | 645 | 15 | 60 | 90 | 60 | 15 | 60 | 75 | 60 | 90 | 30 | 45
Post-restoration | 30 | 30 | 75 | 60 | 15 | 60 | 45 | 60 | 2040 | 105 | 1815 | 75 | 60 | 60 | 60 | 60 | 60 | 105 | 145 | 4245 | 690 | 1620 | 30 | 60 | 30 | 390 | 75 | 390 | 90 | 90 | 480 | 780 | 1695
Chart: Peak discharge (m3/s)
| 376.79500000000002 | 170.41399999999999 | 153.6 | 136.30199999999999 | 129.15600000000001 | 126.52200000000001 | 111.511 | 109.256 | 100.786 | 91.647000000000006 | 85.641999999999996 | 257.64299999999997 | 200.542 | 179.27099999999999 | 178.7 | 165.685 | 162.43199999999999 | 156.39099999999999 | 145.72200000000001 | 143.541 | 127.411
 | 15 | 450 | 420 | 360 | 510 | 210 | 270 | 525 | 330 | 360 | 30 | 375 | 510 | 315 | 300 | 210 | 285 | 375 | 315 | 270
 | 30 | 30 | 30 | 45 | 15 | 60 | 45 | 90 | 285 | 960 | 285 | 285 | 165 | 75 | 45 | 105 | 300 | 255 | 315 | 930 | 345 | 690 | 270 | 75 | 60 | 60 | 120 | 240 | 390 | 2550 | 900 | 195 | 285 | 390
Chart: 
| 376.79500000000002 | 170.41399999999999 | 153.6 | 136.30199999999999 | 129.15600000000001 | 126.52200000000001 | 111.511 | 109.256 | 100.786 | 91.647000000000006 | 85.641999999999996 | 257.64299999999997 | 200.542 | 179.27099999999999 | 178.7 | 165.685 | 162.43199999999999 | 156.39099999999999 | 145.72200000000001 | 143.541 | 127.411
 | 15 | 75 | 60 | 75 | 75 | 60 | 150 | 525 | 795 | 15 | 15 | 30
 | 75 | 30 | 45 | 60 | 75 | 780 | 90 | 435 | 255 | 315 | 75 | 30 | 60 | 60 | 60 | 60 | 60 | 225 | 105 | 90 | 60 | 75 | 90 | 60 | 45 | 75 | 390 | 75 | 60 | 60
ML1 (ditch)
ML2 (floodplain)
ML3 (backwater)
Distance
from river: 400 m 250 m 70 m

## Slide 12
Period | Overspill floodplain discharge threshold (m3/s) | Bank threshold height (m.a.s.l.) | Overspill events N (post-restoration threshold) | Overspill events N (pre- restoration threshold)
Post-restoration (2015-2018) |  | 324.3 | 39 | 6
Pre-restoration (2013-2015) |  | 324.5 | 32 | 9
Overspill threshold
~40
~150

## Slide 13: Conclusions
Post-restoration responses:
  Channel aggradation, erosion of lowered embankment and development of a more natural shape.
  Overspill threshold discharge for backwater connection is ~70% lower.
  For a given discharge, overspill WSE is higher due to improved connectivity. Event response times are site-dependant.
  Annual median water table levels were 4-9 cm higher despite lower annual median river flows.
Improved floodplain connectivity could affect floodplain hydro-ecology, maintain baseflows and attenuate moderate floods.

## Slide 14: Thank you for your attention stephen.addy@hutton.ac.uk
Acknowledgements This study was funded by the Rural and Environmental Science and Analytical Services (RESAS) division of the Scottish Government. Mar Lodge Estate are thanked for access. SEPA supplied discharge and rainfall data. Numerous students and staff from the James Hutton Institute assisted with fieldwork. Restoration funded by EU Life Project: ‘Pearls in Peril’.