## Slide 1: Public outreach for the EC Carbon-14 Source Term project
Name: Erika Neeft & Simon Norris
Organisation: COVRA & RWM
Date: 8 April 2019

## Slide 3: Familiarisation
Radiation?
Not only radioactive waste
Carbon-14?
Not only radioactive waste

## Slide 4: Newsletters
Audience: Public
  No knowledge concerning radiation protection
  Unfamiliar to carbon-14 containing waste
Dissemination plan
  Topics based on scheduled publications
    A3 infographic each Newsletter
    With a carbon-14 analogue of cosmic origin

## Slide 5: Aim
CAST (Carbon-14 Source Term) was an EU research project that aimed to develop understanding of the potential release of carbon-14 from radioactive waste materials under conditions relevant to waste packaging and disposal to underground geological disposal facilities. The project focussed on the release of carbon-14 as dissolved and gaseous species from irradiated metals (steels, Zircaloys), irradiated graphite and spent ion-exchange resins.

## Slide 6: Generation of carbon -14
Visualization of EU research project in one picture,
origin of carbon-14 for the types of waste investigated in CAST

## Slide 7: Generation of carbon -14
 + natural abundance  10,000 times C and 10,000,000 times O

## Slide 8: Generation of carbon-14
Natural carbon-14
80% nitrogen
environmental neutron flux: 0.001 neutrons per cm2 per s
Artificial carbon-14
nitrogen in ppm in materials
Thermal neutron flux in core NPP: 100,000,000,000,000 neutrons per cm2 per s
Carbon-14 concentrations in waste larger than 1 Bq per gram

## Slide 9: Release of carbon-14
1: No chemical degradation rate for graphite and ion exchange resins
1: Chemical corrosion rates for steel and Zircaloy are small in alkaline, reducing environments
2: carbon-14 release as gas, non-ionic or anionic dissolved carbon-14 species
3: E.g. period to pass clay or salt host rock may take several half-lives of carbon-14
4: A common value for dilution for geological disposal is 10,000
5: Any reduced carbon species will be oxidised to carbon dioxide by microbes

## Slide 10: Comparison
Artificial if chemical resistance waste form, diffusion clay host rock
and dilution in surrouding rock formations are included
Natural: 1,000,000,000 carbon-14 molecules per cm2 per year

## Slide 11: Public outreach for CAST
Newsletters and other CAST deliverables can be downloaded at https://www.projectcast.eu until March 2023
References and justification of assumptions used in this presentation:
Thank you for your attention
Any questions?