## Slide 1: Long-term Observations of Atmospheric Speciated Mercury at a Coastal Site in the Northern Gulf of Mexico during 2007–2018
Xinrong Ren1,2,*, Winston Luke1, Paul Kelley1,2, Mark Cohen1, Mark Olson3, Jake Walker4, Ronald Cole4, Michael Archer4, Richard Artz1, Ariel Stein1
1NOAA Air Resources Laboratory
2University of Maryland CISESS
3University of Wisconsin, Wisconsin State Laboratory of Hygiene
4Grand Bay NERR
*Correspondence to: X. Ren (Xinrong.Ren@noaa.gov)
Notes: At NOAA Air Resources Laboratory we run 3 AMNet sites. One of the sites is located in Grand Bay in Mississippi, a coastal site in northern Gulf of Mexico. Today I will be presenting the data collected at this site. First of all I would like to acknowledge my colleagues at NOAA ARL, our site operators at Grand Bay NERR and Mark Olson, the AMNet liaison.

## Slide 2
Motivation
To establish long-term data record of ambient concentrations of mercury species (GEM, GOM, and PBM).
To assess the regional budget of atmospheric mercury using long-term measurements with high-time resolution.
To elucidate source-receptor relationships and examine relative contributions of natural and anthropogenic processes.
Notes: In terms of the motivation behind this study, we would like to establish long-term atmospheric Hg measurements, to assess Hg budget and well as examine the source-receptor relationship to investigate the contributions of nature and anthropogenic processes.

## Slide 3
Site Location and Regional Hg Point Sources
Emission of Hg point sources (kg yr-1)
Grand Bay site
Grand Bay
Colored circles: US EPA NEI of Hg point sources in 2014
AMNet site (MS12) at Grand Bay in Moss Point, Mississippi (30.41N, 88.40W)
A rural site in the northern coast of Gulf of Mexico.
Notes: Here are maps showing the location of the site and regional Hg point sources based on the US EPA national emission inventory for 2014. Colored circles show the Hg point sources with Hg emissions greater than 10 kg/yr. The grand Bay site is located here, in the northern Gulf of Mexico. The zoomed-in maps on the right show the regional Hg point sources near the Grand Bay site.

## Slide 4
Measurements
Period: 2007 – 2018 (still on-going)
Two collocated Tekran Hg speciation systems for GEM/GOM/PBM
Trace gas: O3, SO2, CO, NO, NOy, and black carbon
Met: wind, T, P, RH, precipitation, and solar radiation
Weekly NADP/NTN measurements (major ions in precipitation) and MDN (mercury wet deposition).
Notes: The site have been operational since 2007. We had two collocated Tekran mercury speciation systems to measure gaseous elemental mercury (GEM), gaseous oxidized mercury (GOM) and particulate bound mercury (PBM). We also measured air pollutants like ozone SO2, CO, reactive NO, NOy and black carbon as well as meteorological parameters. We also collect weekly precipitation sample to measure major ions and mercury wet deposition. Here are a few pictures showing the site instrumentation. Sample units are located on the top of a 10-m walk-up tower and analyzers are housed inside a shelter, a picture showing the surrounding area and wet deposition samplers.

## Slide 5
Statistics of Hour Hg Measurements
Notes: Now let’s look at the data. Here is the statistics of hourly measurements of GEM, GOM, and PBM. I apologize this is a busy table, but maybe just focus on this last line, the statistics of the entire 10 years of Hg measurements. The mean concentrations are about 1.4 ng/m3 for GEM, 5 pg/m3 for GOM and 6 pg/m3 for PBM. Here are measurement frequency plots for GEM, GOM and PBM. A nearly normal distribution for GEM, ~30% of GOM concentrations are between 0 and 0.5 pg/m3, and about 14% of the PBM concentrations are closed to zero.

## Slide 6
Inter-annual Variations
A slight decreasing in GEM: -0.5% yr-1 (p<0.01).
A significant decrease in GOM: -7.1% yr-1 (p<0.01).
A slight increasing in PB: +3.5% yr-1 (p>0.01)
High GEM/GOM/PBM events were observed occasionally.
A slight increasing for Hg wet deposition: +3.5% yr-1 (p>0.01).
Notes: Ok, here are time series of Hg data since 2007 for GEM, GOM, and PBM. The blue dots represent hourly measurements, the green circles represent quarterly mean values, and the red dashed line show the linear regression for the quarterly mean. At the bottom I’m also showing you the weekly Hg wet deposition

## Slide 7
Seasonal Variations
GEM: higher in spring/winter, lower in fall.
GOM: higher in spring/fall, lower in summer/winter
PBM: higher in spring /winter, lower in summer.
Hg wet deposition: higher in spring /summer (wet season), lower in fall/winter (dry season).
Monthly precipitation (mmx5)
Notes: Here are seasonal diurnal variations of GEM/GOM/PBM/Hg wet deposition. The linked black circles in the bottom panel are the composite monthly precipitation amounts (units: mm × 5). The mercury wet deposition is roughly proportional to rainfall with the highest amount in summer and lowest amount in fall and winter.

## Slide 8
Diurnal Variations
mean
Notes: Here are whisker plots showing the diurnal variations of GEM/GOM/PBM. On each box, the central mark is the median, the edges of the box are the 25th and 75th percentiles, the green lines represent the mean diurnal variations. As we can see there is a min. GEM in the early morning. We think this is related to the GEM depletion due to fog. Max. GOM was observed in the mid-afternoon, which is probably due to atmospheric oxidation processes or maybe vertical mixing of air to bring higher GOM concentrations in the upper atmosphere to the surface. Nighttime GOM concentrations are close to zero due to dry deposition of GOM. Max. PBM concentrations were observed in the mid-day and PBM concentrations stays elevated, low at night. The right 3 panels show the diurnal profiles in different seasons.

## Slide 9
Correlations of GOM/PBM with O3 and Humidity
Generally positive correlation btw GOM & ozone
Humidity can affect [GOM] at high [O3]
Generally positive correlation btw PBM & ozone.
Humidity can affect [PBM] at high [O3].
Notes: Let’s look at the correlation of Hg with other measurements. Plotted on the left is ozone versus GOM colored by H2O concentration. As we can see there is a positive coloration between GOM and O3 in general, but humidity can affect [GOM] at high ozone levels. On the left, we plotted O3 versus PBM colored by H2O concentration. There is generally positive correlation btw PBM & ozone. Humidity also affects [PBM] at high [O3].

## Slide 10
Correlation of Hg with SO2 and CO
Positive correlation btw GEM and CO, esp. at high levels – biomass burning?
Generally positive correlation btw GOM and SO2 – power plant influence
No significant correlation btw SO2 and GEM/PBM or btw CO and GOM/PBM
Notes: Let’s also look at the correlation of Hg with SO2 and CO for GEM, GOM and PBM. SO2 can be considered as a tracer for plumes from coal-fired power plants and CO is s tracer for vehicle exhaust or biomass burning. There seems to have some positive correlation between GEM and CO, especially at high CO levels that most likely due to bios mass burning. But not significant correlation between SO2 and GEM. For GOM, although scatter, there is positive correlation between GOM and SO2. No significant correlation between PBM and SO2 or between PBM and CO.

## Slide 11
HYSPLIT Trajectory Frequency Analysis -- GEM
HYSPLIT runs
  NAM 12 km met data
  5-day back trajectories
  Only use trajectory endpoints within the PBL
Difference between the normalized percent of trajectory endpoints between the top 10% and bottom 10% of GEM concentrations.
Positive numbers (reds) indicate that grid cells (0.1˚x0.1˚) were more likely to be encountered during high GEM concentration events.
Notes: We ran HYSPLIT to look at 5-day back trajectories. NAM 12 km meteorological data were used. We only consider trajectory endpoints within the mixed layer. Here is the frequency analysis for GEM. The colored dots show the difference between the normalized percent of trajectory endpoints between the top 10% and bottom 10% of GEM concentrations. The positive numbers (warm colors) indicate that grid cells (0.1˚x0.1˚) were more likely to be encountered during high GEM concentration events. To our surprise, this suggests that medium high GEM concentrations were mostly observed in air flow from Gulf of Mexico, suggesting the Gulf is be a significant Hg source for this receptor.

## Slide 12
HYSPLIT Trajectory Frequency Analysis -- GOM
Difference between the normalized percent of trajectory endpoints between the top 10% and bottom 31% of GOM concentrations.
Positive numbers (reds) indicate that grid squares (0.1˚x0.1˚) were more likely to be encountered during high GOM concentration events.
Notes: Here is the trajectory frequency analysis for GOM. Again, the positive numbers (warm colors) indicate that grid cells (0.1˚x0.1˚) were more likely to be encountered during high GOM concentration events. High GOM concentrations were more likely to be observed in the continental air flow.

## Slide 13
HYSPLIT Trajectory Frequency Analysis -- PBM
Difference between the normalized percent of trajectory endpoints between the top 10% and bottom 13% of PBM concentrations.
Positive numbers (reds) indicate that grid squares (0.1˚x0.1˚) were more likely to be encountered during high PBM concentration events.
Notes: Here is the trajectory frequency analysis for PBM. Again, the positive numbers (warm colors) indicate that grid cells (0.1˚x0.1˚) were more likely to be encountered during high PBM concentration events. High PBM concentrations were more likely to be observed in the continental air flow.

## Slide 14
Summary
12 years of continuous measurements of atmospheric mercury species at the Grand Bay site in Mississippi.
GEM: a slight decreasing trend of -0.009 ng yr-1, (0.5% yr-1) with the minimum in fall and in the early morning and higher during mid-day.
GOM: a slight decreasing trend of -0.36 pg m-3 yr-1. higher in spring/summer and peak in mid-afternoon.
PBM: a increasing trend of +0.18 pg m-3 yr-1, higher in winter/spring and peak in the mid-day.
General correlation between GOM/PBM and O3 and between GEM and CO.
Back trajectory frequency analysis suggests potential source-receptor relationships, but the relationships are complex.
Notes: In summary we have collected 12 years of atmospheric Hg data at the Grand Bay site in Mississippi. We observed a slight decreasing in GEM and GOM, but a slight increase in PBM and mercury wet deposition. We found general correlation between GOM/PBM and O3 and between GEM and CO. Back trajectory frequency analysis suggests potential source-receptor relationships, but these relationships are varied and complex.

## Slide 15
Acknowledgements
NOAA Grand Bay NERR and Mississippi Department of Marine Resources for cooperation in facilitating the monitoring site.
NOAA for funding.
University Maryland’s Cooperative Institute for Satellite Earth System Studies (CISESS) funded under a NOAA Cooperative Agreement.
National Atmospheric Deposition Program
Notes: With that, I thank you for your attention.

## Slide 18: Extra slides

## Slide 19
Outline
Monitoring site
Hg Measurements
  inter-annual variations – trends
  Seasonal variations
  Diurnal variations
Correlation with trace gases and met
Back trajectory frequency analysis to look into the source-receptor correlation
Notes: I will show you some info on the monitoring site, Hg Measurements, including inter-annual variations – trends, Seasonal variations, and Diurnal variations. We also looked at the correlation between observed Hg and trace gases and metrological parameters. We also used HYSPLIT for a back trajectory frequency analysis to look into the source-receptor correlation at this site.

## Slide 20
Wind Rose Plots for Significantly Elevated Hg
Highest [GEM] from north
Highest [PBM] from north
Highest [GOM] from S/SW and N/NE/E
[GEM] (ng m-3)
log10[GOM]
log10[PBM]
N=55
N=551
N=391
Notes: Those significantly elevated Hg levels are mainly associated to anthropogenic Hg emissions.

## Slide 21
Wind Climatology (2007-2017) at the Grand Bay Site

## Slide 22
Correlation of GEM/GOM/PBM with Wind Direction

## Slide 23
Correlation of GOM and PBM with Wind Speed

## Slide 24
Correlation of GEM/GOM/PBM with CO

## Slide 25
Correlation of GEM/GOM/PBM with SO2 and NOy
No correlation between GEM and SO2
GOM: max. in mid-afternoon, low at night
PBM: max. in mid-day , stays elevated low at night