## Slide 1: Reducing Water Scarcity by Improving Water Productivity
Landon Marston, Ph.D., P.E.
Assistant Professor
Kansas State University, Civil Engineering
Co-Authors: Gambhir Lamsal, Zach Ancona, Peter Caldwell, Brian Richter, Richard Rushforth, Ben Ruddell, & Kyle Davis
Abstract ID: EGU2020-12550
May 5, 2020
Notes: https://cmgajcbuzz.files.wordpress.com/2015/07/droughtfi.jpg (drought sign)

## Slide 2: Water managers in 4 out of 5 states expect water shortages within their state by 2023.
Mekonnen & Hoekstra, 2016

## Slide 3: How can water scarcity be addressed?
supply augmentation
demand management
Notes: Increasing water supplies through large infrastructure projects (e.g., dams and canals) has been the primary way society has dealt with an inability to meet all water demands.

## Slide 4: How can water scarcity be addressed?
supply augmentation
demand management
Notes: However, as these large infrastructure projects become more physically, economically, or socially intractable, the scales are beginning to tip in favor of demand management strategies to ensure available water supplies can meet all water demands.

## Slide 5: What if all water users adjusted their water use to match their industry benchmark level?
BENCHMARK
$
$
Water savings
$
How much water could be saved and where?
Notes: Benchmarking: If all industries and crop production improved their water use efficiency to that of the X% most efficient within their sector (and in their region!), how much water could be saved across the US economy (and in each region)? What industries and locations offer the greatest water savings, and the greatest savings in proportion to reducing water stress?

## Slide 6: This work relies on a rich and high-resolution dataset of human water use in the U.S.
Useful resource for
  water management and modeling
  environmental LCA
  WF assessments
  benchmarking
Landon Marston ltmarston@ksu.edu
Marston, L., Ao, Y., Konar, M., Mekonnen, M. M., & Hoekstra, A. Y. (2018). High-Resolution Water Footprints of Production of the United States. Water Resources Research, 1–29. https://doi.org/10.1002/2017WR021923
Publication
Dataset
Data available at:
http://waterfootprint.org

## Slide 7
National average water intensity
Marston et al, 2018 WRR
Water productivity varies significantly between and within economic sectors.
Water Intensity [m3/$1000]
Notes: Crop sectors require much more water to produce a $1 worth of goods than other economic sectors.

## Slide 8: Expectations of reasonable water consumption were constrained based on current water utilization rates.
BM25 Scenario
BM10 Scenario
BM50 Scenario
Based on similar production processes and comparable conditions.
# of Water Users
Water Productivity
Notes: Other factors, such as technology, water pricing, water rights, infrastructure, and policy, have all been demonstrated to influence water use and productivity.
Unlike climate and other environmental conditions, these are all human decision points impacting water use.
We identify instances of when these human interventions influencing water consumption have led to more efficient water utilization.
Within each climate region and for each industry, we determine the production areas that use water most efficiently. We determine the median blue water consumption per unit of production, as well as the most efficient quartile and most efficient decile for each industry. These are set as water productivity benchmarks and denoted as BM50, BM25, and BM10, respectively.
Potential Water Savings
Within each climatic region, an industry’s blue water footprint was set at the benchmark level for any area utilizing water less efficiently than it’s industrial benchmark.
Potential water savings is the difference between current water consumption and water consumption when all users productivity is equal to or better than their benchmark.

## Slide 9
Where and how much water would be made available for other uses?
Notes: The greatest water saving potential is in watersheds experiencing some of the greatest water scarcity.

## Slide 10: Water savings can have significant impacts on surface water availability in the over-appropriated Colorado Basin.
Lake Powell
Lake Mead
BM25 Scenario
BM50 Scenario
BM10 Scenario
4.8%
10.0%
13.9%
4.1%
8.6%
11.9%
Powell
Mead
Notes: Lake Mead and Lake Powell are critical for many cities and farms throughout the region that depend on these reservoirs to meet their water supply. These reservoirs have experienced record lows as historic droughts, coupled with increasing demands, have pushed them to their limits. Any additional water can be extremely valuable.

## Slide 11: In the Snake River, reasonable improvements in water productivity can augment summer streamflow by as much as 25%.

## Slide 12: The greatest water savings can be achieved in the agriculture sector.
Central
East North Central
Northeast
Northwest
South
Southeast
Southwest
West
West North Central
Water Savings (km3/yr)
7
5
4
3
2
1
0
6
BM25
BM25
BM10
BM50
Notes: Potential crop water savings for BM10, BM25, and BM50 are aggregated to NOAA climatic regions. A 31% reduction in blue water consumption can be achieved if all farmers utilize water as efficiently as the top decile (BM10) of irrigators and 9% savings is obtainable at BM50. The greatest savings occur in the South. Nearly half of potential crop water savings are from just two crops: corn and alfalfa, which are primarily used for animal feed and biofuel.

## Slide 13
93% of sectors use more water through their supply chains than they consume directly.
BM25 Scenario
Notes: The total direct and indirect water requirements throughout a product’s supply chain were calculated using an environmentally extended version of the Leontief Input-Output model. The agricultural sector can achieve greater water savings than all other sectors combined. The manufacturing sector has the greatest indirect water savings due to its reliance on water intensive commodities as inputs to production.

## Slide 14: In summary, there is still significant water savings to be achieved!
Areas facing water stress also show some of the greatest potential for water savings.
Most industries can save more water by working with their suppliers to reduce their water use than they can save directly by making their own operations more water efficient.
Future research is needed to explore the inherent tradeoffs involved in improved water utilization, such as potential increases in energy or fertilizer consumption which may lead to increased grey water and carbon footprints.
Notes: We set water use benchmarks for each industry based on water-use efficiency levels achieved by others in the industry facing similar constraints. In doing so, we highlight specific industries and locations in the United States that could significantly reduce their water footprint by utilizing existing water management strategies and technologies.
Over 80% of all potential water savings occur in the crop sector, with half of those savings attributable to corn and alfalfa.

## Slide 15: Marston Research Group
Exploring the interactions between water and society
Questions?
ltmarston@ksu.edu
http://marstonresearchgroup.com/
@LandonMarston