## Slide 1: NOOS-Drift An innovative operational transnational multi-model ensemble system to assess ocean drift forecast accuracy
S. Legrand1, K.F. Dagestad2, P. Daniel3, M. Kapel1 and S. Orsi1

## Slide 2: Outline
Introduction
How does it work? General principles
Multi-Model Ensemble analysis strategy
Conclusion

## Slide 3: Drift models, key tools in the daily management of marine activities at national levels
Drift models provide key information in support of maritime safety, coastal and marine environment monitoring or marine resources management
Every country surrounding the North West European Continental Shelf operates at least one national drift trajectory forecast service.
These services run their state-of-the-art modelling system, often developed in-house.
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions
As a consequence, all these services are similar but different
=> So far lack of collaboration and integration between countries

## Slide 4: Similar but different models may lead to significantly different forecast results
Differences/uncertainties can be sorted in 3 classes:
Differences /uncertainties in drift models implementation such as ≠ resolved processes, ≠ parametrizations choices or ≠ calibration coefficients
Differences/uncertainties in met-ocean forcing such as ≠ in time-space resolution ≠ resolved dynamical processes (e.g. tide) errors in dynamical features location and intensity
Uncertainties inherent to dynamical systems theory such as branching effects
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions

## Slide 5: Similar but different models may lead to significantly different forecast results
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions

## Slide 6
Shipping Assistance Division
Although, over the years, national users gained trust in their national drift model predictions, they keep challenging modelers, continuously asking:
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions
« How accurate and reliable are your drift trajectory forecast? »

## Slide 7
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions
« How accurate and reliable are your drift trajectory forecast? »
Analysing the spread of a multi-model ensemble forecast system should answer this challenge.
Several NOOS members operate national drift services.
Let’s federate them and develop a transnational multi-model ensemble system for drift trajectory and call it NOOS-Drift!
NOOS members from Belgium, France and Norway are volunteer to develop the prototype. #StrongerTogether
> http://noos.eurogoos.eu/ > Community Products > NOOS-Drift

## Slide 8: Key specifications of the NOOS-Drift service:
Running on demand the same drift simulation request in different national centres; results must be available within 15’-30’ after submission
Thanks to the ensemble spread, providing quick and easy way to intercompare different model trajectories results and identify possible outliers
Providing a straightforward visualization of the forecast uncertainty
Providing a straightforward identification of areas at risk
Making possible the integration of NOOS-Drift results in users’ systems.
Making the system as automated and robust as possible
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions
NOOS-Drift is in essence a back-office service:
It is not intended to replace or shortcut national services: National services remain the primary point of contact for their national users
A fine analysis of NOOS-Drift ensemble spread requires advanced knowledge about the drift models and their met-ocean forcing

## Slide 9
NOOS-Drift system is based on a distributed system made of
A web application allowing users to request a simulation, visualize or download results;
A series of computational nodes hosted by the participating national centers;
A central server managing the execution of a simulation request, hosting the simulation results and runs the multi-models ensemble analysis
A fit-for-purpose secure communication system based on python/Django enforces a smooth dialog between the different components of the service.
How does it work?
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions
https://github.com/rbins-swap-team/NoosDrift

## Slide 10
1. Service request
The central server collects the incoming service request.
Users can request a new simulation by filling in a web form with
General description of the simulation (start time, duration, forward or backward in time)
Drifter characteristics (oil or objects adrift)
Release scenario / initial conditions
Model set-up
Data of the web form are converted into a JSON object
and then sent to the central server
In order to automate simulations, connected systems may also directly submit a JSON object to the central server
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions

## Slide 11
Web access
Central server
RBINS – MFC
Oserit
Meteorologisk institutt
OpenDrift
Meteo France
MOTHY
2. Service request dispatched
The central server validates the JSON object
and dispatches it towards the calculation centers.
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions

## Slide 12
3. Distributed computation
Each model computes its drift forecast and formats its results into a netCDF-CF file
Each center must run simulations for at least two met-ocean forcing sets:
The met-ocean forcing made of ECMWF wind forecast and CMEMS NWS ocean physics forecast. This first set of forcing covers the whole NWS area.
The met-ocean forcing they would use for their national users. In general, this second set of forcing has a higher spatial resolution and better resolves geographical features locally influencing hydrodynamics (estuary, fjords, small islands, sandbanks, dredged channels…). However, these forcing does not always cover the whole NWS area.
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions

## Slide 13
Web access
Central server
RBINS – MFC
Oserit
Meteorologisk institutt
OpenDrift
Meteo France
MOTHY
4. Forecasts collection
The central server collects the forecasts of the drift models.
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions

## Slide 14
Web access
Central server
RBINS – MFC
Oserit
Meteorologisk institutt
OpenDrift
Meteo France
MOTHY
5. Ensemble Analysis
The central server performs the MME analysis of the forecasts. This step also prepares the GeoJSON objects to be displayed on the web applications
https://github.com/knutfrode/noosdrift
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions

## Slide 15
6. Results distribution
All users can visualize and download simulations results.
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions

## Slide 16: Multi-model ensemble analysis
Let’s assume we have an ensemble of N drift simulations of the same event.
The objectives of the MME analysis is
to intercompare different model trajectories;
to identify possible outliers or equivalently identify simulations with similar behaviour;
to quantify forecast uncertainty;
to identify areas at risk
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions

## Slide 17
At each time step, each particles cloud is projected onto an ellipse.
Intuitively, the drift forecast uncertainty is related to the spread of the ellipses.
A good candidate metric is the area of the smallest disk that encompasses all these ellipses (in red).
Good case
Release location
Center of mass / member
Center of mass of all members
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions

## Slide 18
Outlier
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions
However this disk can quickly become very large, especially in case of outliers or branching trajectories.

## Slide 19
Outlier
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions
In that case, one would like to subdivide the ensemble into 2 clusters.

## Slide 20
Outlier
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions
The clustering is made from a decision tree that minimizes the number of clusters under constraints on the distance between ellipses and angles with respect to the release location.

## Slide 21: NOOS-Drift MME analyses implements this intuitive strategy
  Clustering “Identifying potential outliers”
  Likely impacted areas per cluster (mass centers and radius)
  Risk map (weighted sums of the impacted areas)
1. Introduction | 2. General principle | 3. MME strategy | 4. Conclusions
https://github.com/knutfrode/noosdrift

## Slide 22: Conclusion NOOS-Drift = A transnational multi-models ensemble system to assess drift forecast accuracy in the NWS area
A MME-analysis tool, prototype allowing many future developments & improvements
Standardisation of model outputs based on netCDF-CF, JSON (metadata) and GeoJSON (MME analysis)
Secure and efficient communication system minimizing latency inherent to distributed system (python-Django framework)
Ready to welcome new users and model service providers!