## Slide 1: EGU2020-12814: The joint application of digital modeling and field soil survey data for improvement of the accuracy in soil erosion mapping
Zhidkin Andrey, Mikhail Komissarov, Evgeny Zazdravnykh
zhidkin.ap@mail.ru
Lomonosov Moscow State University
Faculty of Geography
V.V. Dokuchaev
Soil Science Institute
Ufa Institute of Biology UFRC, Russian Academy of Science,
Federal state budgetary institution “Center of agrochemical service “Belgorod”

## Slide 2: Chapters
Erosion and soil cover.
The established practice of mapping of eroded soils in Russia.
The proposing of “New” method.
The results in applying of “New” method in different study sites.

## Slide 3
I
Erosion and
soil cover

## Slide 4
Participation of different soil patterns
I. Erosion and soil cover
Soil degradation as a result of erosion occurs locally in the form of individual small-sized areas

## Slide 5
Erosion rates
t * ha-1 * year-1
% of eroded soils
Plot | slope degree | slope length, m | WaTEM/SEDEM |  | % of eroded soils by field data
 |  |  | t * ha-1 * year-1 | cm/50 years | 
II | 2 | 280 | -6.4 | 3.2 | non
III | 4 | 430 | -14.4 | 7.2 | 10
IV | 5 | 730 | -29.7 | 14.7 | 59
V | 6 | 880 | -42.4 | 21.0 | 60
Erosion of soil cover patterns
I. Erosion and soil cover
<100%

## Slide 6
II
The established practice of mapping of eroded soils in Russia

## Slide 7: The established practice of mapping of eroded soils in Russia
II. The established practice of mapping of eroded soils in Russia

## Slide 8
The established practice of mapping of eroded soils
in Russia
Field work
Satellite image
Topographic map
Soil map
Map of degree of erosional degradation
Land use and agro-technology
categories

## Slide 9: The determination of a number of soil profiles at the study place
The established practice of mapping of eroded soils
in Russia
Field work
Satellite image
Topographic map
Map scale | The complexity of land |  |  |  | 
 | I | II | III | IV | V
 | The number of hectares per one soil profile |  |  |  | 
1 : 2 000 | 3 | 2 | 1.5 | 1 | 0.5
1 : 5 000 | 7 | 5 | 4 | 3 | 2
1 : 10 000 | 25 | 20 | 18 | 15 | 10
1 : 25 000 | 80 | 65 | 50 | 40 | 25
1 : 50 000 | 150 | 130 | 110 | 80 | 50
The ratio of full soil profiles, half-profiles and small soil pits
1:2:7 or 1:4:5

## Slide 10: The fragment of soil degradation map due to erosion
Approximate contours. Displays only the dominant categories of soil degradation.
The established practice of mapping of eroded soils
in Russia

## Slide 11: Map of soil degradation due to erosion
II. The established practice of mapping of eroded soils in Russia
The degree of soil degradation
Caused by erosion
The criteria (which are used in the main slopes)

## Slide 12: The established criteria in division of soils by the degree of degradation due to erosion
Kozmenko, 1948 | 
Category of soils by degree of erosion | Absence (washed out) of humus horizons А+В, %
Weak | <10
Medium | 10-30
Strong | 30-50
Very strong | >50
Sobolev, 1960, 1961 | 
Category of soils by degree of erosion | Absence (washed out) of horizons
Weak | <0.5 of А horison
Medium | 0.5-1 of А horison
Strong | part of В horison
Very strong | total А + В
Surmach, 1954, 1956 | 
Category of soils by degree of erosion | Absence (washed out) of humus horizons А+В, %
Weak | <30
Medium | 30-60
Strong | 60-80
Very strong | 80-100
Excessively (or completely) washed away | part of В horison (total А + В)
The different classifications were used in various times and regions of Russia.

## Slide 13: Disadvantages
The “Expert” principle with a high degree of subjectivity.
Approximate contours. Displays only the dominant categories of soil degradation.
Labor intensity (before the use of GIS, more than 2 people drew maps for several months; and even now using GIS, the drawing of soil contours and the soil erosion map performs manually).
Poorly defined principles of design solutions for reducing soil erosion.
II. The established practice of mapping of eroded soils in Russia

## Slide 14
III
The proposing of “New” method

## Slide 15: Methods: common review
Field work and creation a database of soil properties (field degree of erosion).
Calculation of soil erosion rates (by WaTEM/SEDEM).
Identification of statistical dependence between share of soils with different degree of erosional degradation and erosion rates.
Creation maps of equity share of soils of different degree of erosional degradation.
Creation map of soil combinations by the degree of erosional degradation.
Verification.
III. The proposing of “New” method

## Slide 16: Methods: common review
Field work and creation a database of soil properties (field degree of erosion).
Calculation of soil erosion rates (by WaTEM/SEDEM).
Identification of statistical dependence between share of soils with different degree of erosional degradation and erosion rates.
Creation maps of equity share of soils of different degree of erosional degradation.
Creation map of soil combinations by the degree of erosional degradation.
Verification.
III. The proposing of “New” method

## Slide 17: Methods: common review
Field work and creation a database of soil properties (field degree of erosion).
Calculation of soil erosion rates (by WaTEM/SEDEM).
Identification of statistical dependence between share of soils with different degree of erosional degradation and erosion rates.
Creation maps of equity share of soils with different degree of erosion.
Creation map of soil combinations by the degree of erosion.
Verification.
III. The proposing of “New” method

## Slide 18
Dependence between share of soils with different degree of erosional degradation and rates of erosion
III. The proposing of “New” method

## Slide 19: Methods: common review
Field work and creation a database of soil properties (field degree of erosion).
Calculation of soil erosion rates (by WaTEM/SEDEM).
Identification of statistical dependence between share of soils with different degree of erosional degradation and erosion rates.
Creation maps of equity share of soils with different degree of erosional degradation.
Creation map of soil combinations by the degree of erosional degradation.
Verification.
III. The proposing of “New” method

## Slide 20
Proportion of non eroded soils in pixels
Proportion of weakly eroded soils in pixel
Proportion of medium eroded soils in pixel
Maps of Equity share of soils of different degree of erosional degradation
III. The proposing of “New” method

## Slide 21: Methods: common review
Field work and creation of database of soil properties (field degree of erosion).
Calculation of soil erosion rates (by WaTEM/SEDEM).
Identification of statistical dependence between share of soils with different degree of erosional degradation and erosion rates.
Creation maps of equity share of soils with different degree of erosional degradation.
Creation map of soil combinations by the degree of erosional degradation.
Verification.
III. The proposing of “New” method

## Slide 22
Map of soil combinations
by the degree of erosional degradation
E0 – non eroded soils
E1 – weakly eroded soils
E2 – medium eroded soils
III. The proposing of “New” method

## Slide 23: Methods: common review
Field work and creation of database of soil properties (field degree of erosion).
Calculation of soil erosion rates (by WaTEM/SEDEM).
Identification of statistical dependence between share of soils with different degree of erosional degradation and erosion rates.
Creation maps of equity share of soils of different degree of erosional degradation.
Creation map of soil combinations by the degree of erosional degradation.
Verification.
III. The proposing of “New” method

## Slide 24: Advantages of this method
Formalized representative principles of mapping.
Low labor and high speed of cartographic works.
The possibilities of studying the territory in different scales of space and time.
Possibilities of detailed design of anti-erosion measures, including the territorial planning of land management.
The joint application of digital modeling and field soil survey data

## Slide 25
IV
The results in applying of “New” method in different study sites

## Slide 26: The location of 4 studied sites
IV. The results in applying of “New” method in different study sites

## Slide 27: Kursk and Belgorod studied sites
~1000 soil pits
~670 soil pits

## Slide 28: Kursk site
1) insignificantly-eroded soils (soil losses up to 3 t·ha-1·year-1); 2) slightly-eroded (3–10 t·ha-1·year-1); 3) medium-eroded (10–20 t·ha-1·year-1); 4) highly-eroded (20–40 t·ha-1·year-1); 5) severely-eroded (over 40 t·ha-1·year-1); 6) warpland (accumulation of 3–10 t·ha-1·year-1); 7) virgin lands of the Central Black Earth Re-serve; 8) pastures, hayfields, settlement lands.
IV. The results in applying of “New” method in different study sites

## Slide 29
Traditional method
Fragment of map of soil combinations by the degree of erosion
Meadow chernozem (MCh)
Typical chernozem (TCh)
Calcareous chernozem (CCh)
Leached chernozem (LCh)
MChE1
TChE1
CChE1
LChE1
E0 | 1
 | 2
E0-E1 | 3
E1 | 4
E2 | 5
Verification by detailed studies of key small watersheds
IV. The results in applying of “New” method in different study sites

## Slide 30
Verification by detailed studies of key small watersheds
The proportion of eroded soils according to modeling data
The proportion of eroded soils according to detailed field data
*See details in:
Kozlov D. N. , Zhidkin A. P. , Lozbenev N. I. (2019) Digital mapping of soil cover eroded patterns on the bassis of soil erosion simulation model (northern forest-steppe of the Central Russian Upland). Dokuchaev Soil Bulletin.100. 5-35
IV. The results in applying of “New” method in different study sites

## Slide 31: Belgorod site
1 - non- and slightly eroded with a share> 75%;
2 - medium and strongly eroded> 50%, middle eroded> strongly eroded;
3 - medium and strongly eroded> 50%, strongly eroded> middle eroded.
IV. The results in applying of “New” method in different study sites

## Slide 32: The total area (in thousand ha) of eroded soils according to different mapping methods
Degree of soil degradation | Traditional visual expert method | Digital mapping | 
 | Dominant category | Dominant category | Taking into account the proportion of eroded soils in each pixel
Non- and slightly eroded | 65.2 | 62.1 | 55.7
Medium eroded | 2.5 | 4.3 | 11.3
Strongly eroded | 0.0 | 0.9 | 0.3
*See details in:
Zhidkin A.P., Smirnova M.A. , Gennadiev A.N. , Lukin S.V. , Zazdravnykh E.A. , Lozbenev N.I. (2020) Digital modeling of the structure and erosion degree of soil cover (Prokhorov district of Belgorod region) // Eurasian soil science (on review)
IV. The results in applying of “New” method in different study sites

## Slide 33
Moscow site
1797 year
1861 year
1871 year
1931 year
1954 year
1985 year
2000 year
2018 year
*See details in EGU2020-969
Land Use History - Leading Factor in the Territory
IV. The results in applying of “New” method in different study sites

## Slide 34
Moscow site
*See details in EGU2020-969
Land Use History - Leading Fator in the Territory
non-eroded
very slightly eroded
slightly eroded
medium and strongly eroded
~1300 soil pits
IV. The results in applying of “New” method in different study sites

## Slide 35
SRTM
On the basis of topographic map
1:10 000
On the basis of geodetic survey 1:500
Ufa site
Paleo microrelief greatly reduces the accuracy of digital modeling of soil erosion
Soil map
*See details in:
Zhidkin A., Komissarov M. 2020. Erosion and accumulation microstructures of soil cover in the forest-steppe zone of the Cis-Urals, the republic of Bashkortostan. Vestnik BSAU. № 1. 12-20 (in Russian)
Soil erosion rates, calculated by WaTEM/SEDEM with different DEM
IV. The results in applying of “New” method in different study sites

## Slide 36
Thank you for your attention!
I regret that currently, we could not see each other. Lets meet in EGU 2021!
I will be glad to answer on any questions.
Dr. Andrey Zhidkin
zhidkin.ap@mail.ru