## Slide 1: Sediment sorting in tidal sand wave fields: the internal structure revealed? A model study with Delft3D
Johan Damveld, Bas Borsje, Pieter Roos, and Suzanne Hulscher
Water Engineering & Management, University of Twente, Enschede, Netherlands
EGU2020-13679: Damveld et al.

## Slide 2
Tidal sand waves
Wavelength:
Wave height:
Migration rate:
Interfere with offshore engineering (e.g. wind farms, cables)
Current wind farms
Future wind farms
Sediment sorting over sand waves
General trend shows a coarsening of the crests
Also field sites with finer crests
No information on the internal structure
Netherlands continental shelf
EGU2020-13679: Damveld et al.

## Slide 3: Basic model set-up: Delft3D Flow
Hydrodynamics: 2DV Navier-Stokes + flow continuity
Sediment transport: bed load + slope-induced transport + suspended load
Waterdepth: 25 m
0.65 m/s
0.05 m/s
Mean grain size: 0.35 mm
EGU2020-13679: Damveld et al.

## Slide 4: Model set-up: sediment sorting
Bed stratification:
Active/transport layer
Up to 60 under layers
Base layer
All layers initially well-mixed
: grain size of sediment class
: mass fraction of sediment class
Probability density function of sediment mixture
4 classes
Phi-scale ( 
: sortedness of sediment mixture
Flatter curve  higher sortedness
EGU2020-13679: Damveld et al.

## Slide 5: Sediment sorting: asymmetrical tidal forcing
Mean grain size
Play me
EGU2020-13679: Damveld et al.

## Slide 6: Sediment sorting: model observations
Inner structure revealed: same pattern as lee side surface
Fine sediments get re-entrained due to migration
Sedimentation lee side
Upper: coarse
Lower: finer
Coarser trough due to different motion thresholds among fractions
EGU2020-13679: Damveld et al.

## Slide 7: Sediment sorting: influence on wave height
: sortedness
(=0  uniform sample, perfectly sorted)
Grey dots: North Sea observations
: sand wave height
Increasingly poorly-sorted mixtures lead to lower sand wave heights
: mean grain size
EGU2020-13679: Damveld et al.

## Slide 8: Utilisation: dredging example
Play me
EGU2020-13679: Damveld et al.

## Slide 9: Discussion and conclusions
Including sediment sorting leads to lower sand wave heights
  Model predictions fall in range of North Sea sand waves
Surficial sorting pattern generally agrees with field observations
Internal sediment structure exposed
  Lack of field evidence for validation  any suggestions from EGU community?
This work is undergoing peer-review, so you will be able to read more soon!
EGU2020-13679: Damveld et al.