## Slide 1
Olga Borisova
Institute of Geography, Russian Academy of Sciences
Aleksey Sidorchuk
Moscow State University
The main types of river channel bedforms movement

## Slide 2
The examples are from:
Niger River
Volga River
Vychegda River
Terek River
Ob River
Yenisei River
Lena River

## Slide 3
The main characteristics of the river channel bedforms
Hierarchical structure
Stochasticity of morphology and dynamics
Two main modes of movement: active and passive

## Slide 4
General terms
All dune-like alluvial features in the river channel – sand waves
(although some are not of sand but of gravel, cobbles and boulders)
The smallest (first order) sand waves with wavelength and amplitude
changing with flow depth and velocity – megaripples
Second order sand waves often, but not necessarily, covered by megaripples – dunes_1
Third order sand waves often covered by dunes_1 and megaripples, but not necessarily – dunes_2
Usually, the larger sand waves in the hierarchy
(mezoforms) are called bars
They also can be of several orders and are
usually covered by smaller bedforms
(microforms)

## Slide 5
The lower Volga River

## Slide 6
The lower Volga River
Hierarchical structure
Dunes of the first order (dunes_1) on the dunes of second order (dunes_2) in side-scan sonar image
Bedforms in the river channel are usually organised into hierarchical complexes, where smaller bedforms move along the surface of larger ones.

## Slide 7
Dunes_1 Dunes_2 Bars_1
Probability density functions
Sand waves wavelength
Sand waves amplitude
Stochasticity of morphology
The lower Volga River

## Slide 8
Photo by J. de Kramer
The lower Volga River

## Slide 9
Stochasticity of morphology
The lower Yenisei River
Wavelenth, m
Probability density function
Spectral density function
Bars_1
Dunes_1
Dunes_2
Wavelenth, m

## Slide 10
The lower Yenisei River
Dunes_1 Dunes_2
Probability density functions
Sand waves wavelength
Sand waves amplitude
Stochasticity of morphology

## Slide 11
The Lena River
Observation
site

## Slide 12
Megaripple amplitude h and wavelength L probability density functions at different specific discharges Ud m2/s
The Lena River
Stochasticity of morphology
L m
h m
N

## Slide 13
The Ob’ River
Observation
site

## Slide 14
15:15
16:45
16:15
15:45
18:50
19:15
19:45
20:15
Orsko-Borsky
shallows,
August 7, 1993
50 m
The Ob’ River
Active megaripples on passive dunes
Two main modes of movement: active and passive
The celerity of passive dunes is 0.2-0.4 m/hour; that of megaripples 1.5 m/hour

## Slide 15
Observation
site
The Niger River

## Slide 16
Active bedforms are three-dimensional, symmetrical, with gentle slopes. They move without significant change in shape, since all parts of their surface move at the same speed.
The Niger River near Ajaokuta
23.09-09.10.1978
30 m asl
25 m asl
Two main modes of movement: active and passive
Water level, m asl.
date

## Slide 17
Passive bedforms are two-dimensional, asymmetric, with steep leeward slope. Their tops move faster than theirhollow so that the bedform is skewing.
Two main modes of movement: active and passive
m
The Niger River near Ajaokuta
28.10-23.11.1978
Transformation of active dunes into passive ones
Water level, m asl.
date
Water level, m asl.

## Slide 18
A new generation of active dunes appears on the surface of passive
dunes
Two main modes of movement: active and passive
The Niger River near Ajaokuta
18.01-20.02.1979
Water level, m asl.
date

## Slide 19
The Vychegda River
Observation
site

## Slide 20
Active dunes on the bar
The Vychegda River
Dune wavelength
Dune amplitude
Two main modes of movement: active and passive

## Slide 21
The Vychegda River
Dune celerity by points along the bar, m/hour
Dune celerity by points (detrended)
along the bar, m/hour
Points on the dune
Distance along the bar, m

## Slide 22
Histograms of dune
celerity by points
Detrended dune celerity by points: means and max/min, m/hour, showing a general stability of active dunes shape
Points on the dune
The Vychegda River

## Slide 23
The Terek River
A stable section
of the Terek River
channel
long profile 1
long profile 2

## Slide 26
The flow depth-velocity diagram
with the areas of existence of
active and passive dunes
with active megaripples

## Slide 27
Active dunes_1 celerity C
as the function of flow depth D and velocity U
m/s
Terek River
Niger River
Active megaripples celerity C
as the function of flow depth D
and velocity U
Ob and Lena Rivers
m2/hour
Chart: 
| 1.0449999999999999 | 1.03 | 1.0049999999999999 | 0.99 | 0.94 | 0.93 | 0.92 | 0.91 | 0.9 | 0.9 | 0.88 | 0.84 | 0.82 | 0.81 | 0.77 | 0.74 | 0.72 | 0.72 | 0.69 | 0.65 | 0.61 | 0.55000000000000004 | 0.52249999999999996 | 0.52 | 0.47 | 0.45
 | 3.2557 | 2.6598 | 1.7867 | 1.144 | 3.0382 | 3.2229 | 3.2796 | 1.238 | 1.3241 | 3.2083 | 2.2169 | 3.1139 | 3.2951 | 0.87083 | 1.4167 | 1.4988 | 1.6883 | 1.1255 | 0.43361 | 0.56968 | 0.24792 | 0.16111 | 0.39631 | 0.1125 | 0.46875 | 0.30868
CD=2.8U
3.4
Passive dunes celerity C
as the function of flow depth D
and velocity U
The Niger, Ob and Vychegda Rivers

## Slide 28
The remaining questions
Hierarchical structure of the sand wave system can be found on the majority of large and medium-size rivers, and even in the large experimental flumes. An existence of the megaripple - bar pairs was explained theoretically using the small perturbation method (Sidorchuk, 1996). An existence of the pair megaripple - dune, although it is the most common one, still has no theoretical explanation.
Stochasticity of morphology and dynamics of sand waves, presumably, is caused by the stochastic nature of the river flow turbulence. The typical form of probability density functions for the morphological and dynamic characteristics of the dunes is close to asymmetric gamma-function or lognormal function, although the flow turbulence is described by symmetrical normal distribution. This phenomenon still requires the theoretical explanation
The two main modes of sand waves movement, active and passive, often are not distinguished. An active mode is common for megaripples even during the low water levels, but the active dunes movement can be detected only during the high floods or in rapid flows. With the decrease of water level and flow velocity the active dunes rapidly transform into passive ones. The larger sand waves are usually in the passive mode of movement. This phenomenon requires further investigation and theoretical explanation.

## Slide 29
A few papers
Sidorchuk A. Y. Morphology of dune-like relief in rivers // Water Resources. — 2020. — Vol. 47, no. 1. — P. 65–76
Alekseevskii N. I., Sidorchuk A. Y. Morphology and dynamics of active bed forms in the Terek R. channel // Water Resources. — 2017. — Vol. 44, no. 2. — P. 226–236.
Sidorchuk, A. Evaluating bedload transport rate in a river bed taking into account data on the active and passive bed-forms dynamics // Water Resources. — 2015. — Vol. 42, no. 1. — P. 38–51.
Sidorchuk A.Y. Bed-form dynamics In the Nizhne-sheshurovskii shallows of the Vychegda River// Russian Meteorology and Hydrology— 2000. — no. 4. — P. 62–69.
Sidorchuk A. The structure of river bed relief // Coherent flow structures in open channels. — Wiley Chichester, UK, 1996. — P. 397–421.
Zaitsev A.A., Kirik O.M., Lodina R.V., Sidorchuk A.Yu., Chalov R.S. Channel changes on the Lena River in the transition of confined channel to wide floodplain//Water Resources — 1991 — № 6 — P. 22-30.