## Slide 1: A smoother algorithm with a multiple calibration-constrained null-space Monte Carlo method toward land subsidence prediction with uncertainty analysis
Graduate School of Frontier Sciences, University of Tokyo
Acknowledgement: Council for Science, Technology and Innovation(CSTI), Cross-ministerial Strategic Innovation Promotion Program (SIP), Enhancement of National Resilience against Natural Disasters (Funding agency:NIED)
Masaatsu Aichi
EGU2020-16906
Note: Part of this study has been published in Aichi M. (2020): Land subsidence modelling for decision making on groundwater abstraction under emergency situation. Proc. IAHS, 382, 403–408, 2020
https://doi.org/10.5194/piahs-382-403-2020

## Slide 2: Background: Typical land subsidence behavior in Tokyo
Chart: 
 | -12.35 | -14.67 | -12.3 | -18.73 | -17.55 | -18.62 | -18.11 | -21.81 | -21.35 | -22.53 | -20.99 | -22.94 | -22.69 | -24.18 | -20.99 | -19.86 | -22.48 | -28.6 | -29.78 | -30.24 | -30.45 | -32.4 | -31.94 | -29.83 | -29.37 | -32.35 | -35.07 | -35.54 | -36.26 | -28.55 | -28.19 | -35.07 | -38.26 | -48.49 | -5 | -15 | -18.11 | -20.73 | -17.91 | -14.46 | -17.7 | -27.57 | -27.36 | -18.06 | -16 | -16.21 | -19.29 | -30.14
Hydraulic head [m]
Ground surface elevation [m]
Year
Leveling (@Pile 3377)
Hydraulic head
(@Kameido #1)
Hydraulic head at well construction
(Koto area)
after Endo et al. (2001)

## Slide 3
Background: New problem after groundwater recovery
Buoyancy
GL (m)
0
-10
-20
-30
-40
B4
B3
B2
B1
-50
Ground
Anchor
Weight
Land subsidence
(mm): Kameido
1951
1971
1991
1961
1981
Groundwater level
(m, T.P): Kameido
Koto area Pumping rate
(1000m3/day)
Buoyancy problem (Ueno)
No Data
Construction of Shinkansen express at Ueno station
Construction of Soubu line at Tokyo station
Countermeasures against high groundwater level

## Slide 4: Background: Heterogeneity of the past maximum effective stress
Depth (m, GL)
0
0
100
200
300
Pore pressure, kPa
10
20
30
40
hydrostatic
1983
A history of pore pressure profile
in the aquitard. (Aichi, 2008)
Log (mean effective stress)
Void ratio
1974
(unsaturated)
1977
Holocene
Part of the thick clay was not fully drained
The past maximum effective stress is heterogeneous
Numerical modelling is necessary to reproduce & predict land subsidence

## Slide 5: Research objectives
Highly uncertain modeling is expected in land subsidence simulation
  Heterogeneity of the subsurface formations
  the evolution of the past maximum effective stress under the historical groundwater abstraction
  Observation is limited
→Continuous model calibration and uncertainty analysis as monitoring data is obtained

## Slide 6: Concept & Algorithm
Filter vs Smoother
  Smoother was chosen to follow hysteresis of clay deformation
Resampling strategy
  Every observation time step
  Next model ensemble should be generated near current better models in parameter space
  Null-space Monte Carlo method (Doherty, 2015) was adopted for effective generation (though not Bayesian)
Generating models by Initial guess
Determining the number of the models to be generated from the i-th model based on the likelihood
Generating models by null-space Monte Carlo method
Observed data collection
Future predictions by generated models

## Slide 7: 1D vertical test model and boundary condition
0m
-56m
-35m
Yurakucho
7gouchi
Specified head
condition
Head=0 condition
aquifer
Chart: 
 | -12.35 | -14.67 | -12.3 | -18.73 | -17.55 | -18.62 | -18.11 | -21.81 | -21.35 | -22.53 | -20.99 | -22.94 | -22.69 | -24.18 | -20.99 | -19.86 | -22.48 | -28.6 | -29.78 | -30.24 | -30.45 | -32.4 | -31.94 | -29.83 | -29.37 | -32.35 | -35.07 | -35.54 | -36.26 | -28.55 | -28.19 | -35.07 | -38.26 | -48.49 | -5 | -15 | -18.11 | -20.73 | -17.91 | -14.46 | -17.7 | -27.57 | -27.36 | -18.06 | -16 | -16.21 | -19.29 | -30.14
Hydraulic head [m]
Ground surface elevation [m]
Year
Leveling (@Pile 3377)
Hydraulic head
(@Kameido #1)
Hydraulic head at well construction
(Koto area)
after Endo et al. (2001)

## Slide 8: Land subsidence simulator
（ :Specific storage[1/m],:compression index [-]、ρ:water density[kg/m3], g:gravitaional acieration factor[m/s2]）
Darcy’s law & Mass conservation of groundwater
Modified Cam-Clay model with linear elasticity

## Slide 9: Parameter space
Physical properties | Nanagouchi F. |  |  | Yurakucho F. |  | 
 | initial guess | lower limit | upper limit | initial guess | lower limit | upper limit
Hydraulic conductivity [m/day] |  |  |  |  |  | 
Uniaxial drained bulk modulus [GPa] |  |  |  |  |  | 
Compression index [-] |  |  |  |  |  | 
Density of solid [103kg/m3] |  |  |  |  |  | 
Void ratio in virgin compression by 1 MPa of effective stress [-] |  |  |  |  |  | 
The past maximum elevation of the top of the formation [m] |  |  |  |  |  | 
Physical properties | Nanagouchi F. |  |  | Yurakucho F. |  | 
 | initial guess | lower limit | upper limit | initial guess | lower limit | upper limit
Hydraulic conductivity [m/day] |  |  |  |  |  | 
Uniaxial drained bulk modulus [GPa] |  |  |  |  |  | 
Compression index [-] |  |  |  |  |  | 
Density of solid [103kg/m3] |  |  |  |  |  | 
Void ratio in virgin compression by 1 MPa of effective stress [-] |  |  |  |  |  | 
The past maximum elevation of the top of the formation [m] |  |  |  |  |  | 

## Slide 10: Test Result
Subsidence [m]
“Prediction”
Learning
“Prediction”
Learning
Subsidence [m]
The convergence of predictive uncertainty was confirmed by the test with the existing hydraulic head/land subsidence monitoring data
Computational load was not learge: Laptop (NEC LAVIE, Intel Core i7-7500U 2.7GHz, 8GB RAM, Windows 10) could conduct 95 year analysis in 3 hours
Total size of ensemble is 50 in this test. Top 5 models are extracted in this figures.

## Slide 11: Parameter range of best 5 models after the calibration
Physical properties | Nanagouchi F. |  |  | Yurakucho F. |  | 
 | best model | lowest value | largest value | best model | lowest value | largest value
Hydraulic conductivity [m/day] |  |  |  |  |  | 
Uniaxial drained bulk modulus [GPa] | .1 |  |  |  |  | 
Compression index [-] |  | .75 |  | 4 | .54 | 
Density of solid [103kg/m3] |  |  |  |  |  | 
Void ratio in virgin compression by 1 MPa of effective stress [-] |  |  |  |  |  | 
The past maximum elevation of the top of the formation [m] |  |  |  | .4 |  | 
Physical properties | Nanagouchi F. |  |  | Yurakucho F. |  | 
 | best model | lowest value | largest value | best model | lowest value | largest value
Hydraulic conductivity [m/day] |  |  |  |  |  | 
Uniaxial drained bulk modulus [GPa] |  |  |  |  |  | 
Compression index [-] |  |  |  |  |  | 
Density of solid [103kg/m3] |  |  |  |  |  | 
Void ratio in virgin compression by 1 MPa of effective stress [-] |  |  |  |  |  | 
The past maximum elevation of the top of the formation [m] |  |  |  |  |  | 
The parameter uncertainty of hydraulic conductivity and compression index was reduced well while that of the other parameters was not because of less sensitivity.

## Slide 12: Conclusion
A numerical scheme for the land subsidence modelling with the visualization of prediction uncertainty based on the Monte Carlo smoother approach with the null-space Monte Carlo method for model resampling.
The proposed scheme demonstrated that it can satisfactory reproduce the existing land subsidence with real time inversion and uncertainty analysis.
Further improvements to include
  the boundary condition uncertainty
  the methodology to find the optimal number of models.

## Slide 13: References
Aichi, M.: Coupled groundwater flow/deformation modelling for predicting land subsidence, In Groundwater management in Asian cities: technology and policy for sustainability, Takizawa S (eds.), 105-124, Springer-Verlag: Tokyo, 2008.
Doherty J.: Calibration and uncertainty analysis for complex environmental models, Watermark Numerical Computing, 2015.
Endo, T., Kawashima, S., and Kawai, M.: Historical review of development of land subsidence and its cessation in Shitamachi Lowland, Tokyo, J Japan Soc Eng Geol, 42,74-87, 2001. (in Japanese)