## Slide 1
Application of hyperspectral remote sensing in the longwave infrared region for assessing the influence of settled desert dust from different origins on several arid soil surfaces
Gila Notesco, Shahar Weksler and Eyal Ben-Dor
Remote Sensing Laboratory, Department of Geography and Human Environment, Porter School of Environment and Earth Science, Tel Aviv University, Israel

## Slide 2
Dust from the desert, through Aeolian processes, is one of the sources that determine the nature of the soil especially in southern Israel .
Most common minerals in soils and desert dust―quartz, clay minerals and carbonates―have fundamental spectral features in the longwave infrared (LWIR, 8–12 µm) region due to the fundamental vibration modes of the silicon–oxygen bond (Si–O) in quartz and clay minerals, and the carbon–oxygen bond (C–O) in carbonates.
Accordingly we assume that:
LWIR hyperspectral remote sensing data can be used to determine soil surface mineralogy and to assess the interaction of the surface with desert dust particles.
Introduction

## Slide 3
April –May
September
Tel-Aviv
The Middle East and dust storm event From Sahara (West)
N

## Slide 4
https://moag.maps.arcgis.com/apps/webappviewer/index.html?id=1fbe80a86d6c4430930d868259d4caf2
The Israel Soil Spectral Library
>2000 Soils Samples
72 Chemical attributes
Aggregate size
Minerology
Chart: Soil Spectra
Soil Attributes
Soil Spectra Files
Sample Location OM Clay Smectite Free Iron Oxides ………
A1 34,5467.67 2.4 % 34% 23% 1.6%
36,654,32

## Slide 5
https://moag.maps.arcgis.com/apps/webappviewer/index.html?id=1fbe80a86d6c4430930d868259d4caf2

## Slide 6
Ground-based hyperspectral LWIR images of soil samples were acquired with Telops’ Hyper-Cam hyperspectral sensor, located at a distance of 2 m from the samples, covering the LWIR spectral region (8.0–11.7 µm) with 122 bands and a spectral resolution of 4 cm-1. The emissivity spectrum of each pixel was calculated according to:
Lsλ = ελLbλ(T) + (1 − ελ)Ldλ
where ελLbλ(T) is the surface emission at wavelength λ with ε as the surface emissivity, and Lb(T) as the radiance from a blackbody at surface temperature T; (1-ελ)Ldλ is the surface reflection of the radiance incident on the surface from the atmosphere at wavelength λ with Ld as the downwelling radiance. with Lb(T) as the fitted tangent blackbody radiation curve, and downwelling radiance (Ld) as the radiance measured from a gold plate.
Soil samples – emissivity spectra
Gold plate
(b)
LWIR image (band 10.62 μm)
RGB image

## Slide 7
Emissivity spectra analysis
The mineral(s)-related emissivity features were used to create spectral indicants to identify the most abundant mineral(s) in each soil sample
a Nε: normalized emissivity value at indicated λ; b ε: emissivity value in the indicated λ range.

## Slide 8
Indicants and indices, based on mineral-related emissivity features, were used to determine the content of quartz (Q), clay minerals (CM), and carbonates (C) in the soil—from more to less abundant minerals.
Indicants and indices
a Nε is the normalized emissivity value at the indicated wavelength (λ); b ε is the emissivity value in the indicated wavelength range.
Most abundant mineral | Spectral indicant
Clay minerals | Nελ = 9.56µma < Nελ = 8.21µm and Nελ = 8.21µm > 0.98
Carbonates | ελ = 8.06-8.12µmb < ελ = 8.21µm and/or Nελ = 11.24µm < 0.995 with Nελ = 8.21µm > 0.98
Quartz | Excluding the above
SQCMI (Soil Quartz Clay Mineral Index) = Nελ = 9.56 µm/(Nελ = 8.21 µm x Nελ = 8.85 µm) |  |  | 
SCI (Soil Carbonate Index) = Nελ = 11.24 µm x Nελ = 10.51 µm/Nελ = 8.85 µm |  |  | 
A higher SQCMI value indicates a higher concentration of quartz relative to clay minerals; a smaller SCI value indicates a higher concentration of carbonates in the sample.
Soil type | Indicant | Relative amount of mineral(s)
Q | SCI < 1.010 | C > CM
 | 1.010 ≤ SCI < 1.020 and SQCMI > 1.020 | C > CM
 | SCI > 1.020 SCI > 1.050, SQCMI > 1.200 | CM > C no C, no CM
CM | Absorption at 8.12 µm and/or SCI < 1.005 | C > Q
C | SQCMI > 1.010 with Nελ = 8.21µm < 0.990 | Q > CM

## Slide 9
Most abundant mineral(s): LWIR spectral-based vs. XRD analysis results
Type of each soil sample according to the most abundant mineral(s): carbonates, clay minerals and quartz; each circle represents a soil sample.
Spectral-based classification (O empty circle) fits the XRD analysis results (● filled circle) in most (90 %) soil samples (where circle’s color is identical) !!!!

## Slide 10
Soil
Dust
Working Locations
N

## Slide 11
Soil samples - emissivity spectra
Gray dashed lines indicate the wavelengths used to create indicants and indices as follow

## Slide 12
Soil sample/type | SQCMI | SCI | Mineralogy (more to less abundant)
1 / Loess | 1.032 | 1.009 | Q C CM
2 / Brown alluvial_1 | 1.007 | 1.011 | CM Q C
3 / Brown alluvial_2 | 1.010 | 1.006 | Q C CM
4 / Brown steppe | 1.003 | 1.005 | CM C Q
5 / Brown desert skeletal | 0.997 | 1.000 | C CM Q
6 / Terra Rossa | 0.956 | 1.018 | CM Q C
Mineralogy of soil samples

## Slide 13
Soil sample\dust | SQCMI | SCI | Mineralogy (more to less abundant)
Loess | 1.032 | 1.009 | Q C CM
Dust_1 | 1.015 | 0.998 | C Q CM
Dust_2 | 1.026 | 1.005 | Q C CM
Dust_3 | 1.125 | 1.072 | Q CM
Dune sand | 1.453 | 1.278 | Q
Dispersed dust mineralogy
Increasing Q,
decreasing C
The effect of dispersed dust on the soil surface
Additional desert loess soils (henceforth dust_2 and dust_3) and dune sand, with different mineral contents, were dispersed on the surface of a loess soil sample.
ΔSQCMI and ΔSCI values, where Δ is the difference between after and before the dust dispersion, were calculated.

## Slide 14
After a first LWIR image was acquired, desert loess soil (henceforth dust_1) was dispersed on the surface of each soil sample. A second LWIR image was acquired; the emissivity spectrum of each soil sample, and then the SQCMI and SCI values of each sample, were recalculated.
Dust dispersion on Soils’ background (small scale )
50g/m2
100g/m2
250mg/m2

## Slide 15
The effect of one selected dispersed dust on the soils surface
(dust_1 C Q CM On 6 soils)
Without dust_1 (empty circles), and covered with 50 g m-2 dust_1 (filled circles); x represents the index values of dust_1.
SQCMI
SCI
The addition of carbonates-rich dust_1 (lowest SCI value) resulted in decreased SCI values, expressing the increase in the amount of carbonates.
Changes in the amount of quartz, relative to clay minerals, were noticed mainly in the clay minerals-rich 6/terra rossa soil (increased SQCMI value, indicating an increase in the relative amount of quartz), and in the quartz-rich 1/loess soil (decreased SQCMI value, indicating a decrease in the relative amount of quartz).
SQCMI
SCI
A higher SQCMI value indicates a higher concentration of quartz relative to clay minerals; a smaller SCI value indicates a higher concentration of carbonates in the sample.

## Slide 16
ΔSQCMI (a) and ΔSCI (b) values resulting from the dispersion of 50 g m-2 (small triangles) and 100 g m-2 (big triangles) of dust_1 (blue), dust_2 (green), dust_3 (orange) and dune sand (red) on the surface of 1/loess soil; x-axis offset for clarity.
The effect of dispersed all dusts on a selected soil surface (1/loess Q C CM )
Loess |  |  | Q C CM
Dust_1 |  |  | C Q CM
Dust_2 |  |  | Q C CM
Dust_3 |  |  | Q CM
Dune sand |  |  | Q
A higher SQCMI value indicates a higher concentration of quartz relative to clay minerals; a lower SCI value indicates a higher concentration of carbonates in the sample.
Q
c

## Slide 17
Regional-scale mineralogical changes
The Hyper-Cam sensor was located at a distance of 3 and 8 m from points A and B, respectively, resulting in a spatial resolution of 0.5 and 1 cm, respectively. Aluminum foil signs (delimiting 1-m2 regions) were placed on the surface.
Field campaigns were conducted in two study areas, consisting of agricultural fields with different soil types. In each area, after a first LWIR image was acquired, desert dust-like materials were dispersed on the surface, and then a second LWIR image was acquired and the emissivity spectrum of each pixel was calculated, resulting in before- and after-dust-dispersion emissivity images. Then, the SQCMI and SCI values of each pixel in each image were calculated resulting in before- and after-dust-dispersion SQCMI and SCI images.
Brown alluvial soil,
mineralogy: Q C CM
●B
●A
Loess soil,
mineralogy: Q CM C
●A
●B
50 g m-2 dust_1 (region 1), 250 g m-2 dust_2 (region 2), 250 g m-2 dust_3 (region 3) and 250 g m-2 dune sand (region 4);
Dust Sources
Loess Q CM C
Alluvial QC CM

## Slide 18
Mineralogical changes resulting from settling of the dust particles – brown alluvial soil
(a) SAM rule map* emphasizing changes on the surface resulting from the dispersion of 50 g m-2 dust_1 (region 1), 250 g m-2 dust_2 (region 2), 250 g m-2 dust_3 (region 3) and 250 g m-2 dune sand (region 4); a larger angle (θ) indicates bigger changes on the surface. Note that the addition of dust_1, with different mineralogy than the brown alluvial soil, is more noticeable than the addition of dust_2, despite the former's smaller amount (50 g m-2 and 250 g m-2, respectively). ΔSQCMI (b) and ΔSCI (c) images; blue color represents ΔSQCMI and ΔSCI ≈ 0, i.e., no mineralogical changes. The nonhomogeneity of θ, ΔSQCMI and ΔSCI values within a region, resulting from the dispersion procedure, emphasizes the sensitivity for detecting local mineralogical changes in the soil surface.
The addition of dust_1 to the surface resulted in negative ΔSCI values, indicating an increase in the amount of carbonates, whereas the addition of dust_3 or dune sand resulted in positive ΔSQCMI and ΔSCI values, indicating an increase in the relative amount of quartz and a decrease in the amount of carbonates, respectively.
*Dividing the after-dust-dispersion emissivity image by the before-dust-dispersion image and applying the SAM algorithm to the resultant divided image, with a unity spectrum as the endmember spectrum (representing “no change” between the two images).
0.003 θ (radians) 0.030
(a) SAM rule map
2
1
4
3
-0.020
0.100
(b) ΔSQCMI image
2
1
4
3
2
1
4
3
(c) ΔSCI image
Loess Q CM C
C Q CM
Q C CM
Q CM
Q
Dust_1
Dust_2
Dust_3
Dune sand
Soil
CM Q C
_1
_2
_3
_4
Region

## Slide 19
Mineralogical changes resulting from settling of the dust particles – loess soil
-0.060
0.140
(a)
(b)
3
2
1
3
2
1
(c)
(d)
3
2
1
3
2
1
ΔSQCMI image (a) and ΔSCI image (c) emphasizing changes on the surface resulting from the dispersion of 100 g m-2 dust_2 (region 1), 100 g m-2 dune sand (region 2) and 50 g m-2 dune sand (region 3); ΔSQCMI image (b) and ΔSCI image (d) resulting from the dispersion of 250 g m-2 dust_2 (region 1), 250 g m-2 dune sand (region 2) and 50 g m-2 dune sand (region 3); green color represents ΔSQCMI and ΔSCI ≈ 0, i.e., no mineralogical changes.
The addition of dust_2 to the surface resulted in negative ΔSQCMI and ΔSCI values, indicating a decrease in the relative amount of quartz and an increase in the amount of carbonates, respectively, whereas the addition of dune sand resulted in positive ΔSQCMI and ΔSCI values, indicating an increase in the relative amount of quartz and a decrease in the amount of carbonates, respectively.
Soil Q C CM
ΔSQCM
ΔSCI
1 - Q C CM, 100 g m-2
2,3 - Q 100, 50 g m-2
1 - Q C CM, 250 g m-2
2,3 - Q 250, 50 g m-2

## Slide 20
VNIR-SWIR reflectance spectra– field measurements – loess soil
Iron Oxides

## Slide 21
Future Notes: Orbital Sensors
9.56 mm
8.06-8.12 mm
11.24 mm
Missing for our indices:

## Slide 22
LSTM –Option 1
LSTM –Option 2
9.56 mm
8.06-8.12 mm
11.24 mm
Missing for our indices:
Light changes may align LSTM with the Soil suggested Indices

## Slide 23
Quartz and Carbonates are the major minerals active in the LWIR region to assess dust accumulation on the soil surface
Using the two indices SQCMI and SCI it is able to identify mineralogical changes (from dust origin) depended on the mineral composition of the dust compared to the soil surface mineralogy, and the amount of settling dust.
Spatial imaging of soil mineral abundance and monitoring of mineralogical changes resulting from settled desert dust is possible on a local l scale.
Utilization of the LWIR spectral region and the suggested procedure can be used to study the mineralogical effects of other processes, natural and unnatural, affecting the soil surface.
Future orbital LWIR mission may benefit from the results of this study
Conclusions

## Slide 24
Thank You for your attentions !!
TAU-RSL