## Slide 1
The role of coastal wetlands in reducing back bay flooding: New Jersey Back Bays case study
European Geophysical Union Vienna, Austria 8 May 2020
United States
Gregory Slusarczyk and Mary A. Cialone
US Army Corps of Engineers (USACE) Engineer Research & Development Center (ERDC)
US Army Corps
Of Engineers ®

## Slide 2: Overview
The goal of the project was to determine effectiveness of large-scale Natural and Nature Based Features (NNBF) measures for reducing storm surge water levels in portions of New Jersey Back Bay (NJBB) domain
The Approach was to numerically simulate the Designed large-scale NNBF concepts with use of
  coupled Two-dimensional, depth averaged ADCIRC hydrodynamic model and Steady-State Spectral Wave Model STWAVE
  Standalone ADCIRC model
forcing from synthetic tropical cyclone events generated jointly by OceanWeather Inc. (OWI)/ERDC as part of the North Atlantic COAST COMPRIHENSIVE STUDY (NACCS)
Simulations did NOT include the effects of tides

## Slide 3: Modeling scenario 1 (Configuration 5: Brigantine area)
Coupled ADCIRC and STWAVE
Configuration 5: grid with NNBF measures (with-project-conditions)
Configuration 3: grid without NNBF measures (without-project-conditions)
Storm surge barriers at Great Egg Inlet and Absecon Inlet (Configuration 5 & 3)

## Slide 4: Modeling scenario 2 (Configuration 8: Holgate and Great Egg Harbor areas)
ADCIRC standalone (no waves)
Configuration 8: grid with NNBF measures (with-project-conditions)
North: grid without NNBF measures (without-project-conditions)
Storm surge barriers at Manasquan Inlet and Barnegat Inlet (Configuration 8 & North)

## Slide 5: Selected Storms
Ten synthetic tropical storms from NACCS selected to minimally cover the range of
Storm size
Direction
Intensity
for the NJ coastal region and demonstrate the varying surge response in this region
NJBB Storms | Landfall Angle (deg N) | Central Pressure Deficit (hPa) | Rmax (km) | Forward Speed (km/hr)
1 | -40 | 88 | 65 | 16
2 | -60 | 78 | 125 | 65
3=350 | -60 | 68 | 52 | 26
4 | -60 | 58 | 88 | 28
5 | -20 | 88 | 55 | 62
6 | -20 | 78 | 82 | 27
7 | 0 | 78 | 74 | 38
8 | 20 | 78 | 73 | 38
9=636 | 40 | 78 | 47 | 14
10 | 40 | 83 | 67 | 59

## Slide 6: Storm 350 Scenario 1 Brigantine
Maximum Surge Envelope
Difference (Config5-Config3)
Zoom of Difference (Config5-Config3)
(m)
(m)

## Slide 7: Storm 350 - Scenario 1 brigantine
Base and Config5 time-series map showing point 49, 50, and 59 and the time-series for these 3 points

## Slide 8: Storm 636 Scenario 1 brigantine
(m)
(m)
Difference (Config5-Config3)
Zoom of Difference (Config5-Config3)
Maximum Surge Envelope

## Slide 9: Storm 636 – Scenario 1 Brigantine
Base and Config5 Time series map showing point 49, 50, and 59 and the time-series for these 3 points

## Slide 10: Storm 350 Scenario 2 Holgate
Zoom of Difference (Config8-North)
Difference (Config8-North)
Maximum Surge Envelope
(m)
(m)

## Slide 11: Storm 350 – scenario 2 near Holgate
Base and Config8 time-series map showing point 33, 73, and 61 and the time-series for these 3 points

## Slide 12: Storm 636 scenario 2 Holgate
Difference (Config8-North)
Zoom of Difference (Config8-North)
Maximum Surge Envelope
(m)
(m)

## Slide 13: Storm 636 – scenario 2 near Holgate
Base and Config8 time-series map showing point 33, 73, and 61 and the time-series for these 3 points

## Slide 14: Storm 350 scenario 2 Great Egg Harbor
(Config8-BaseNorth)
Difference (Config8-North)
Maximum Surge Envelope
(m)
(m)

## Slide 15: Storm 350 – scenario 2 near Great Egg Harbor
Base and Config8 time-series map showing point 111, 117, and 49 and the time-series for these points

## Slide 16: Storm 636 scenario 2 Great Egg Harbor
Difference (Config8-North)
Maximum Surge Envelope

## Slide 17: Storm 636 – scenario 2 near Great Egg Harbor
Base and Config8 time-series map showing point 111, 117, and 49 and the time-series for these points

## Slide 18
Pros
  Most of the area of interest experienced storm surge reduction by 10-30 cm due to NNBF measures
  The reduction occurred over long period of time (~10 hrs)
Cons
  Some areas (Holgate) experienced water level increase due to north-to-south wind direction (Storm 636)
Summary