## Slide 1: ROmanian Methane Emissions from Oil&gas
Thomas Röckmann and the The ROMEO team
PI of ROMEO project, coordination of Marie Curie training network MEMO2
Professor for Atmospheric Physics and Chemistry, Utrecht University, The Netherlands

## Slide 2: Outline
    Objectives and campaign overview
    Participants and methods employed
    First results

## Slide 3: Why Romania?
Romania: relatively large onshore oil and gas reservoirs within EU
high production
high emissions reported
UNFCCC statistics
Reported emissions from oil & gas from EU countries
very few measurements

## Slide 4: ROMEO: Emission quantification at 3 scales:
Basin scale: 2 aircraft
Well scale: 6 vehicle teams
2 drone teams
1 leak detection team
City scale (Bucharest):
3 vehicle teams
30 sept – 20 oct
30 sept – 20 oct
(component scale)
17 aug – 31 aug

## Slide 5: ROMEO Participants
Additionally, two major O&G producers (OMV Petrom and Romgaz) provide activity data to the project and learn from the science.

## Slide 6
Romanian O&G reservoirs

## Slide 7
ROMEO focus areas

## Slide 8
The ROMEO team

## Slide 9
Facility-
level
Component-
level
Approaches used during ROMEO
Detect leaks and facilitate immediate repair
Quantify all facility emissions
Requires scientific experts
100s of m
Basin-
level
Focus on total emissions
Requires scientific experts
Notes: CH4 emissions can be detected using an infrared camera
  It visualizes the radiation properties of hydrocarbon and other gases
This is what you can see here. But you can also miss plumes.
Why potentially miss plumes?
  Strong winds dilute the signal
  Emitting component not in line of sight, large plume could look like background
  Approach focuses on leaks, not other intended emissions
The magnitude of the emissions can then be quantified using a high flow sampler
  It measures the flow rate of the gas directly at the source and the CH4 concentration
  Advantage is that it can measure individual component-level emissions accurately
  These are traditionally used to generate EFs for inventories
Disadvantage is that it quantifies only what you measure. This is really important
  If you fail to detect the plume, you can’t measure it.
  Even if emissions are detected from the distance, it may be difficult to access (if need a manlift) or may be unsafe if the leak is very large.
  No matter the reason, if it isn’t quantified, it won’t appear in an inventory.

## Slide 10
Reliable quantification: Tracer release measurements
Analytical instrument w. high resolution
Global Navigation Satellite System
Principle
Plume traverese recorded at 17:10 on October 17th, at oil well. DTU Environment, 2020
Charlotte Scheutz, Antonio Delre, Technical University of Denmark
Release an artificial gas (tracer) at the target site
Observe plumes of tracer and target
More detailed math
Notes: CH4 emissions can be detected using an infrared camera
  It visualizes the radiation properties of hydrocarbon and other gases
This is what you can see here. But you can also miss plumes.
Why potentially miss plumes?
  Strong winds dilute the signal
  Emitting component not in line of sight, large plume could look like background
  Approach focuses on leaks, not other intended emissions
The magnitude of the emissions can then be quantified using a high flow sampler
  It measures the flow rate of the gas directly at the source and the CH4 concentration
  Advantage is that it can measure individual component-level emissions accurately
  These are traditionally used to generate EFs for inventories
Disadvantage is that it quantifies only what you measure. This is really important
  If you fail to detect the plume, you can’t measure it.
  Even if emissions are detected from the distance, it may be difficult to access (if need a manlift) or may be unsafe if the leak is very large.
  No matter the reason, if it isn’t quantified, it won’t appear in an inventory.

## Slide 11
Example applications
Drive-by
Combination ground-based and aircraft measurements

## Slide 12
Mass balance from drone flights

## Slide 13
Leak detection with FLIR camera
Compressor station: Many detected leaks fixed in short period
Wells: Often open vents/valves

## Slide 14: Example raster flights (INCAS aircraft)
Black dots:
Facilities
Wind
South of Transylvanian Alps
North of Transylvanian Alps
Quantitative evaluation will be performed with atmospheric models

## Slide 15: Example mass balance flight (SA aircraft)
Individual cluster
Quantifying and reconciling 2 individual regional flights on different days with additional flights at cluster-scale
Region including Ploiesti (downstream, non-O&G)

## Slide 16: Limitations
  Low winds during campaign period complicated/precluded quantification on many days
    Both ground-based and aircraft-based work affected
        still > 150 ground-based and ≈ 20 aerial quantifications
    No problem for component level (FLIR camera) measurements

## Slide 17: Summary aircraft work
9 regions surveyed
15 raster measurements (including repeats)
21 cluster quantification attempts (including repeats)
6 region quantification attempts (including repeats)
1 large venting source quantification attempt

## Slide 18: Summary ground-based work
7 regions surveyed
> 1200 wells and facilities screened
  Vehicles, drones and aircraft, using different methods
> 150 wells and facilities quantified

## Slide 19: ROMEO phase A summary
Same flux on 2 days
Gas
blind
spot
Target area
Phase B
Aerial quantifications (whole box)
Aerial quantifications (cluster)
Clusters 3
5 Clusters
5 Clusters + vent + facility
1 Cluster

## Slide 20: ROMEO phase A summary
12 ground
10 ground
42 ground
29 ground
20 ground
19 ground
Target area
Phase B
Aerial quantifications (whole box)
Aerial quantifications (cluster)
Ground quantifications

## Slide 21: Preliminary results
Methane emissions detected from (very roughly) half of screened facilities
  Consistent between vehicle and on-site measurements (FLIR camera)
  CH4 enhancements 1- 2,000 ppm (1000 * background) at distances 10-100m away from facility
  Aircraft sees ≈ 100 ppb CH4 enhancements at ≈ 100 meters altitude close to production clusters
Emission rates between <10-2 g/s and 102 g/s for individual facilities
Almost no gas flaring in the surveyed regions
Limited gas collection from oil wells
Visually, maintenance conditions appear highly variable across Romania

## Slide 22: Preliminary results
  Oil wells: emissions mostly due to facility design/state (e.g. open pipes), operational procedures (e.g. not properly closed valves). Only partly due to leaking equipment (e.g. flanges, pressure gauges).
  Oil wells with H2S emissions are much better maintained and emit much less.
  Gas wells: Generally lower emissions but large measured CH4 concentrations due to improperly closed valves/vents and (less often) leaking equipment.

## Slide 23: Preliminary results
  Compressor stations: high numbers of leakages at individual flanges, valves, vents, pressure regulators etc. Considered easily fixable by LDAR team.
  Storage facilities (different types): storage tanks often require maintenance (holes in tanks), but many facilities are also designed to vent (no gas collection), especially older facilities.
  Collection manifolds: generally in good state and few leaks

## Slide 24: Outlook
  Continue evaluation:
    Finish and integrate all quantifications
    Add data from 1200 “screenings”
    Derive final emission distributions
    Up-scaling to national scale
    Compare ground-based and aircraft – derived emissions
    Compare to inventories and reported emissions
    Report and publish data
  ROMEO phase B in planning (2020 or 2021)
    Mostly in Transylvania, plus revisits in southern part planned (gas areas)

## Slide 25: ROMEO impact
  Improved emissions estimates for industry and policy
  Optimize mitigation strategies

## Slide 26: Thanks for your attention