## Slide 1
Introduction
Website
P
PE
Data
Method
Catchments
Results
Models
Scenarios
Perspectives
Daily Q
Daily P, PE, T
ESP
ECMWF
P0
Gardenia (BRGM)
GR6J (Inrae)
Mordor (EDF)
PRESAGES (LOTERR)
SIM (Météo-France)
Calibration
Real-time forecasting
Tool outputs
2017-2019 low-flow periods

## Slide 2
GR6J
PRESAGES
SIM
MORDOR
GR6J
GARDENIA/EROS
Developed in R (based on airGR package) and Fortran
Five hydrological models (SIM run independently)
Daily ensemble low-flow forecasting up to 90-day ahead
Operational on 210 French catchments since July 2017
Main characteristics

## Slide 3
Introduction
Website
P
PE
Data
Method
Catchments
Results
Models
Scenarios
Perspectives
Daily Q
Daily P, PE, T
ESP
ECMWF
P0
Gardenia (BRGM)
GR6J (Inrae)
Mordor (EDF)
PRESAGES (LOTERR)
SIM (Météo-France)
Calibration
Real-time forecasting
Tool outputs
2017-2018 low-flow periods

## Slide 4
Introduction
Restrictions in water use due to drought in France
17 October 2018
home
Early anticipitation of low-flow periods needed to improve water management
In France in 2013: 73% of total withdrawals from rivers
Water uses affected by water shortages in rivers
Climate change: perspectives of more severe summer low flows
Lack of forecasting tool at national scale
24 July 2017
Vigilance
Alerte
Crisis
Reinforced alert

## Slide 5
 | Min | 25% | Median | 75% | Max
Area (km²) | 9 | 167 | 385 | 1169 | 110188
Median elevation (m) | 29 | 132 | 193 | 423 | 1794
Flow availability (years) | 4 | 25 | 44 | 52 | 61
Rate of missing data (%) | 0 | 1 | 3 | 7 | 69
Catchments
home
Test catchments selected by French operational services (OS) involved in low-flow management
OS provided lists of catchment with limited human influences
210 catchments for real-time operational forecasting: 9 to 110 000 km²
Various hydrological regimes (oceanic, Mediterranean, mountainous)
2020: spatial extension to around 800 catchments over France

## Slide 6
Hydrological model | Short name | Institution | Type | Spatial resolution | Number of free parameter | Assimilation method | Post-treatment method
GARDÉNIA | GARD | BRGM | Conceptual | Lumped | 4 to 13 | X | 
GR6J | GR6J | Inrae | Conceptual | Lumped | 6 to 8 | X | 
MORDOR | MORD | EDF-DTG | Conceptual | Lumped or semi-ditributed | 11 to 18 | X | 
PRESAGES | PRES | Lorraine Univ, | Conceptual | lumped | 7 to 10 | X | 
SIM | SIM | Météo-France | Physically based | Distributed | No calibration |  | X
GARD
GR6J
MORD
PRES
SIM
Which hydrological models?
Five hydrological models available in PREMHYCE
Four lumped storage-type models (called here GARD, GR6J, MORD and PRES) and one distributed and more physically oriented model (SIM)
Various formulations of low-flow simulation
Use of assimilation schemes and/or statistical correction procedures in forecasting mode
Different numbers of free parameters (prior expert calibration and/or automatic calibration through the PREMHYCE module)
Multi-model combination to be implemented soon
Multi-model combination
home

## Slide 7
2009
How to forecast low-flow using hydrological models?
1. Initialization
Streamflow simulation by the model over a past period (typically at least one year) prior to the date j, using weather inputs observation over that period.
At time j, available model state variables, resulting from the integration of past conditions and representing the basin's potential to generate runoff
3. Forecast
From the previously determined initial conditions, model simulations of streamflows over the forecast period, using a weather forecast scenario derived or a climate archive
Simulation of future streamflow from j+1 to j+L
Step repeated for each available scenario, starting each time with the same initial conditions at j
An ensemble of streamflow forecasts is generated, each member of this set being relative to a given scenario.
2. Assimilation (also called updating)
Use of the measurements available on the catchment to correct the model errors at time j, typically a difference between the observed and simulated values ​​of flow at this time
Appropriate assimilation approaches to minimize these errors, for example by updating model internal states, thereby generating an updated state vector
This step of assimilation is not systematically implemented in all models
4. Statistical processing
Statistical analysis of the members of the hydrological forecast to determine probabilities of being under low-flow thresholds
Post-processing approaches to correct the observed average model bias over a long time period (e.g. a systematic overestimation of low flows)
Which scenarios are used?
home

## Slide 8
Daily streamflow
  National streamflow archive (HYDRO database)
  4 to 61 years (1959-2019)
Daily climatic variables
  Precip. (P), Potential evapotransp. (PE), Temp. (T)
  SAFRAN climate reanalysis (Météo-France)
  61 years (1959-2019)
  Forecasting scenarios
P
PE
Which data are used?
home

## Slide 9
2009
Model
  Several future meteorological inputs sources:
  ESP: Climatic archive (~60 scenarios)  includes severe drought conditions
  Zero-precipitation scenario  worst case streamflow forecast
  ECMWF ensemble meteorological forecasts (up to 10 days)
01/05/2010
01/06/2010
01/07/2010
01/08/2010
01/09/2010
Which forecasting scenarios?
home

## Slide 10
Website
(restricted
access)
home
Click
here

## Slide 11
Click on a model
back
Website
(restricted
access)

## Slide 12
back
Q forecast with climatic archive (ESP)
Q forecast with P=0
Natural variability of Q
Q obs
Q forecast with P & PE obs
Vigilance
Alert
Reinforced alert
Normal
Cumulative P with climatic archive
Quantiles 10-90%
Catchment : | Ill at Didenheim | Code HYDRO : | A1080330 |  | 
Hydrol. Model | Gardenia | Date of forecast : | 11/04/2017 | Lead-time (days) | 90
Thresholds | Vigilance (m3/s) : 1,10 | Alert (m3/s) : 1,10 | Reinforced alert (m3/s) : 1,10 | Crisis (m3/s) : 1,10 | 
Synthesis plot
Temperature with climatic archive
Outputs for the Gardenia model
Synthesis plot
Text files
home

## Slide 13
Catchment : | Ill at Didenheim | Code HYDRO : | A1080330 |  | 
Hydrol. Model | GR6J | Date of forecast : | 11/04/2017 | Lead-time (days) | 90
Thresholds | Vigilance (m3/s) : 1,10 | Alert (m3/s) : 1,10 | Reinforced alert (m3/s) : 1,10 | Crisis (m3/s) : 1,10 | 
Synthesis plot
back
Q forecast with climatic archive (ESP)
Q forecast with P=0
Natural variability of Q
Q obs
Q forecast with P & PE obs
Vigilance
Alert
Reinforced alert
Normal
Quantiles 10-90%
Cumulative P with climatic archive
Temperature with climatic archive
Outputs for the GR6J model
home
Synthesis plot
Text files

## Slide 14
Catchment : | Ill at Didenheim | Code HYDRO : | A1080330 |  | 
Hydrol. Model | Mordor | Date of forecast : | 11/04/2017 | Lead-time (days) | 90
Thresholds | Vigilance (m3/s) : 1,10 | Alert (m3/s) : 1,10 | Reinforced alert (m3/s) : 1,10 | Crisis (m3/s) : 1,10 | 
Synthesis plot
back
Q forecast with climatic archive (ESP)
Q forecast with P=0
Natural variability of Q
Q obs
Q forecast with P & PE obs
Vigilance
Alert
Crisis
Normal
Quantiles 10-90%
Cumulative P with climatic archive
Temperature with climatic archive
Outputs for the Mordor model
home
Synthesis plot
Text files

## Slide 15
Catchment : | Ill at Didenheim | Code HYDRO : | A1080330 |  | 
Hydrol. Model | Presages | Date of forecast : | 11/04/2017 | Lead-time (days) | 90
Thresholds | Vigilance (m3/s) : 1,10 | Alert (m3/s) : 1,10 | Reinforced alert (m3/s) : 1,10 | Crisis (m3/s) : 1,10 | 
Synthesis plot
back
Q forecast with climatic archive (ESP)
Q forecast with P=0
Natural variability of Q
Q obs
Q forecast with P & PE obs
Vigilance
Alert
Crisis
Normal
Quantiles 10-90%
Cumulative P with climatic archive
Temperature with climatic archive
Outputs for the PRESAGES model
home
Synthesis plot
Text files

## Slide 16
Observed precipitation
Extremely wet
Wet
Neutral
Dry
Moderately dry
Extremely dry
SPI (Standardized Precipitation Index): Comparison between P and historical mean P over a same period of the year
Deficit on spring & summer
Rainy start of year 2018
Summer/Autumn 2018: large deficit
Winter 2016/2017: Large rainfall deficit
2017-2018-2019 drought periods
next
Spring-summer 2019: slight but long deficit
Moderately wet

## Slide 17
General streamflow deficit
Wet start of year 2018
General streamflow deficit
+ wet
+ dry
Observed Streamflow
next
2017-2018-2019 drought periods

## Slide 18
next
Mayenne river at Ambrières-les-Vallées : d+15
Observation in the low part
of ensemble streamflow forecasts
Qobs
Natural variability of Q
Ensemble streamflow forecast (ESP)
Forecasts with PREMHYCE on the 2017 & 2018 periods

## Slide 19
Mayenne river at Ambrières-les-Vallées : d+15
Qobs
Natural variability of Q
Ensemble streamflow forecast (ESP)
Late low-flow period well forecasted
Usefulness Q forecasts compared to historical Q
back
home
Forecasts with PREMHYCE on the 2017 & 2018 periods

## Slide 20
Perspectives
  Deployment over France
  Module to take into account human influences
  Improvement of assimilation methods
  Implementation of multi-model combination
  Seamless hydrological forecasts