## Slide 1: FP_ILM: Extremely fast volcanic SO2 plume height retrieval based on S5P/TROPOMI data using inverse learning machines
Dmitry Efremenko, Pascal Hedelt,
Diego Loyola, and Robert Spurr

## Slide 2: SO2 LH Overview
SO2 sources: Biogenic emissions, fossil fuel combustion, refineries smelting, volcanoes
Major air pollutant
Volcanic eruption ejects large amounts of ash and trace gases, including SO2
Ash and SO2 can be collocated in fresh plumes, SO2 proxy for ash
Impact on human health, public as well as air traffic safety
Depending on height, lifetime from days to several weeks
  Acid rain, Sulfates
Regular ground-based monitoring only for limited amount of volcanoes
Satellites allow for global daily measurements of SO2 amount (VCD), plume height (LH) and aerosol load

## Slide 3: Raikoke eruption June – July 2019

## Slide 4: SO2 LH retrieval
Determination of the vertical distribution is challenging and not easily extracted from UV spectral signatures
  VCD: direct effect on the optical depth
  LH: indirect effect on OD – influence on number of photons passing through the SO2 layer as well as the layer OD due to the temperature dependency of the SO2 absorption cross-sections
SO2 LH retrieval algorithms for UV developed so far rely on direct fitting, which involves time-consuming radiative transfer calculations
  Not applicable in NRT environment
High spatial resolution and data amount of S5P require fast algorithms

## Slide 5: SO2 LH retrieval algorithm FP-ILM: Full Physics Inverse Learning Machine
Novel method: Full-Physics Inverse Learning Machine (FP_ILM) for extremely fast and accurate retrieval of the SO2 plume height
  Combination of smart sampling, dimensionality reduction & machine learning
  Offline training phase (slow)
  Online application of inversion operator (fast)
  Processing speed: 2ms / TROPOMI Pixel
  Accuracy: 2km for SO2 > 20 DU
    Efremenko et al (2017): Volcanic SO2 plume height retrieval from UV sensors using inverse learning machines IJRS, Vol 38
    Hedelt et al. (2019): SO2 Layer Height retrieval from Sentinel-5 Precursor/TROPOMI using FP_ILM, AMT-2019-13, Vol. 12, No. 10
Development in the framework of ESA S5P Innovations: SO2 LH project
https://atmos.eoc.dlr.de/so2-lh/ (Google search: ‘SO2 LH’)

## Slide 6: Full Physics Inverse Learning Machine (FP_ILM)
Smart parameter grid (8D)
Non-uniform, optimized (Loyola et al. 2016)
Geometry, surface properties, O3 VCD, SO2 VCD, SO2 LH
US Standard atmosphere, TOMS O3 Reflectance Spectra (310-335 nm)
LIDORT RRS, (Spurr et al. 2008)
Convolution with ILS, added noise
Principal Component Analysis Extract main information from spectra, reduce dimensionality
Machine Learning: Neural Network
Application to measured data
1
3
5
7

## Slide 7: Principal component regression
Plume height (PH) is a weighted sum of principal components (PCs):
Accuracy estimation based on synthetic spectra:
Regression coefficients αi and PCs are estimated from synthetic spectra;

## Slide 8: Application to GOME-2 (Kasatochi 2010)

## Slide 9: FP-ILM: version with neural network
Training of neural network
Input: Training spectra
  PC scores
  Viewing/surface properties
Output:
  SO2 LH
  Trained NN
Application to real data
1. Application of PC operator
  Dimensionality reduction of spectra
  2. Application of NN
    SO2 LH

## Slide 10: FP-ILM: Application test data
Application to simulated spectra (SNR=1000) test dataset with prescribed
SO2 LH @ 2.5, 5, 12, 20, and 27km,

## Slide 11: Application to S5p: Sinabung eruption Feb. 2018 (Hedelt et al. 2019)
MLS
CALIPSO
VCD
SO2 LH

## Slide 12: Application to S5p: Raikoke eruption Jun-Jul 2019 (Hedelt et al. 2019)
~1000DU of SO2
SO2 LH: Up to 16km

## Slide 13: Application to S5p: Taal eruption Jan 2020
Taal volcanic eruption (Philippines)
SO2 LH: Up to 18 km (Preliminary)

## Slide 14: Summary
A novel method (FP_ILM) for the precise and extremely fast retrieval of volcanic SO2 layer height (LH) based on S5P/TROPOMI data is proposed;
A combined principal components analysis (PCA) and neural network approach (NN) is implemented;
The FP_ILM approach enables for the first time to extract the SO2 LH information in a matter of seconds for an entire S5P orbit and thus applicable in NRT application.
Development in framework of ESA S5P+I: SO2 LH project.
Hourly S5P SO2 LH results for volcanic detections @Twitter: @DLRSO2
The algorithm details can be found in
Efremenko D.S., Loyola D., Hedelt P. and Spurr R. // International Journal of Remote Sensing. 2017. V. 38:sup1, P. 1-27. https://doi.org/10.1080/01431161.2017.1348644
Hedelt P., Efremenko D., Loyola D., Spurr R., Clarisse L. // Atmospheric measurement techniques. 2019. V. 12. P. 5503. https://doi.org/10.5194/amt-12-5503-2019