## Slide 1: On the use of Geostationary Lightning Mapper (GLM) data as proxy for heavy precipitation
1Vandoir Bourscheidt, 2Maria-Helena Ramos
1 Federal University of São Carlos (UFSCar, Brazil) - currently visiting scientist at INRAE
2 National Institute for Research on Agriculture, Food and Environment (INRAE, Antony, France)
EGU session HS7.1 - Precipitation measurement: techniques, processes and hydrological applications at the catchment scale, Tuesday, 05 May 2020

## Slide 2: Motivation Lightning data from GLM
Geostationary Lightning Mapping (GLM) is a new sensor onboard GOES fourth generation (G16 and G17) with the unprecedent capability to detect the luminous energy from lightning at every few seconds and for whole Americas and Pacific (centered at 75°W and 137°W);
Similar sensors will be available on other satellites (METEOSAT and Fengyun) in the close future, hopefully extending its coverage to the entire world.
Since applications are expected to advance over deep convection and severe weather, hydrological rainfall-runoff models could benefit specially from the perspective of heavy rainfall events;
Studies of its applicability (and limitations) are just starting;
Outline
Motivation
Background
Material and methods
Results
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation

## Slide 3
Several studies suggest a reasonable relation between lightning data and precipitation;
Relations include:
  Rainfall-lightning ratio (RLR) approach or rain mass per lightning (e.g. Tapia, Smith and Dixon, 1997)
  The direct lightning-precipitation relationship (LPR) (e.g. Minjarez-Sosa et al. 2017; Zhou, Qie and S. Soula, 2001)
  Probabilistic and qualitative relationships using classes (e.g. Xu et al., 2013; Morales and Anagnostou, 2003)
Most of the studies are based on the comparison of lightning data against Weather Radar and Gauges;
General observation suggest lightning as a tool to classify/distinguish precipitating systems;
Background Lightning x Precipitation relationship
Outline
Motivation
Background
Material and methods
Results
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation

## Slide 4
General idea: evaluate GLM against gauges and weather radar data
Based on the physical aspects of lightning that constitute its products (flash, groups, energy, flash area, etc.), GLM data may be analyzed in several ways.
For the present work, three approaches will be evaluated:
  Use the gridded product (GLM GRIDS);
  Evaluate a Gaussian Kernel (KDE) method to spread discharges over an area;
  Count detected flash (filtered by quality flag);
Besides, different areas will be aggregated:
  Average around ground stations
  Average over watershed area (based only on the radar)
  Pixel by pixel
Material and methods
Outline
Motivation
Background
Material and methods
  About the GLM GRIDDED product
  About the study area
Results
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation
Example of GLM flashes and related KDE

## Slide 5
  Gridded format implemented by Bruning et al. (2019) for operational use that aggregates multiple information from original GLM file;
    Product with the same grid as GOES ABI (fixed grid);
    More focused on the meteorological aspects of lightning occurrence;
    Possibility to obtain many variables at once.
  Data is downloaded as NETCDF and afterward converted in a grid with 2x2km and hourly time steps
  6 products are used in this study:
    Flash extent density (FED)
    Group extent density (GED)
    Flash centroid average (FCT)
    Group centroid average (GCT)
    Flash Area (Farea, in km2)
    Group Area (Garea, km2)
Outline
Motivation
Background
Material and methods
  About the GLM GRIDDED product
  About the study area
Results
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation
About the GLM gridded product

## Slide 6
  Data for this analysis result from CEMADEN (Brazilian National Centre for Monitoring and Early Warning of Natural Disasters)
  Radar and Gauge data were selected based on its availability
    Ready to use “rain product” was further processed to improve relation against rain gauges based on simple arithmetic and a spatial filter (Wiener)
  Analysis were conducted in 2 areas:
    Jaraguari (MS)
    Tres Marias (MG)
  Period:
    27 Jan 2020 – 15 Mar 2020
Outline
Motivation
Background
Material and methods
  About the GLM GRIDDED product
  About the study area
Results
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation
About the study area
Radar evaluated so far
Jaraguari
Tres Marias

## Slide 7
Lightning is more “localized” than radar
Gauges X Radar fits better with LOG SCALE
Relation between Flash /Group Area and Density might be useful
Outline
Motivation
Background
Material and methods
Results
  Overview
  Radar x Gauges
  Radar x GLM
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation
Overview (using Gauges)
Time series analysis and general relationship
GLM GRIDS
RADAR

## Slide 8
Low/No relation between GLM vs. Gauges: effect of GLM pixel size?
Relation varies for individual stations (see boxplot)
Low improvements in multiple regression (<0.1)
Outline
Motivation
Background
Material and methods
Results
  Overview
  Radar x Gauges
  Radar x GLM
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation
Overview (using Gauges)
Time series analysis and general relationship
LOG(Gauges) x
 | N | R2
Radar | 297 | 0,300
Farea | 427 | 0,025
Garea | 427 | 0,042
Log(DenFED) | 336 | 0,026
Log(DenGED) | 336 | 0,041
Log(DenKDE) | 336 | 0,053
Gauges x
LOG(Gauges) x
Log(DenFCT) | 169 | 0,063
Log(DenGCT) | 252 | 0,015
Log(Flashes) | 104 | 0,034
Boxplot of R2 values distribution over gauge stations

## Slide 9
The relation includes LOG transformation on precipitation data.
A good agreement is observed for all stations; results are similar for Jaraguari.
Outline
Motivation
Background
Material and methods
Results
  Overview
  Radar x Gauges
  Radar x GLM
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation
Radar versus Gauges
Example for Tres Marias radar/stations

## Slide 10
The analysis was conducted at both regions
Day-night variations seem to be important
Variables with higher relation were chosen:
  Radar vs. FED Radar vs. GED Radar vs. Group Area
  Radar vs. KDE Radar vs. Flash Area
Outline
Motivation
Background
Material and methods
Results
  Overview
  Radar x Gauges
  Radar x GLM
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation
Radar versus GLM
Pixel-by-pixel analysis
Tres Marias
Jaraguari

## Slide 11
Outline
Motivation
Background
Material and methods
Results
  Overview
  Radar x Gauges
  Radar x GLM
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation
Radar versus GLM
Pixel-by-pixel analysis – correlation over time
Two variables are presented: Group Density and Group Area
Correlation (Pearson) varies over time depending mainly on the amount of coverage between radar and GLM
Large (small) R values for higher (lower) co-coverages

## Slide 12
Relationship GLMxRadar is better than GLMxGauges (slide 8)
Inverse relation for Flash /Group Area might be useful to improve multiple regression models
Group Density (logscale) shows the best relationship with radar
Outline
Motivation
Background
Material and methods
Results
  Overview
  Radar x Gauges
  Radar x GLM
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation
Radar versus GLM
Analysis for watersheds - relation between products
R2 (GLM x Radar) distribution for many watersheds and for each GLM variable (lower axis)

## Slide 13
Multiple regression suggested: Log(Group Density) + Group Area + Solar Elevation (Day/Night condition)
R2 improved by 50% compared to a single variable.
Outline
Motivation
Background
Material and methods
Results
  Overview
  Radar x Gauges
  Radar x GLM
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation
Radar versus GLM
Analysis for watersheds – multiple variables

## Slide 14
Multiple regression suggested: Log(Group Density) + Group Area + Solar Elevation (Day/Night condition)
R2 improved by 25% compared to a single variable.
Radar versus GLM
Analysis for gauges and watersheds – multiple variables
Outline
Motivation
Background
Material and methods
Results
  Overview
  Radar x Gauges
  Radar x GLM
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation
Gauges
Watersheds

## Slide 15
Random Forest applied to the variables using radar
Relation (and N) is lower for gauges than over watersheds
Radar versus GLM
Analysis for gauges and watersheds – multiple variables
Outline
Motivation
Background
Material and methods
Results
  Overview
  Radar x Gauges
  Radar x GLM
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation
MSE: 21.02
R2: 0.24
Importance:
DenGED: 0.37
Garea: 0.35
Sun_Alt : 0.29
MSE: 25.12
R2: 0.44
Importance:
DenGED: 0.43
Garea: 0.32
Sun_Alt: 0.25
Gauges
MSE: 3.59
R2: 0.61
IMportance:
DenGED : 0.46
Garea: 0.28
Sun_Alt : 0.26
MSE: 6.88
R2: 0.48
Importance:
DenGED: 0.44
Garea: 0.3
Sun_Alt: 0.26
Watersheds

## Slide 16
Outline
Motivation
Background
Material and methods
Results
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation
Final Remarks
Radar and gauges relationship is good considering a LOG scale
GLM is better related to radar than gauges possibly due to GLM pixel size limitation (originally ~8km);
Relationship increases when considering values averaged over the watershed areas;
General low relationship probably associated with the flash duration and flash rate trade-off (as discussed in Zhang and Cummins 2020): some severe systems seem to present less flashes than expected;
The join flash area and group density analysis seems promising, bearing in mind that smaller areas maybe more related to more intense thunderstorms
Next steps:
  Evaluate the predicted models (regression and RF) with a hydrological model;
  Extend the analysis over a larger dataset to confirm or improve the results.

## Slide 17
Outline
Motivation
Background
Material and methods
Results
Final remarks
  On the use of Geostationary Lightning Mapper data as proxy for heavy precipitation
Final remarks
Mentioned references:
  Zhang, D., & Cummins, K. L. ( 2020). Time evolution of satellite‐based optical properties in lightning flashes, and its impact on GLM flash detection. Journal of Geophysical Research: Atmospheres, 125, e2019JD032024. https://doi.org/10.1029/2019JD032024
  Minjarez-Sosa, C.M., C.L. Castro, K.L. Cummins, J. Waissmann, and D.K. Adams, 2017: An Improved QPE over Complex Terrain Employing Cloud-to-Ground Lightning Occurrences. J. Appl. Meteor. Climatol., 56, 2489–2507, https://doi.org/10.1175/JAMC-D-16-0097.1
  Xu, W., R.F. Adler, and N. Wang, 2013: Improving Geostationary Satellite Rainfall Estimates Using Lightning Observations: Underlying Lightning–Rainfall–Cloud Relationships. J. Appl. Meteor. Climatol., 52, 213–229, https://doi.org/10.1175/JAMC-D-12-040.1
  Zhou, Y., Qie, X., and Soula, S.: A study of the relationship between cloud-to-ground lightning and precipitation in the convective weather system in China, Ann. Geophys., 20, 107–113, https://doi.org/10.5194/angeo-20-107-2002, 2002.
  Bruning, E., Tillier, C. E., Edgington, S. F., Rudlosky, S. D., Zajic, J., Gravelle, C., et al. ( 2019). Meteorological imagery for the geostationary lightning mapper. Journal of Geophysical Research: Atmospheres, 2019; 124: 14285– 14309. https://doi.org/10.1029/2019JD030874
  Morales, C.A. and E.N. Anagnostou, 2003: Extending the Capabilities of High-Frequency Rainfall Estimation from Geostationary-Based Satellite Infrared via a Network of Long-Range Lightning Observations. J. Hydrometeor., 4, 141–159, https://doi.org/10.1175/1525-7541(2003)4<141:ETCOHR>2.0.CO;2
  Tapia, A., J.A. Smith, and M. Dixon, 1998: Estimation of Convective Rainfall from Lightning Observations. J. Appl. Meteor., 37, 1497–1509, https://doi.org/10.1175/1520-0450(1998)037<1497:EOCRFL>2.0.CO;2
Acknowledgments:
  The authors would like to thank the Brazilian Agency CAPES for the financial support (process n. 88887.466472/2019-00).