## Slide 1
Data & Decision Science for Energy Transition
Towards a seamless approach for photovoltaic forecasting
Thomas Carriere, George Kariniotakis
EGU2020 Sharing Geosciences Online

## Slide 2: Motivation
Large variety of forecasting products required for electricity markets:
Day-ahead schedule:
Horizon +12 to +36 hours
Resolution ~1 hour
Intra-day market:
Horizon +30 minutes
Resolution ~30 minutes
Storage planning:
Horizon as close to real-time as possible
Resolution as high as possible

## Slide 3: Motivation
PV power forecasting models are often designed for one specific horizon/resolution
In this work we propose a single model to cover all PV forecasting products
This effectively simplifies the usage of PV power forecasts in several decision-making processes

## Slide 4: Motivation
Proposition based on the Analog Ensemble (AnEn) method
  Combine heterogenous sources of input
  Forecasts adapted to market time frames:
    Provide both intra-day and day-ahead accurate forecasts
    Provide forecasts with both high (i.e. 5 minutes) and low (i.e. 30 minutes) temporal resolutions
    Provide forecasts starting at any time of the day
  As fast as possible
  Probabilistic forecasts for decision under uncertainty
To implement
Already present in the state-of-the-art
To check after implementation

## Slide 5: Methodology
2. Select k most similar past inputs
NWP, Clear-sky |  |  |  |  | 
Predictive inputs (NWP, Clear-sky) |  |  |  |  | 
Past observations |  |  |  |  | 
Observation inputs (Measurements, Satellite) |  |  |  |  | 
1. Compute similarity between current and past inputs
Past productions
3. Obtain the k corresponding past productions =
Analog Ensemble
4. Derive PDF from the Analog Ensemble using a KDE approach
Production Forecast
?

## Slide 6: Methodology
To achieve short-term forecasts:
Measurements for very short-term
Satellite data for short-term
Source: Solar Training 2016, OIE- Transvalor

## Slide 7: Methodology
Standard AnEn model:
The weights are optimized on a training set (“wrapper”)
  We propose a “filter” approach to compute the weights directly from the history without an optimization loop

## Slide 8: Methodology
When is the forecast horizon:
The weights are dependent on the forecast horizon.
  Compute the weight of each feature based on its Mutual Information (MI) with the measurements
  Normalize the weight so that the sum of all the weights coming from a same data source is not higher than a set limit.

## Slide 9: Methodology
  Satellite data: Estimation of GHI time series for each pixel from geostationary satellite images following [Blanc2011]
    Very large number of redundant features
    Selection of representative pixels based on MI with the measurements
T + 30 minutes
T + 90 minutes
T + 250 minutes
[Blanc2011]: Philippe Blanc et al., The HelioClim project : Surface solar irradiance data for climate applications, In: Remote Sensing 3.2 (2011)

## Slide 10: Methodology
  3 AM
  12 AM
  17 PM
  Average over all starting times

## Slide 11: Evaluation of the AnEn model
Evaluation of the AnEn model on a portfolio composed of 12 PV plants ranging from 2 to 10 MW.
Measurements with 5- and 30-minute resolutions are used
Benchmark models are implemented:
  Day-ahead forecasts: Quantile Random Forest (QRF) and Bayesian Automatic Relevance Determination (ARD)
  Intra-day forecasts: Clear-sky index persistence and integrated auto-regressive (ARIMA) model

## Slide 12: Result – 30 minute resolution
Forecast performance for day-ahead forecasts (30-minute resolution, plant n°4):
CRPS: Continuous Ranked Probability Score, normalized by installed PV capacity
Reliability diagram: nominal vs. observed quantiles
Possible range for a perfectly reliable model

## Slide 13: Result – 5 minute resolution
Forecast performance for intra-day 5-minute forecasts. QRF and ARD models are discarded due to computational cost:
RMSE: Root Mean Square Error, normalized by installed power

## Slide 14: Computing time
Computing time required for providing a forecast for a given horizon in seconds
 | 30-minute resolution |  | 5-minute resolution | 
 | Training | Forecasting | Training | Forecasting
AnEn | - | 1.87 | - | 8.77
Persistence 1 | - | 5e-3 | - | 6e-3
Persistence 2 | - | 5e-3 | - | 6e-3
ARIMA | 9.2e-2 | 2.5e-7 | 10e-2 | 3.7e-3
QRF | 4.26 | 1.3e-2 | 68.0 | 4e-2
ARD | 10.75 | 10e-3 | 154 | 1e-3

## Slide 15: Conclusions and perspectives
A single forecasting model that can quickly provide accurate forecast for temporal resolutions from 5-minute to 1-hour, and horizon from 5 minutes to 3 hours
Additional types of data could be used:
  All-sky imagers
  Neighboring plants or weather stations
  Infra-red satellite data
  Commercial forecasts from third entities
More details in: T. Carriere, C. Vernay, S. Pitaval, F.P. Neirac, G. Kariniotakis, A Novel Approach for Probabilistic Photovoltaic Power Forecasting Covering Multiple Time Frames, IEEE Transactions on Smart Grid