## Slide 1
Winter Arctic sea ice bottom evolution detected by thermistor
string-based ice mass balance buoys (SIMBA)
Bin Cheng1, Timo Vihma1, Yubing Cheng1,7, Zeling Liao2, Ruibo Lei3, Mario Hoppmann4, Yubao Qiu5,
Amy Solomon8, Roberta Pirazzini1 and Stein Sandven6
1Finnish Meteorological Institute, Meteorological Unit, Helsinki, Finland (bin.cheng@fmi.fi)
2School of Data and Computer Science, Sun Yat-sen University, GangZhou, China
3Polar Research Institute of China (PRIC), Shanghai, China
4Alfred Wegener Institute (AWI), Bremerhaven, Germany
5Institute of Remote Sensing and Digital Earth (RADI), Chinese Academy of Sciences (CAS), Beijing, China
6Nansen Environmental and Remote Sensing Center (NERSC), Thormoehlensgate 47, 5006 Bergen, Norway
7Institute of Atmospheric Physics, Chinese Academy of Sciences, China
8 Physical Sciences Laboratory, NOAA , USA
Objectives
Long term sustainable real time monitoring snow and ice mass balance and air-snow-ice-ocean temperature variations in the Arctic Ocean using sea ice mass balance buoy (SIMBA).
Develop a reliable algorithm to retrieve snow depth and ice thickness from SIMBA data.
Investigate thermodynamic snow and sea ice mass balance in the Arctic Ocean.
Notes: This presentation demonstrate the deployment of thermistor string-based ice mass balance buoys (SIMBA) in the Arctic Ocean since summer 2018. We present how SIMBA data has been processed and some preliminary results on ice mass balance at bottom.

## Slide 2
SIMBA
CRREL_IMB
CRREL-SIMB3
There are several type of IMBs with different technology configurations
We use the simplest one (SIMBA)
Notes: We are aiming a SIMBA observation network, so cost-cutting is crucial.

## Slide 3
< 0.4 m
< 0.8 m
< 3.0 m
< 1.0 m
Air
Snow
Ice
Water
Air-Snow-Ice-Water (ASIW) system and temperature distribution vertically through ASIW in cold condition.
SIMBA Environmental vertical temperature: ET-field
Notes: SIMBA mainly observes temperature profile through air-snow-ice-ocean. The SIMBA thermistor string has 240 sensors and sensor interval is 2 cm.

## Slide 4
Air
Snow
Sea ice
Ocean
Time(t)
t0
t2
t1
T0
T1
T2
T1=T1-T0
T2=T2-T0
SIMBA Heating temperature field (HT-field)
Schematically illustration on now the SIMBA heating works: a small identical heating element is applied on each sensor. The heating is done once per day. The heating interval usually lasts for 60 s and 120 s.
Notes: In addition, SIMBA measures the heating temperature (SIMBA-HT) applying a small identical heating element on each sensor. The heating is applied once per day. The heating interval usually lasts for 60 s or 120 s. The temperature changes in air, snow, ice and water are different due to the different heat conductivities.

## Slide 5
Δzs,i(j) = 2 cm
Liao et al., 2018, IJDE https://doi.org/10.1080/17538947.2018.1545877
Notes: A SIMBA-algorithm was developed by Liao and others (2018) and used to extract snow depth and ice thickness from SIMBA-ET data. The algorithm was targeted for SIMBA data obtained from the Arctic Ocean, where the snow/ice interface remained unchanged.

## Slide 6
SIMBA- ET and SIMBA-HT field and algorithm (Liao et al, 2018) derived interfaces:
snow surface; sea level and ice bottom
Notes: How the SIMBA algorithm results look like.

## Slide 7
©CHINARE2018
©NABOS2018
© MOSAiC2019
©CAATEX2019
The Coordinated Arctic Acoustic
Thermometry Experiment
Chinese National Arctic Research Expedition
Nansen and Amundsen Basins Observational System
High-resolution Snow and Ice Mass Balance Array(SIMBA)
Notes: Several international Arctic field campaigns have been carried out in the past few years.

## Slide 8
CHINARE2018 (mid-August)
North of Chukchi Sea and Beaufort Sea:
Mean Hice = 2.4m
Mean Hsnow = 0.06m
NOBAS2018 (mid-September)
East Siberian Sea:
Mean Hice = 2.3m
Mean Hsnow = ~0m
CAATEX2019 (late-August)
North Pole:
Mean Hice = 1.7m
Mean Hsnow = 0.06m
MOSAiC2019 (October)
North of Laptev Sea:
Mean Hice = 1 m
Mean Hsnow = 0.11m
SIMBA buoys drift trajectories
Notes: The SIMBA buoys deployment and drift trajectories until early May 2020. The MOASiC deployments are largely active. For other deployment campaigns, only few SIMBA are still working.

## Slide 9
Table was made on
12, November, 2019
33 SIMBAs buoys are listed here.
More SIMBA buoys will probably be deployed in the Arctic Ocean during MOSAiC leg 3/4, CHINARE2020
and other field campaigns.
Table was checked on 22, April, 2020
17 SIMBA buoys in the table are still working

## Slide 10
Notes: SIMBA ice bottom evolution. Those SIMBAs were deployed during NOBAS field campaign in the East Siberian Sea. The white lines show the initial ice surface (valid until surface melting start in the melting season)

## Slide 11
SIMBA deployed during NABOS2018
Preliminary daily ice growth rate at ice bottom.
Bottom sea ice formation:
First winter:~
[70 cm - 110 cm]
Second winter:~
[40 cm - 70 cm]

## Slide 12
Notes: Those are SIMBA buoys deployed during CHINARE2018 and CAATEX 2019. The white lines show the initial ice surface (valid until surface melting start in the melting season)

## Slide 13
CHINARE2018
CAATEX2019
Two SIMBA deployed during CHINARE2018
160 cm?
60 cm
60 cm
70 cm
60 cm
Two SIMBA deployed during CAATEX2019

## Slide 14
FMI0601
FMI0605
Initial snow depth = 15 cm
Initial ice thickness = 180 cm
Initial snow depth = 13 cm
Initial ice thickness = 97 cm
Two SIMBA buoys measurement during MOSAiC
Freezing up of the borehole is associated with initial ice thickness and weather condition
Freezing up is visible from HT field.
Ice growth at bottom:
FMI0601: 40 cm
FMI0605: 115 cm
Ice thickness by early May:
FMI0601: ~220 cm
FMI0605: ~212 cm

## Slide 15
15
© CRREL-SIMB3
Snow depth and ice thickness derived from SIMBA_ET/HT. The results are comparable with CRREL-SIMB3 snow and ice thickness.

## Slide 16
Summary
Snow and Ice Mass Balance Array (SIMBA) buoys have been deployed in the Arctic Ocean and hopefully will continue to be deployed in the coming seasons.
A SIMBA-algorithm can retrieve snow depth and ice thickness from SIMBA ET and HT measurements reasonable well. In cold condition, the results are comparable with the results from CRREL-SIMB3 (seasonal ice mass balance buoy equipped with acoustic sounders).
The SIMBA HT fields are more visible for ice bottom detection.
Winter ice bottom growth rate: 0.2 - 0.35 cm/day.
The variation of ice growth at bottom are associated with:
  SIMBA location (CHINARE2018, NOBAS2018)
  initial ice thickness (CHINARE2018, NOBAS2018, CAATEX 2018, MOSAiC)
  oceanic heat flux (To Be Investigated)
  snow condition (TBI)