## Slide 1
Nowcasting Lightning Occurrence Using Machine Learning Techniques
The Challenge of Identifying Outliers
1 Swiss Federal Institute of Technology (EPFL), Switzerland
2 University of Leeds, UK
3 University of Applied Sciences of Western Switzerland (HES-SO), Switzerland
Amirhossein Mostajabi1, Declan L. Finney2, Marcos Rubinstein3, Farhad Rachidi1

## Slide 2: Outline
Data
Training
Model
Prediction
Challenge of Identifying the outliers
  Influence on the model’s performance
  Possible approaches to optimize the process
Forming the database
  12 stations in Switzerland
  Gathering the data points and labeling criterion
  Data visualization
Algorithm workflow
  Data preparation
  Training
  Evaluation metrics
  Prediction results

## Slide 3: Selected sites
12 meteorological stations in Switzerland
Area of interest
r = 30 km
Meteorological station

## Slide 4: Database
[Period of gathering data: 2006-2017]
Time Stamp in UTC
Meteorological features
(mean value in 10 min)
End of the 10 minute time intervals
.
.
.
Electric field
(maximum value in 10 min)
Any activity in 30 km (from LLS)
Only available at Säntis station
Used as a competitive baseline
Area of interest
r = 30 km
Notes: The database consists of around 7 million data, each includes values for 4 meteorological features in 10-min intervals.

## Slide 5: Data visualization
Säntis and Monte San Salvatore
[2006-2017]
Lightning activity: “Yes”
Lightning activity: “No”

## Slide 6: Parallel coordinate plot
Luzern
[2006-2017]
Lightning activity: “Yes”
Lightning activity: “No”

## Slide 7
Hits
Misses
Correct rejections
False Alarms
Target=0
Target=1
Output=1
Target=1
Output=0
Target=0
Output=0
Output=1
Hits
Misses
Correct rejections
False Alarms
Target=0
Target=1
Output=1
Target=1
Output=0
Target=0
Output=0
Output=1
Feeding the model with Data Part 1 and evaluating the results using 4-fold CV
2
Partitioning data at each station into
Data Part 1 (2006-2009) and Data Part 2 (2010-2017)
1
Algorithm

## Slide 8: Training the model
XGBoost algorithm
Illustration is adopted from https://blog.quantinsti.com/xgboost-python/.
Notes: Illustration is adopted from https://blog.quantinsti.com/xgboost-python/
Xgboost stands for eXtreme Gradient Boosting and is developed on the framework of gradient boosting.
The sequential ensemble methods, also known as “boosting”, creates a sequence of models that attempt to correct the mistakes of the models before them in the sequence. The first model is built on training data, the second model improves the first model, the third model improves the second, and so on.
In the example image above, the train dataset is passed to the classifier 1. The yellow background indicates that the classifier predicted hyphen and the blue background indicates that it predicted plus. The classifier 1 model incorrectly predicts two hyphens and one plus. These are highlighted with a circle. The weights of these incorrectly predicted data points are increased and sent to the next classifier. That is, to classifier 2. The classifier 2 correctly predicts the two hyphens that classifier 1 was not able to classify. But classifier 2 also makes some other errors. This process continues and we have a combined final classifier which predicts all the data points correctly.

## Slide 9
Re-labeling the data in Data Part 1 based on the evaluation results as either “accepted” or “rejected” and training another model (i.e., detector)
Feeding Data Part 2 into the ”detector”
3
Chart: 
| Accepted | Rejected
Data Part 2 | 85 | 15
4

## Slide 10
Repeating steps 2-5 many times and calculating the similarity score for each execution
6
Comparing the distribution of rejected samples in both, Data Parts 1 and 2, and trying to fit the two distributions
5
Air pressure
Air temperature
Relative humidity
Wind speed
month
Final evaluation of the ML model using 8-fold cross validation using Data Part 2
8
Selecting the data corresponding to the execution with the highest similarity score
7
Distribution of rejected
Samples at Data Part 1
Distribution of rejected
Samples at Data Part 2

## Slide 11: Model evaluation results using Data Part 2
Säntis station
Evaluation metrics
3 competitive
baselines
The CAPE model uses a threshold of Convective Available Potential Energy (CAPE) to assess the risk of lightning.
The electrostatic field method (the E-FIELD model) is based on detecting when the vertical electrostatic field (E(z)) exceeds a specific threshold to issue the warning.
To generate forecasts based on the data, the PERSISTENCE model assumes that in every 10-min interval, the forecast is the same as the observation in the previous interval.
Notes: Evaluation of the skill of warnings of long-range lightning activity for one of the lead time ranges Säntis station. The results from ML model are shown as solid black columns, results from PERSISTENT model are shown as columns filled with dot patterns, results from CAPE model are shown as columns filled with vertical lines, and results from E-FIELD model are shown as solid gray columns (POD: Probability of Detection, FAR: False Alarm Ratio, CSI: Critical Success Index, HSS: Heidke Skill Score)

## Slide 12: Model evaluation results for Data Part 2
Säntis and Monte San Salvatore
[Three lead time ranges]
Similar performance was obtained for different lead times and different locations.
Notes: Evaluation of the skill of warnings of long-range lightning activity for three ranges of lead times at a, b, c Säntis (Subset 1) and a′, b′, c′ Monte San Salvatore (Subset 2) station. The results from ML model are shown as solid black columns, results from PERSISTENT model are shown as columns filled with dot patterns, results from CAPE model are shown as columns filled with vertical lines, and results from E-FIELD model are shown as solid gray columns (POD: Probability of Detection, FAR: False Alarm Ratio, CSI: Critical Success Index, HSS: Heidke Skill Score)

## Slide 13: Distribution pattern of positive samples
Group A and B
[2006-2017]

## Slide 14: Distribution pattern of the positive class
PDF and PCA analysis
[2006-2017]
PDF analysis
PCA analysis

## Slide 15
The challenge of identifying the outliers
Different executions might lead to different results
Chart: 
| Correct | Misclassified | Unknown
Data Part 2 | 85 | 10 | 7.5
The final evaluation is done only on the accepted samples
The unknown section is not considered either in the training or the testing stage
The portion of each class in the “unknown” category is important

## Slide 16
Possible approaches to optimize the process
Including more input parameters:
  Temporal (month, day, hour)
  Atmospheric (dew point, precipitation, cloud coverage, …)
  Lightning (previous records of lightning activity)
Limiting the portion of lightning-active and lightning-inactive samples inside the rejected subset.
Simultaneous training of the main model and the detector to reduce the number of rejected samples
Trying time series algorithms to take into account the changes in the information from previous time steps

## Slide 17
Results for approach 1: extending the input parameters
Initial input parameters
Air pressure
Air temperature
Wind speed
Relative humidity
1. Adding more parameters
Hour
Day
Month
Previous lightning record
2. Optimizing the hyperparameters
Advantages
No detector is required anymore.
Fast online inference is possible.
Precision = 70 %
Recall = 63 %
Persistence
Lead time= 20-30 min
Recall
Precision
0 %
100 %
0 %
100 %
Precision = 72 %
Recall = 70 %
Lead time= 10-20 min
Recall
Precision
0 %
100 %
0 %
100 %
Persistence
Precision = 81 %
Recall = 78 %
Lead time= 0-10 min
Recall
Precision
0 %
100 %
0 %
100 %
Persistence
Recall = POD
Precision= 100%-FAR