## Slide 1: Air Pollution and its potential climate effect in Delhi, India
Presenter: Ying Chen
Lancaster Environment Centre
Email: y.chen65@lancaster.ac.uk
Luke Conibear, Yu Wang, Liang Ran, Jianjun He, Lina Wang, Oliver Wild
EGU2020-223 D3110

## Slide 2: Outline
PM2.5 pollution in Delhi (health impact)
What is unique of PM2.5 in Delhi? (climate impact)
Summary

## Slide 3: Air Quality in Delhi
2018 Diwali
India: 9 out of top-10 most polluted cities in the World
Delhi: ranking at 6th according to WHO
~11K mortality in Delhi (Chowdhury et al., 2016)
~ 1M mortality over India (Luke et al., 2018)
Source: www.urbanupdate.in & www.ndtv.com

## Slide 4
Air Quality in Delhi
Global Pop.-weighted
Chinese City-level
Beijing
Delhi
MODIS image
Delhi

## Slide 5
Representativeness of Obs@US Embassy

## Slide 6
Representativeness of Obs@US Embassy
Source: Chen et al., 2020 AEX

## Slide 7
How bad is PM2.5 in Delhi
95%
5%
Mean
Median
75%
25%
Source: Chen et al., 2020 AEX

## Slide 8
How bad is PM2.5 in Delhi
Weekdays = Weekend
Winter > Post-monsoon (Autumn) > Pre-monsoon (Summer) > Monsoon
Shift morning peak from 8-9am (Summer) to 10am (Winter)
Source: Chen et al., 2020 AEX

## Slide 9
How bad is PM2.5 in Delhi
Diwali Fest
New Year Fest
Monthly: 180 µg/m3
Diwali: 320 µg/m3
short-term exposure: ~22 person/day
Healthy
Unhealthy
Source: Chen et al., 2020 AEX

## Slide 10
How bad is PM2.5 in Delhi
255 days/year
Source: Chen et al., 2020 AEX

## Slide 11
Where does PM2.5 come from?
Source: Dr. Mukesh Sharma@IIT-Kanpur
Local Sources
Regional Transport
Combination of local and regional sources (NCR).
However, not transport from too far (unless dust storm), since faster windspeed lower PM2.5
Road Dust

## Slide 12: Outline
PM2.5 pollution in Delhi (health impact)
What is unique of PM2.5 in Delhi? (climate impact)
Summary

## Slide 13
Physical Property: Hygroscopicity
RH increase and water uptake
Cloud activation:
Indirect radiative forcing
Hydrologic cycle
Wet scavenging
…
Source: Chen et al. (2018)
Hygroscopic growth:
Direct radiative forcing
Lower visibility
Fasten heteo. reactions
Deposition rate
Influence obs. directly
…

## Slide 14
High hygroscopicity (κchem) and RH  Bigger size  larger light scattering  lower visibility
Physical Property: Hygroscopicity
κchem:
indicator of hygroscopicity of chemical components mixtures
hygroscopicity  κ-kӧhler + Mie Theories  retrieve -- Key parameters (Meteo., PM2.5 and Vis.)
Water
Water uptake  visibility
Visible light scattering
Wang, Y., and Chen, Y.*: Hygroscopicity in Delhi, GRL (2019)

## Slide 15
Source: Mukherjee and Toohey, 2016
Check retrieve method with Beijing data: good agreement
κchem bias of 0.01-0.04 (~5-30%), compare with 9-month direct measurements
Physical Property: Hygroscopicity
Study in Beijing

## Slide 16
Physical Property: Hygroscopicity
Wang, Y., and Chen, Y.*: Hygroscopicity in Delhi, GRL (2019)

## Slide 17
Physical Property: Hygroscopicity
Examples of κchem values:
Dust = 0
Organics = 0.1-0.3
Beijing = 0.20
Delhi = 0.42
Sulfate/Nitrate = 0.67
Sea-salt = 1.2
Source: Petters and Kreidenweis, (2007)
Wang, Y., and Chen, Y.*: Hygroscopicity in Delhi, GRL (2019)

## Slide 18: Summary
Pollution:
Severe PM2.5 in Delhi, with annual ave. ~110 µg/m3, much worse than Beijing
About 70% of citizens’ lifetime expose to an unhealthy PM2.5 condition, cause more than 10k mortality per year
Diwali Fest (fireworks) increase ave. PM2.5 from 180 µg/m3 to 320 µg/m3, leads to extra 22 person/day mortality
Climate:
Higher hygroscopicity in Delhi (κchem=0.42) than in Beijing and Asian ave. (κchem=0.2)
Higher light scattering enhancement and cloud activation, leads to more important DRF/IRF on climate
(Chen Y., et al., 10.1016/j.aeaoa.2019.100052, 2020)
(Wang, Y., and Chen, Y, 10.1029/2019GL082339, 2019)

## Slide 19
Acknowledgements:
I would like to thanks the contributions from Luke Conibear, Yu Wang, Liang Ran, Jianjun He, Lina Wang, Oliver Wild.
This work is funded by NERC DelhiFlux (NE/P01531X/1) projects. The archived hourly measurements of PM2.5 recorded at the U.S. Embassy in Delhi are available through the AirNow platform maintained by the U.S. Department of State and the U.S. Environmental Protection Agency at https://www.airnow.gov/. The archived meteorology variables recorded are available through the Integrated Surface Database—Surface Data Hourly Global data product maintained by the U.S. National Oceanic and Atmospheric Administration—National Climatic Data Center at https://www.ncdc.noaa.gov/.

## Slide 20
References:
Chen Y., et al., Local characteristics of and exposure to fine particulate matter (PM2.5) in four indian megacities, 10.1016/j.aeaoa.2019.100052, 2020.
Chen Y., et al., Influence of cutoff shift on aerosol measurements, https://doi.org/10.1016/j.atmosenv.2018.09.049, Atmospheric Environment, (2018).
Wang, Y., and Chen, Y.*: Significant Climate Impact of Highly Hygroscopic Atmospheric Aerosols in Delhi, India, Geophysical Research Letters, 0, 10.1029/2019GL082339, 2019.
Chowdhury, S. & Dey, S., Environment International 91, 283-290, doi:https://doi.org/10.1016/j.envint.2016.03.004 (2016).
Conibear, L., Butt, E. W., Knote, C., Arnold, S. R. & Spracklen, D. V., Nature Communications 9, 617, doi:10.1038/s41467-018-02986-7 (2018).
CPCB, National Ambient Air Quality Standards, Central Pollution Control Board, New Delhi, India, (2009).
CPCB, National Air Quality Index Report, Central Pollution Control Board, New Delhi, India, (2014).
Mukherjee, A., and Toohey, D. W.:, Earth's Future, 4, 381-395, doi:10.1002/2016EF000367, (2016).
Titos, G., et al., Atmospheric Environment, 141, 494-507, https://doi.org/10.1016/j.atmosenv.2016.07.021, (2016).
Pringle, K. J., et al., Atmos. Chem. Phys., 10, 5241-5255, 10.5194/acp-10-5241-2010, (2010).
Petters, M. D., and Kreidenweis, S. M.:, Atmos. Chem. Phys., 7, 1961-1971, 10.5194/acp-7-1961-2007, (2007).
Sharma, S. K., et al., Bulletin of Environmental Contamination and Toxicology, 100, 695-701, 10.1007/s00128-018-2313-9, (2018).
Huang et al., Nature, 10.1038/nature13774, (2014).

## Slide 21
Thank you for your attention !