## Slide 1
Likely and high-end impacts of regional sea-level rise on the erosion of European sandy coasts under high greenhouse gas emissions scenario
Rémi Thiéblemont1, Gonéri Le Cozannet1, Alex Toimil2, Benoît Meyssignac3 & Iñigo Losada2
1BRGM – French Geological Survey
2IH-Cantabria
3LEGOS - CNES/CNRS
http://www.le-ptit-train.com/environnement.htm#gallery-5
EGU VIRTUAL MEETING
MAY. 7th 2020

## Slide 2: INTRODUCTION
What is the impact of high-end sea-level projections on the retreat of European shoreline ?
Global sea-level projections
2100
2050
2000
0.0
0.5
1.0
1.5
RCP8.5
RCP2.6
Global Mean Sea-Level (m)
0.3 m
1.1 m
High-end scenarios
(e.g. Stammer et al., 2019)
SROCC, 2019
2

## Slide 3: WORKFLOW
Relative Sea-Level Change
EUROSION Coastal Geomorphology
Sandy Shoreline Change Projections at European Scale
Bruun Rule*
SLR-induced Shoreline Retreat Model
3 scenarios :
RCP8.5
High-End A (83rd of RCP8.5)
High-End B (worst model)
2 approaches:
1% constant slope
Deltares global slope dataset (Athanasiou et al., 2019)
3
Identifying sandy coast segments (~25% of total length)
*controversial, but delivers larger erosion impacts than the alternative PCR model (Ranasinghe et al., 2011)
Notes: Say orally how much of sandy coast segments

## Slide 4: SEA-LEVEL PROJECTIONS & BEACH SLOPES
RSLR projections (2100 minus 1986-2005)
High-End B – Worst model case
ΔRSLCRCP8.5-med > 0.7 m
ΔRSLCHigh-end-B > 1.7 m
Slope (%)
Baltic
North Sea
Atlantic
Med. Sea
B. S
Median Nearshore Slope/Country
4

## Slide 5: RESULTS
5
Shoreline changes per country in 2100 – 1% slope case
Baltic Countries overall less impacted due to the GIA influence
The relative contribution of the different components to regional SLR varies with scenarios => source of uncertainty in future projections.

## Slide 6: RESULTS
6
Larger shoreline retreats are projected for Europe when variations in nearshore slope are considered.
Accounting for nearshore slopes leads to large regional variability
Larger projected erosion in Northern Europe than Southern Europe, particularly under high-end scenarios,
Shoreline changes per country in 2100 – (Deltares-1%) slope case