## Slide 1: Seasonal streamflow forecasts fostering hydro power cascade operation applying the Adaptive Policy Search (APS) framework
Christoph Libisch-Lehner
Harald Kling
Martin Fuchs
Hans-Peter Nachtnebel

## Slide 2: Table of Contents
Case Study
Research Question & Experimental Setup
Methods
Results
Discussion
Summary & Outlook

## Slide 3: Case Study Drin River‘s Hydro Power Cascade
1
Backbone of Albania’s energy system with a total installed capacity of 1,350 MW
consists of three reservoirs:
main purpose is hydro power generation in a non-liberalized market
serves also as flood control for downstream river reaches
Reservoir | Active storage [hm³] | Turbine flow [m³/s] | Rated power [MW] | Basin [km²] | Mean inflow [m³/s]
Fierza | 1860 | 494 | 500 | 12,194 | 178
Komani | 111 | 736 | 600 | 13,692 | 96
Vau I Dejes | 151 | 565 | 250 | 14,029 | 27
  Observed Inflows:
  Map overview:

## Slide 4: Research Question and Experimental Setup
2
Opportunities: What is the value of adopted reservoir operation policies based on inflow predictions compared to pre-optimized policies?
Adaption: How and when react the policies to new information?
Challenges: Does it work all the time?
Three experiments
Deterministic: inflows are known  benchmark experiment
Robust optimization: (i) operating policy is pre-optimized based on stochastic inflow replicates and (ii) simulated over historic inflows
Rolling horizon: (i) policy, derived in 2., serves as in initial policy, whose parameters are (ii) periodically re-optimized based on inflow predictions

## Slide 5: Methods Direct Policy Search (DPS)
3
Machine Learning Approach
Three main components:
  Numerical model of the Reservoir Cascade System (daily time steps)
  Operating Policy, expressed as Radial-Basis-Function-Network with 3 inputs, 5 hidden nodes and 1 output:
    * Downstream reservoirs are operated as run-off-river power plants
  Evolutionary Algorithm (i.e., NSGA2)
Robust Optimization:
  Accounts for uncertainty of the problem by means of ensembles and by certain measures of robustness
  Inflow ensembles derived by (i) Stochastic Streamflow Generator or (ii) inflow predictions
  DPS - Framework
  Case Study specific Objectives and Constraints:
  Objective: maximization of revenues over simulation period
  Constraints:
    c1: Fierza reservoir is not allowed to be tapped, meaning that the water balance is balanced over one year of operation
    c2: Fierza water level is not allowed to be in the flood zone at any time
I

## Slide 6: Methods Adaptive Policy Search (APS)
3
Derivative of Direct Policy Search
Re-optimization takes place on every 1st and 15th of a month
Parameterset of the initial policy is re-optimized based on new information about the system state:
  Actual Water Level (controlled)
  Hydrological system state (uncontrolled)
Final parameterset of the previous step serves as an intial parameterset for the re-optimization
Hydrological predictions are derived by ”Ensemble Streamflow Prediction” method
Ensemble Streamflow Prediction
fixed energy prices
Water level predictions
Release predictions
observations
  APS: Rolling Horizon Model
Flood zone
Flood zone

## Slide 7
3
Inflow prediction method that relies on:
  calibrated hydrological model (i.e., COSERO)
  historical meteorological data (i.e., observed pairs of temperature and precipitation)
No meteorological forecasts are used
Predictions are corrected by an AR1-output correction model
Long-term skill is acceptable during the melting period, since COSERO models the current hydrological system state (e.g., snow)
Methods Ensemble Streamflow Prediction (ESP)
  Streamflow prediction: schematic description
AR1-model
correction
Input
Output
COSERO

## Slide 8: Results DPS vs. APS: Objective Function
4
Annual revenues strictly follow the inflow conditions
Mean annual revenues can be significantly improved by 1.1 %
Bootstrapping the difference for different sets:
  APS improves the revenues in more than 95 %
  improvement is more reliable during dry years
  during wet years it is possible that the revenues are decreased (due to lower heads)
experiment | mean annual revenue [Mio €] | percentage of deterministic
deterministic | 192.3 | -
DPS | 186.2 | 97 %
APS | 188.3 | 98 %
  Annual revenue streams from 3 experiments:
  * in 2006, both DPS and APS outperform the deterministic experiment due to constraint violations (compare next slide)
  Bootstrapping the difference of APS and DPS
  * total repetitions: 10,000

## Slide 9: Results DPS vs. APS: Constraint Violations
4
Constraints are soft-constraints (i.e., it is physically possible to violate them)
Deterministic experiment almost never violates constraints
DPS fullfills the end-storage constraint, but often fails in terms of the flood-constraint
APS slightly fails in terms of the end-storage constraint, but clearly outperfoms DPS in terms of the flood constraint:
Naturally, the effect during wet years is higher than during dry years
  Annual revenue streams from 3 experiments:
  * First panel: shows the end-storage of each year, which must be greater or equal than the start storage. * Second panel: ﬂood constraint and counts the days where the water level touches the ﬂood storage – the number of days should be 0.
  * in 2003, each experiment violates the flood constraint due to high inflows at the beginning of the year
  * in 2010, APS reduces the the ﬂood constraint by 62 days compared to DPS
  Bootstrapping the difference of APS and DPS
  * total repetitions: 10,000
experiment | annual average of days where the water level is in the flood zone | reduction
DPS | 18 | -
APS | 5 | - 72 %

## Slide 10: Results Parameter Changes
4
The final parameter set of the previous optimization step serves as a starting population
Naturally, there are only changes if the optimization problem is better solved (i.e., increased objective function or less constraint violations)
The temporal change of the parameter set can be monitored:
  changes of Node 2 parameters are very pronounced, whereas the others behave rather smooth
  changes are pronounced at the beginning of the year and after the dry season (i.e., September – Decmeber)
The changes are comprehensible, because:
  Node 2 is not active at the initial parameter set (compare slide 16)
  The first two optimization steps are considered as a warming-up phase
  Inflow predictions are skillful from March – August, while the rainy season cannot be well predicted: operating policy as to be adjusted according to new information and, thus, parameters are changed.
absolute changes in the parameters are calculated, such as:
  Parameter set consists of 35 parameters (7 per Node):

## Slide 11: Discussion Radial Basis Function Network
5
It is well known, that RBFN’s are good in interpolation but what about extrapolation in case of unobserved states?
RBFN’s are trained for the “most important” or “most representative” states of the system – but what about about less frequent but critical states?
RBFN’s are black boxes: we need to open them
Input-Response Functions
  for all combination of inputs (i.e., cos(t), S(t) and price(t)) the outputs (i.e. release decisions)
  shows the full state-action space
  RBFN interpolates within and extrapolates for unobserved states
A qualitative assessment by an expert is possible
The reported “instabilities” require regular updates of the parameter set  APS
  Input-Response function:
  derived from robust optimization experiment and trained on stochastic replicates
  serves as an initial policy for the APS rolling horizon
  16,024,008 points (based on storage discretization)
  Filtered Input-Response function:
  observed states within the last optimization run
  84,826 points, which is considerably less
  Qualitative assessment:
    No storage below 0.64 was observed in the ﬁnal run and, thus no releases are suggested below this threshold
    Three peaks, at 0.7, 0.8 and 0.99 of the active storage are observed. This structure can be explained by looking at the right, figure which shows the distribution of observed water levels in the ﬁnal optimization run.
    On this basis, the drop in the input-response-function can be explained, but is it really justiﬁed?

## Slide 12: Summary
6
Opportunities: Improved reservoir operation in terms of increased revenues at lower flood risk In an operational context: in case inflow predictions fail for a short time, the reservoir can be operated with the rule optimized the day before
Adaption: Parameters are changing if predictions are struggling, or if constraint violations are imminent
Challenges: In case inflow predictions are misleading, adopted policies are misguided accordingly
Outlook
More frequently re-optimized policy (i.e., daily)
first results are promising:
experiment | revenues 1st Nov – 31st Dec 2016 [Mio €] | max. water level [m.asl]
DPS | 50.7 | 292.5
APS | 49.7 | 289.2
APS daily | 51.2 | 289.6
7

## Slide 14: Adendum Stochastic Streamflow Generator
8
challenges:
  3 reservoirs with natural inflows (cross-correlation)
  daily timestep
simple approach:

## Slide 15: Adendum AR1-Output Correction
8
The output correction is based on the comparison between simulated and observed discharge at the last available observation value:
the forecasted error εt is calculated from the last observed error and an autoregressive coefﬁcient rQ, which depends on a corresponding inﬂow class.

## Slide 16: Adendum Input-Response-Function
8
Opening of the Radial-Basis-Functions
Input-Response-Function of each Node
gives valuable insights
Node 2 is not active in the initial parameter set