## Slide 1: Future water supply and Demand in the Peruvian Andes: Assessment and implications
Professor Andrew Wade (University of Reading, UK)
Geography and Environmental Science

## Slide 2: Overview
Aim: to understand how climate change will impact water availability, farming (lives and livelihoods) and local communities in the Peruvian Andes – (as a precursor to understanding adaptation)
Based on water balance, ethnographic and archaeological study
Detailed, nuanced study of four catchments and their communities
Present-day water gap in Rio Ancash determined
Future demand assessed
Next step: to assess future water availability (melt, lake release)
Cordillera Blanca
Cordillera Negra

## Slide 3: Co-authors
Dr Harvey Rodda (Hydro-GIS Ltd, UK)
Professor Nick Branch (University of Reading, UK)
Marcos Bruzzone (Water Resource Associates, UK)
Dr Alex Herrera ( Universidad de los Andes - Colombia)
Dr Francisco Araujo-Ferreria (University of Reading, UK)
Dr Frank Meddens (Pre-Construct Archaeology Ltd, UK)
Douglas Walsh (Asociación Andina Cusichaca, Peru)
Dr Kevin Lane (Universidad de Buenos Aires, Argentina)

## Slide 4: AIM
To understand how climate change will impact water availability, farming (lives and livelihoods) and local communities in the Peruvian Andes – (as a precursor to understanding adaptation)
Cordillera Blanca
Cordillera Negra

## Slide 5: Study areas
Rio Ancash
Rio Llullán
Chorrillos Valley
Pamparomas

## Slide 6
Rio Ancash

## Slide 7: Variation in Precipitation
SENAHMI. Data from 01.09.1995 to 31.08.2014

## Slide 8: Research questions
Is there sufficient water to sustain farming presently in the:
  wet season?
  dry season?
How will the water supply and demand change in the future (next 100-200 years), and what will the impact be on lives and livelihoods?
Can adaptation strategies be co-developed with local communities to address water availability (and quality) issues?

## Slide 9: Methodology
Asses water supply
  Precipitation
  River and lake outflows
  Irrigation flow (modern and ancient)
  Groundwater (springs), Wetlands (store and release)
  Done by flow gauging and isotopes, and historic data collation
Asses water demand
  Cropwat
  Done through crop area and cropping pattern assessment
  Collation of weather data
Iterative procedure to discuss findings with local communities, both from water balance study but also other challenges highlighted by ethnographic study, and co-develop adaptation strategies.

## Slide 10: Assessing Supply

## Slide 11: Flow gauging – Irrigation Canals
Llanganuco irrigation canal – Photos: Frank Meddens
Velocity-area gauging

## Slide 12: Flow gauging – RIO AnCASH
Rio Ancash– Photo: Frank Meddens
Dilution gauging

## Slide 13: Assessing DEMAND

## Slide 14: CROPWAT
Dry season irrigation requirements
Inputs
  Precipitation
  Air temperature
  Sunshine hours
  Relative humidity
  Wind speed
Crop and crop co-efficients
Soil moisture and infiltration
Crop water demand

## Slide 15: Preliminary results
Chart: CROPWAT Results
| Barley | Carrots | Chocho Beans | Flowers | Maize | Ollucos | Onions | Peas | Potatoes
Water use | 254.6667 | 395 | 187.0333 | 282.7333 | 262.8 | 300.1667 | 148.4667 | 231.3667 | 300.1667
Effective Rainfall | 12.9 | 16.2 | 11.8 | 12.9 | 12.8667 | 13 | 11.8 | 12 | 13
Irrigation Requirement | 241.8 | 379 | 175.2333 | 269.9 | 250 | 287.7667 | 136.9333 | 219.5 | 287.7667

## Slide 16: Preliminary results
Catchment | Area (km2) | Crop Area (km2) | Total Crop Water Requirement (m3/day) | Maximum Available Irrigation Water (m3/day)
Present day | 137.5 | 26.2 | 48,900 | 30,900
Climate change | 137.5 | 26.2 | 52,160 | To be determined in next phase

## Slide 17: Conclusions
Precipitation (wet season) and inundation irrigation are main ways to supply crops with water
Groundwater/springs and seeps from wetlands are used, but these sources are very localised
There is a water gap in the Rio Ancash in the dry period, as the crop water demand is only partially satisfied by the available irrigation water.
The CROPWAT Climate Change simulation in the Rio Ancash shows an increase in effective rainfall but this does not off set the larger increase in crop water requirements due to higher air temperatures, so irrigation requirements will become higher.

## Slide 18: Next steps
Complete present-day water balance, and that under climate change
Consider different climate change scenarios and climate variability
Merge results with those from ethnography work to nuance understanding of key challenges.
Consider how glacial melt and lake levels will change over time, and the impact on water availability
Explore the water quality data collected
Under a new, follow-on project called CROPP led by Joy Singarayer (Reading) consider climate variability further, impacts on montane biodiversity, and further integrate hydrological and ethnographic research.