## Slide 1: Reservoir Response to Heat Generating Nuclear Waste in Bedded Salt
Richard S. Jayne
Presented by:
EGU 2020 Virtual Meeting
Monday 4 May 2020

## Slide 2: Brine Availability Test in Salt (BATS) Team
Sandia National Laboratories (SNL)
Kris Kuhlman, Melissa Mills, Rick Jayne, Courtney Herrick, Ed Matteo, Charles Choens, Martin Nemer, Yongliang Xiong, Jason Heath
Los Alamos National Laboratory (LANL)
Phil Stauffer, Hakim Boukhalfa, Eric Guiltinan, Thom Rahn, Doug Ware
WIPP Test Coordination Office (TCO), LANL
Doug Weaver, Brian Dozier, Shawn Otto
Lawrence Berkeley National Laboratory (LBNL)
Yuxin Wu, Jonny Rutqvist, Mengsu Hu

## Slide 3: Brine Availability Test in Salt (BATS)
BATS Goal:
  Monitoring brine distribution, inflow, and chemistry from heated salt using geophysical methods and direct liquid & gas sampling
Why Salt?
  Salt long-term (104 – 106 yrs.) benefits at km-scale
    Low porosity and permeability
    High thermal conductivity
    No flowing groundwater
    Creep closure
Salt Complexities
  Brine and salt are corrosive
  Evaporites are very soluble in water
  Salt creep requires drift maintenance
  Excavation Damaged Zone (EDZ)
Borns & Stormont (1988)

## Slide 4: Background on Brine in Salt
Water types in bedded salt
  Disseminated clay ( vol-% total; vol-% brine)
  Intragranular brine (fluid inclusions; vol-%)
  Hydrous minerals (e.g., polyhalite, bischofite, epsomite)
  Intergranular brine (between salt crystals; vol-%)
These water types:
  respond differently to heat & pressure
  have varying chemical composition
  differ in stable water isotope makeup
EDZ increases intergranular → primary flow path
Q: How do water types contribute to Brine Availability?
Polyhalite
Intergranular
Fractures
10.1 cm diameter core CT data (Betters et al., 2020)
Clay
Fluid
Inclusions
WIPP fluid inclusions, 2 mm scale bar
(Caporuscio et al., 2013)

## Slide 5: Questions BATS Experiment Seeks to Answer
Understand and predict THMC processes impacting brine availability
  How much of each water type in bedded salt?
  Water response to pressure (), stress (), and temperature ()?
  How does EDZ control migration of water (, , relative perm. )?
  How does EDZ evolve with , , and ?
  Is two-phase flow in EDZ important for predictions?
  How to best simulate brine pulse after heating?
OBJECTIVE: Utilize PFLOTRAN and TOUGH numerical modeling codes to match the most recent heating/cooling cycle at WIPP.

## Slide 6: Waste Isolation Pilot Plant (WIPP) Context
Small-scale
Brine inflow (1992)
BATS (2020)
Small-scale
Mine-by (1991)
650 m depth
500 ft (152 m)
scale bar
Layout of WIPP North End
⇽N

## Slide 7: BATS Experimental Setup
Heated
Unheated
(Drift layout drawing by WIPP TCO)

## Slide 8: January - March 2020 BATS Test Data
Heat on
Heat off
N2 flowrate change

## Slide 9: Utilizing 1-D Models to Match Field Test
1D radially symmetric
  121 grid cells
  1 km total model domain (0.03 – 150 m)
  DRZ 0.03 – 1.75 m
Heater in contact with salt
  air causes issues with matching field data (radiative heating)
Simulate 29 days of heating and 13
  Incorporates the on/off cycles in early time and gradual lowering of energy input
Match temperatures measured at 3 thermocouples in-plane with heater
  HE1 – TC3 – 0.4m
  HT2 – TC8 – 0.68 m
  HT1 – TC8 – 1.01 m
Cross-section central
(HP) borehole

## Slide 10: Excavation Damaged Zone (EDZ) Strongly Controls Temperature profile

## Slide 11: 3-D Modeling of Field Test
Preliminary Results/Workflow
  Well geometry  LaGriT  Voronoi
    Outputs Voronoi mesh for TOUGH and PFLOTRAN
  10 m x 10 m x 10 m
    ~650,000 grid cells
  Include open-air boreholes
Refinement around wells
VOROCRUST
  Code developed at Sandia
  Voronoi cells
  Test discretization

## Slide 12: Future Work
Can we use 1-D models to map the EDZ to incorporate into more complex 3-D models?
Constrain reservoir parameters via laboratory experiments
  Thermal conductivity vs. temperature
  Heat capacity vs. temperature
Instead of a distinct separation of the EDZ and intact salt, have reservoir parameters decay as a function of distance from borehole and drift?
Match brine inflow into borehole.
How to incorporate permeability as a function of temperature?

## Slide 13: Thank You!