## Slide 1
Defining irrigation thresholds in remote sensing-based decision support systems:
a review of crop models mechanistic descriptions of crop water stress
Dr. Massimo Tolomio
Prof. Raffaele Casa
Department of Agronomy and Forestry Sciences (DAFNE)
Tuscia University (UNITUS), Viterbo (Italy)
massimo.tolomio@unitus.it, rcasa@unitus.it
Objectives:
Reviewing water stress and irrigation scheduling methods of dynamic crop models
Assessing the potential for the use of remote and proximal sensing observations in improving model simulations
Exemplify the use of automatic irrigation scheduling of a selection of crop models
7-May-2020

## Slide 2
Biomass growth estimation:
Water driven
AQUACROP
CROPWAT
Radiation driven
DSSAT
RZWQM2
STICS
DAISY
EPIC
WOFOST (carbon driven)
Mixed
(keeping the most limiting):
APSIM
CROPSYST
Water stress estimated on
Soil Water content
AQUACROP
CROPWAT
WOFOST
ET deficit
DSSAT
RZWQM2
CROPSYST
DAISY
EPIC
Mixed
STICS
APSIM
Water stress impacts
Canopy expansion
First stress to be triggered
Usually not considered for irrigation scheduling
Stomatal conductance (transpiration)
High impact on crop yield
Senescence
Accelerated or anticipated senescence
Biomass partitioning
Slight water stress can increase biomass allocated to reproductive organs
A simplified categorization:
Defining irrigation thresholds in remote sensing-based decision support systems: a review of crop models mechanistic descriptions of crop water stress
7-May-2020

## Slide 3
MODELS PRESENTED
AQUACROP http://www.fao.org/aquacrop/en/
developed by FAO, simulates weather, crop, soil and water interaction
DSSAT https://dssat.net/
Decision Support System for Agrotechnology Transfer. Simulates growth, development and yield as a function of the soil-plant-atmosphere dynamics. Includes nutrient cycling and crop management. Has inherited CERES crop modules.
RZWQM2 https://www.ars.usda.gov/plains-area/fort-collins-co/center-for-agricultural-resources- research/rangeland-resources-systems-research/docs/system/rzwqm/
Root Zone Water Quality Model 2. Simulates the growth of the plant and the movement of water, nutrients and pesticides over, within and below the crop root zone of a unit area. Has inherited DSSAT crop modules.
STICS https://www6.paca.inrae.fr/stics_eng/
Simulateur mulTIdisciplinaire pour les Cultures Standard. Simulates the soil-crop-atmosphere system, including plant, water and nitrogen modules.
Defining irrigation thresholds in remote sensing-based decision support systems: a review of crop models mechanistic descriptions of crop water stress
7-May-2020

## Slide 4
Calcinato (northern Italy)
Maize
May – September 2016
Sandy – Loam soil
Surface Irrigation
Capitanata (southern Italy)
Tomato
May – September 2016
Silty – Clay soil
Drip Irrigation
With basic data:
Tmin, Tmax, solar radiation
Soil class
Planting and harvest date
Potential of remote and proximal sensing (RS) data for improving simulations (parameterization):
LAI
Soil Water in the topsoil (SW)
Actual evapotranspiration (ETa)
 | Calcinato | Capitanata
Irrigation type | Surface | Drip
Irrigation nr. | 11 | 26
Avg. volume / irrigation (mm) | 117 | 16
Cumulative Irrigation (mm) | 1292 | 465
Defining irrigation thresholds in remote sensing-based decision support systems: a review of crop models mechanistic descriptions of crop water stress
7-May-2020

## Slide 5
AQUACROP adjustment of key parameters of growth, phenology and soil is made easier by the GUI. Aquacrop uses canopy cover, that can be obtained from RS or LAI.
Potentially: Aquacrop-OS (open-source version) can provide better option for optimization.
Chart: Canopy Cover (%)
Chart: Topsoil moisture (mm/mm)
AQUACROP
DSSAT
Chart: LAI
Chart: Topsoil moisture (mm/mm)
TOMATO
DSSAT phenology and growth parameters can be adjusted through the choice of the variety and using the GLUE tool (Generic Likelihood Uncertainty Estimator).
Potentially: GLUE can be extended to include more parameters.
Defining irrigation thresholds in remote sensing-based decision support systems: a review of crop models mechanistic descriptions of crop water stress
7-May-2020

## Slide 6
Chart: ETa (mm)
Chart: Topsoil moisture (mm/mm)
Chart: LAI
Some of the crop and soil RZWQM2 parameters were estimated using the built-in optimization tool (P-Est), assigning priority to crop parameters. STICS crop parameters were adjusted with the built-in LAI fitting tool.
Potentially: careful choice of the parameters to calibrate and experience with the optimization processes and tools can further improve simulations.
Chart: LAI
Chart: Topsoil moisture (mm/mm)
Chart: ETa (mm)
RZWQM2
STICS
MAIZE
Defining irrigation thresholds in remote sensing-based decision support systems: a review of crop models mechanistic descriptions of crop water stress
7-May-2020

## Slide 7
Normalized RMSE (%) |  |  |  | 
CROP | MODEL | Variable | Standard | Adjusted
TOMATO | AQUACROP | LAI | 37.6 | 15.6
 |  | Topsoil moisture (mm/mm) | 23.2 | 18.6
 | DSSAT | LAI | 92.9 | 21.3
 |  | Topsoil moisture (mm/mm) | 20.7 | 17.7
MAIZE | RZWQM2 | LAI | 94.4 | 26.4
 |  | Topsoil moisture (mm/mm) | 27.5 | 25.0
 |  | ETa (mm/day) | 29.9 | 29.5
 | STICS | LAI | 54.9 | 18.8
 |  | Topsoil moisture (mm/mm) | 47.0 | 45.8
 |  | ETa (mm/day) | 33.4 | 35.7
Dry matter Yield (kg/ha) |  |  |  | 
CROP | MODEL | Standard | Adjusted | Observed
TOMATO | AQUACROP | 6308 | 5532 | 5000
 | DSSAT | 10468 | 4713 | 5000
MAIZE | RZWQM2 | 6870 | 8955 | 9000
 | STICS | 11422 | 9886 | 9000
Straightforward parameterization with RS data greatly improved yield and LAI prediction and slightly topsoil moisture predictions, while ETa showed the greatest discrepancies.
High observed ETa fluctuations due to uncertainty in estimation and to peculiar field conditions after the application of great amounts of water with surface irrigation.
Defining irrigation thresholds in remote sensing-based decision support systems: a review of crop models mechanistic descriptions of crop water stress
7-May-2020

## Slide 8
Based on SW depletion
Triggered when a % of TAW or RAW is depleted.
TAW: Total Available Water
Soil water that plants can potentially uptake, hold between Field Capacity (FC) and Plant Wilting Point (PWP)
RAW: Readily Available Water
Portion of TAW that plants can potentially uptake without incurring in stomatal conductance stress
Tested models
AQUACROP
DSSAT
RZWQM2
Based on ET deficit
Triggered when the ratio between actual and potential ET (ETa/Etp) drops below a user-specified threshold.
Tested models
STICS
RZWQM2
Calibrated
Models
AUTOMATIC IRRIGATION SCHEDULING
Defining irrigation thresholds in remote sensing-based decision support systems: a review of crop models mechanistic descriptions of crop water stress
7-May-2020

## Slide 9
Chart: Topsoil moisture (mm/mm)
Chart: Topsoil moisture (mm/mm)
AQUACROP
% RAW depletion + refill to FC
Irrigation is triggered at user-specified RAW % depletion, to refill the root zone to FC.
In this case:
Irrigation starts at 100% RAW depletion.
DSSAT
% TAW depletion + refill to FC
Irrigation is triggered at user-specified TAW % depletion, to refill to FC the soil down to a specified depth.
In this case:
Irrigation starts at 50% TAW depletion of the 0-50 cm soil layer.
Water volumes suggested per each intervention may be too high for drip irrigation…
TOMATO
examples
SW-based thresholds
Drip irrigation
…but the user can set the irrigation volumes…
Defining irrigation thresholds in remote sensing-based decision support systems: a review of crop models mechanistic descriptions of crop water stress
7-May-2020

## Slide 10
Chart: Topsoil moisture (mm/mm)
Chart: Topsoil moisture (mm/mm)
AQUACROP
% RAW depletion + fixed amount
Irrigation is still triggered at user-specified RAW % depletion.
In this case:
Irrigation starts at 100% RAW depletion.
DSSAT
% TAW depletion + fixed amount
Irrigation is still triggered at user-specified TAW % depletion.
In this case:
Irrigation starts at 50% TAW depletion of the 0-50 cm soil layer.
Assuming 16 mm of water applied in each intervention (the average of observed data)…
…the suggestions are more realistic.
TOMATO
examples
SW-based thresholds
Drip irrigation
Defining irrigation thresholds in remote sensing-based decision support systems: a review of crop models mechanistic descriptions of crop water stress
7-May-2020

## Slide 11
Chart: Topsoil moisture (mm/mm)
Chart: Topsoil moisture (mm/mm)
RZWQM2
ET deficit + refill to ETp
Irrigation is triggered when the ETa/Etp ratio drops below a user-defined value. Applied volume can be set to recharge up to 100% of ETp.
In this case:
Irrigation starts at 80% ETa/Etp, to recharge 100% of Etp.
STICS
ET deficit + refill to FC
Irrigation is triggered when the ETa/Etp ratio drops below a user-defined value. Applied volume is automatically set to refill SW up to FC.
In this case:
Irrigation starts at 80% ETa/Etp.
Water volumes suggested by RZWQM2 per each intervention may be too low for surface irrigation.
RZWQM2 has also the option to create a SW-based irrigation schedule (similar to DSSAT).
MAIZE
examples
ET-based thresholds
Surface irrigation
Defining irrigation thresholds in remote sensing-based decision support systems: a review of crop models mechanistic descriptions of crop water stress
7-May-2020

## Slide 12
 | AUTOMATIC IRRIGATION SCHEDULING SUMMARY |  |  |  |  | 
TOMATO | MODEL (Scheduling method) | PROD (kg/ha) | Cumulative ETa (mm) | Irrigation nr. | Cumulative Irrigation (mm) | Irr. Water Productivity (kg/m3)
 | AQUACROP (SW + refill) | 5523 | 433 | 5 | 319 | 1.76
 | DSSAT (SW + refill) | 4705 | 570 | 6 | 273 | 1.72
 | AQUACROP (SW + fixed amount) | 5491 | 432 | 15 | 240 | 2.29
 | DSSAT (SW + fixed amount) | 4675 | 560 | 16 | 256 | 1.83
 | Observed | 5000 |  | 26 | 465 | 1.08
MAIZE | RZWQM2 (ET) | 7628 | 503 | 20 | 221 | 3.46
 | STICS (ET) | 11570 | 385 | 6 | 302 | 3.83
 | Observed | 9000 |  | 11 | 1292 | 0.70
When rationally set up, all the models suggested similar schedules in terms of:
cumulative irrigation
number of interventions
irrigation water productivity
Defining irrigation thresholds in remote sensing-based decision support systems: a review of crop models mechanistic descriptions of crop water stress
7-May-2020

## Slide 13
TAKE HOME MESSAGES
Dynamic crop models helps to identify and quantify water stress effects on canopy expansion, stomatal closure, senescence and biomass partitioning as well as water stress thresholds.
Water stresses are estimated from the soil water content or from the ratio of actual to potential evapotranspiration.
Crop models and field experience help to set rational automatic irrigation schedules.
Remote and proximal sensing data help to improve model simulations, obtaining more accurate estimations of irrigation requirements and irrigation water productivity.
Defining irrigation thresholds in remote sensing-based decision support systems: a review of crop models mechanistic descriptions of crop water stress
7-May-2020

## Slide 14
THANKS FOR THE ATTENTION
Defining irrigation thresholds in remote sensing-based decision support systems: a review of crop models mechanistic descriptions of crop water stress
7-May-2020