## Slide 1
    Cristina Saceanu1, Adriana Paluszny1, Robert Zimmerman1 & Diego Mas Ivars2
    EGU General Assembly 2020
    4th May 2020
Impact of deposition borehole geometry on mechanical spalling in nuclear waste repositories
    1 Department of Earth Science and Engineering, Imperial College, London, UK
    2 Swedish Nuclear Fuel and Waste Management Company (SKB), Solna, Sweden; Division of Soil and Rock Mechanics, Royal Institute of Technology (KTH), Stockholm

## Slide 2
    1
    Spalling & Nuclear Waste Disposal
Schematic representation of a deep nuclear waste repository (SKB-TR-10-12 (2010))
Modified from Read (2004)
Spalling is a common type of rock failure that occurs at the boundaries of deep excavations, and it is usually defined as tensile failure that occurs when the tangential stress at the borehole boundary exceeds the tensile strength of the rock (Martin, 2005).
Spalling is expected to occur around the deposition boreholes in deep mined nuclear waste repositories (Martin, 2005).

## Slide 3
    2
    Modelling Approach
A damage mechanics approach is used to describe the fracture initiation process (Mazars et al., 2015).
Fracture growth is determined by stress intensity factors (SIFs), that are calculated at the fracture tips. These control the stress magnitude at the tips and determine whether or not the crack will extend at the specified tip (Thomas et al., 2020).
Failure, length, and angle criteria are evaluated to determine which fracture tips will extend, by how much, and in what direction (Thomas et al., 2020).
The simulations are conducted using a finite element-based fracture growth simulator that computes deformation in the system based on the mechanical properties of the rock (Paluszny and Matthäi, 2009).
Initial fracture surface
Propagation vectors at
different growth steps

## Slide 4
    3
    Experimental Setup
  Cone shaped
  borehole
  Wedge shaped
  borehole
  Model Properties (SKB TR-08-05 (2007))
  Circular
  borehole
  Borehole configurations
  Boundary Conditions
Rock properties | Value used
Density | 2.73 g/cm3
Young’s Modulus | 76 GPa
Poisson’s Ratio | 0.23
Uniaxial Compressive Strength | 226 MPa
Tensile Strength | 13 MPa
KIC | 3.8 MPa/m1/2
Borehole properties | 
Young’s Modulus | 10 Pa
Poisson’s Ratio | 0
KIC | 1010 MPa/m1/2

## Slide 5
    4
    Results
  Cone-shaped
  borehole
  Wedge-shaped
  borehole
  Circular
  borehole
Borehole configuration | Maximum Spalling Depth (m) | Spalling Width (°) | Total Fracture Surface Area (m2)
circular | 0.44 | 63 / 52 | 2.0
cone | 0.47 | 60 / 62 | 2.23
wedge | 0.49 | 90 / 47 | 2.46
  Perspective view
  Top view

## Slide 6
References
1. Martin, D. (2005). Preliminary assessment of potential underground stability (wedge and spalling) at Forsmark, Simpevarp and Laxemar sites. Technical report R-05-71, Svensk Karnbranslehantering AB.
6. Thomas, R.N., Paluszny, A., and Zimmerman, R.W. (2020). Growth of three-dimensional fractures, arrays, and networks in brittle rocks under tension and compression. Computers and Geotechnics, 121, 103447.
7. SKB TR-08-05 (2007). Site description of Forsmark at completion of the site investigation phase. SDM-Site Forsmark. Technical report TR-08-05, Svensk Karnbranslehantering AB.
3. Read, R. (2004). Twenty years of excavation response studies at AECL’s Underground Research Laboratory. International Journal of Rock Mechanics and Mining Sciences, 41(8), 1251-1275.
2. SKB TR-10-12 (2010). Design and production of the KBS-3 repository. Technical report TR-10-12, Svensk Karnbranslehantering AB.
5. Mazars, J., Hamon, F. and Grange, S. (2015). A new 3D damage model for concrete under monotonic, cyclic and dynamic loadings. Materials and Structures, 48(11), 3779-3793.
4. Paluszny, A. and Matthäi, S. (2009). Numerical modeling of discrete multi-crack growth applied to pattern formation in geological brittle media. International Journal of Solids and Structures, 46(18-19), 3383-3397.