## Slide 1
Assessing the operational value of short-term forecast information under climate change
Henrique Moreno Dumont Goulart1,4, Matteo Giuliani1, Jonathan Herman2, Scott Steinschneider3, Andrea Castelletti1
1 Politecnico di Milano, IT
2 University of California Davis, US
3 Cornell University, US
4 Deltares, NL

## Slide 2: Water resources management in California
Lake Oroville, 2014
Lake Oroville, 2017
Motivation:
value of inflow forecasts only assessed over historical hydroclimatic conditions
climate projections suggest increasing variability with more frequent and intense extreme events
How much will be the value of forecast information under future more variable conditions?

## Slide 3: Case study: Folsom Reservoir
Operating objectives:
Water supply
Flood protection for the city of Sacramento
97 scenarios of future inflows from a U.S. Bureau of Reclamation study in which downscaled climate data from the CMIP5 ensemble are fed into the variable infiltration capacity (VIC) model

## Slide 4: Methodology
1. Expected Value of Perfect Information | EVPI = maximum potential improvement between a perfect operating policy (assuming full knowledge of the future) and a baseline operating policy (with no forecast information) | 
2. Synthetic Forecast Generation | Synthetic inflow forecasts capture error structure of existing forecast system, i.e. NCEP daily S2S reforecasts with 3-day lead time used as input for SAC-SMA hydrologic model with degree-day snow routine | 
3. Forecast value | Forecast value = gain in performance obtained by a policy informed with the inflow forecast designed via policy tree with respect to the baseline solution | 
cost
perfect policy
baseline policy
EVPI

## Slide 5: Results: Expected Value of Perfect Information
Some discrepancies between absolute and relative values generate inconsitent perceptions of forecast value between end-users and operators, hindering forecast uptake
Absolute value:
(end-user benefit)
Relative value:
(operator benefit)
Absolute value
Relative value

## Slide 6: Results: Future forecast value
Absolute forecast value increases in the future
Relative forecast value depend on the projected climate

## Slide 7
Henrique Moreno Dumont Goulart, Matteo Giuliani, Jonathan Herman, Scott Steinschneider, Andrea Castelletti