## Slide 1
May 8, 2019
Novel robotic chamber system for the accurate and precise determination of spatio-temporal CO2 flux dynamics on heterogeneous cropland
Vaidya S, Schmidt M, Rakowski P, Verch G, Augustin J, Sommer M, Hoffmann M

## Slide 2
Introduction:
Measurement of CO2 gas exchange is crucial for the accurate assessment of terrestrial carbon (C) sink.
However, uncertainties occur by ignoring the dynamics of CO2 fluxes caused by land use management or small scale soil heterogeneity resulted due to soil erosion.
Current approaches to measure CO2 gas exchanges have limitations accounting for small scale spatial heterogeneity (eddy covariance and automatic chambers) or short-term temporal variability (manual chambers) Influences the CO2 flux estimations while determining sink and source function.
To face these challenges, we developed a novel robotic chamber system with a high temporal and spatial resolution.
The purpose is to apply in manipulation experiment for testing the land use management practices which aims to sequester additional C and bind more N in a range of soil types.

## Slide 3
Spatial resolution
Temporal resolution
Why is this work important and timely?
Manual chambers
Eddy covariance
Automatic chambers
Hypothesis:
new robotic chamber system is capable to detect:
short term temporal dynamics
Small scale spatial heterogeneity
of measured net ecosystem exchange (NEE) and derived flux components
Robotic chamber system
High temporal and high
spatial resolution
High spatial resolution
but low temporal resolution
High temporal resolution
but low spatial resolution
Spatial resolution limited to measurement
plots /also influencing the biomass
development

## Slide 4
Advantages of robotic chamber system:
High temporal and spatial resolution to demonstrate the effect of weather conditions, plant phenology, land use management and different soil properties on CO2 fluxes
Offers the possibility to carry out supplementary measurements exactly on the plots where the gas exchange measurements are made without disturbing the plant development
Additional CH4, N2O and H2O gas analyzers can be added along with CO2 gas analyzer for concurrent measurements
Act as a mobile platform and can move in 3 dimensions; x-axis (along the track), y-axis (perpendicular to track) and z-axis (moving chambers up and down)
y-axis
y-axis
x-axis
z-axis

## Slide 5
Study site and robotic chamber system
CaboZALF-D area near village of Dedelow, Uckermark region, NE Germany (53°23N, 13°47E showing 36 plots) at an area of 110×16×5 m.
(b) Three distinct soil types (RG-ca: extremely eroded, LV-ng: strongly eroded and LV-cc: non eroded)
(c) Robotic chamber system comprised of a gantry crane mounted on two tracks (110 m) transporting multiple sensors and two transparent closed chambers.

## Slide 6
CO2 concentration and auxillary measurements
CO2 concentration was measured during two months (08 July-09 September) for spring barley
The measurement frequency was 4 sec over a 7 min deployment time using two transparent chambers connected via 5 m tubes to two infrared gas analyzer
For data collection and controlling the system, a CR6 data logger and additional CDM-A116 analog multiplexer were used
Leaf area index were measured weekly till harvest and other environmental variables such as PAR, air temperatures were recorded inside and outside the chambers
Moreover, air humidity, air pressure, precipitation, wind speed and wind direction were recorded using WXT520 weather transmitter

## Slide 7
Results : Temporal Resolution
Crop senescence
Mineralization
peak
Regermination
Die off regerminated plants

## Slide 8
High cumulated Reco fluxes in non eroded
soil as compared to srongly and extremely
eroded soil
High cumulated GPP fluxes in non eroded
soil as compared to srongly and extremely
eroded soil
High cumulated NEE fluxes in non eroded
soil as compared to srongly and extremely
eroded soil
Results : Spatial Resolution
pH range
Non-eroded soil – 4.6 - 6.3
Extremely eroded soil – 7.4 - 7.6
LAI range
Non-eroded soil – 1.3-2.8
Extremely eroded soil – 1.1-1.7
Phosphorous range
Non-eroded soil – 1.3-2.2
Extremely eroded soil – 2.7-3.3
RG-ca: extremely eroded, LV-ng: strongly eroded and LV-cc: non eroded

## Slide 9
Conclusion:
The CO2 fluxes were low (only ~34% of usual seasonal amplitude), due to measuring in conditions when plants were in 1) senescence and 2) soil was dry for a long time
Despite that, we were able to demonstrate the effect of
weather conditions,
crop phenology,
landuse management and
soil properties
on the temporal and spatial dynamics of the CO2 fluxes
The results demonstrate that the novel robotic chamber system can well represent the short term temporal differences and small scale spatial heterogeneity contributing to accurate and precise determination of CO2 flux dynamics on heterogeneous cropland

## Slide 10
Acknowledgements:
The study is supported by the German Federal Ministry of Food and Agriculture (FNR Grant: 22404117) within the project “Krumensenke”
The authors would like to thank all the team members of Pfannenstiel Pro project GmbH for designing the structure of robotic chamber system, ATTEC Automation Gmbh for developing the scripts to operate the system and Nobert Bonk who ensured the continuous operation of the robotic chamber system

## Slide 11
THANK YOU !
March 2, 2019