## Slide 1
Hydro-meteorological thresholds based on synthetic dataset for improved prediction of rainfall-induced shallow landslides
Pasquale Marino1, David James Peres2, Roberto Greco1, Thom A. Bogaard3
1Dipartimento di ingegneria, Università degli Studi della Campania ‘Luigi Vanvitelli’, via Roma 9, 81031 Aversa (CE), Italy
2Department of Civil Engineering and Architecture, University of Catania, 95123 Catania, Italy
3Section Water Resources, Department of Water Management, Faculty of Civil Engineering and Geosciences, Delft University of Technology, PO Box 5048, 2600 GA, Delft, The Netherlands
Pasquale Marino1, David J. Peres2, Roberto Greco1,and Thom A. Bogaard3

## Slide 2
HIGHLIGHTS:
Hydro-meteorological thresholds show improvement in landslide forecasting, compared to the traditional and widely-used meteorological thresholds
The use of soil moisture information, either in near-surface, even more in root-zone, can enhance the capability of forecasting shallow landslides
To get datasets long enough to carry out statistical analyses, synthetic time series of rainfall and soil cover response have been generated, using a stochastic rainfall model and a physically based infiltration model.
Article title:
Marino P, Peres DJ, Cancelliere A, Greco R and Bogaard TA (2020) Soil moisture information can improve shallow landslide forecasting using the hydrometeorological threshold approach. Landslides, accepted for publication. DOI: 10.1007/s10346-020-01420-8

## Slide 3
CASE STUDIES
Cervinara (Campania, Southern Italy)
P = 325 mm in 48 hrs (15/16-12-1999)
Giampilieri (Sicily, Southern Italy)
P = 220mm in 7 hrs (1-10-2009)
The red zones represent the areas affected by debris flows triggered by a rainfall event of 325mm in 48 hours for Cervinara, and of 220mm in 7 hours
Main geotechnical and geometrical characteristics:
Test sites | Soil dry unit weight, (N m-3) | Soil effective cohesion, (kPa) | Soil effective friction angle, (°) | s | r | Ks (m-1) | Soil cover, d (m) | Slope average inclination angle, (°)
Cervinara | 6500 | 0 | 38 | 0.75 | 0.05 | 0.29 | 1.5 - 2.5 | 40
Giampilieri | 15600 | 5.7 | 37 | 0.35 | 0.045 | 0.072 | 1.5 - 2.5 | 35 - 45
Test sites |  |  |  | s | r | Ks (m-1) | Soil cover, d (m) | 
Cervinara | 6500 | 0 | 38 | 0.75 | 0.05 | 0.29 | 1.5 - 2.5 | 40
Giampilieri | 15600 | 5.7 | 37 | 0.35 | 0.045 | 0.072 | 1.5 - 2.5 | 35 - 45

## Slide 4
RAINFALL DATASET
Rain gauge | Cervinara (Campania) |  |  |  |  |  | 
Season | September | October | November | December-March | April | May-June | July-August
 (h-1) | 0.0150 | 0.00524 | 0.00257 | 0.0238 | 0.00809 | 0.00386 | 0.00900
 | 2.684 | 36.4 | 57.1 | 2.601 | 38.7 | 21.6 | 1.396
 (h-1) | 0.265 | 0.156 | 0.0167 | 0.813 | 0.123 | 0.116 | 24.5
 (h-1) | 1.411 | 57.3 | 1.430 | 0.280 | 15.5 | 8.59 | 1.231
 (hb mm-b) | 0.330 | 0.0471 | 0.450 | 0.967 | 0.186 | 0.158 | 0.268
Rain gauge | Giampilieri (Sicily) |  |  |  |  |  | 
Season | September-October |  | November | December | January-March |  | April-August
 (h-1) | 0.0212 |  | 0.00149 | 0.00319 | 0.00230 |  | -
 | 1.57 |  | 42.4 | 42.6 | 44.3 |  | -
 (h-1) | 2.12 |  | 0.00596 | 0.00988 | 0.0102 |  | -
 (h-1) | 0.840 |  | 0.941 | 0.677 | 0.721 |  | -
 (hb mm-b) | 0.463 |  | 0.693 | 1.035 | 1.134 |  | -
1000 years hourly rainfall series has been generated with the Neyman-Scott Rectangular Pulse (NSRP) model (Neyman and Scott 1958).
The parameters have been calibrated based on experimental data available: from 1st January 2001 to 31st December 2017 with time resolution of 10 minutes for the case study of Cervinara, and from 1st May 2002 to 31st December 2013 with hourly resolution for Giampilieri.
Seasonally calibrated parameters of the NSRP model of rainfall for the two test sites

## Slide 5
PHYSICALLY BASED MODEL OF INFILTRATION AND DRAINAGE PROCESSES IN THE UNSATURATED SLOPE COVER
The parameters have been assigned according to available laboratory and field observations
The modelling of the flows has been carried out using the 1D Richards’ equation (Richards 1931), implemented in HYDRUS-1D software (Šimůnek et al. 2008):
Leakage component at the soil-bedrock interface has been approximated by the following equation:

## Slide 6
DEFINITION OF RAINFALL EVENTS AND OF LANDSLIDES TRIGGERING
Factor of safety at z = 200cm 1 (infinite slope hypothesis)
Periods with at least 2.0 mm rainfall depth, preceded and followed by at least 1 day with less than 2.0 mm rainfall.
Test sites | Number of events | Critical pressure height, (m)
Cervinara | 53061 | -0.16
Giampilieri | 24492 | 0.51
Test sites | Number of events | 
Cervinara | 53061 | -0.16
Giampilieri | 24492 | 0.51

## Slide 7
METEOROLOGICAL THRESHOLDS
The power-law red lines , obtained by maximising the true skill statistic (TSS) for 1000 years long synthetic data sets, represent the thresholds separating the two classes of events.
Precipitation Intensity-Duration (I-D) landslide threshold of Cervinara (a) and of Giampilieri (b)
TSS
Indicator | Cervinara | Giampilieri
Optimal True Skill Statistic, TSS | 0.934 | 0.720
Total number of landslides, P | 42 | 231
True Alarms, P-M | 40 | 198
Missed Alarms, M | 2 | 33
False Alarms, F | 963 | 3327

## Slide 8
HYDRO-METEOROLOGICAL THRESHOLD
The optimal hydro-meteorological thresholds have been identified as power-law equations in the plane
The meteorological variable is the P-event depth
The 1st hydro variable is , 0-5 cm average soil moisture
The 2st hydro variable is , 0-100 cm average soil moisture
could be derived from remote sensing, could be obtained by sensors or modelled using remote sensing input
Cervinara
 | Cervinara |  |  |  | 
Threshold | Time lag [h] | Best TSS | N. of landslides | M | F
- H | 24 | 0.947 | 42 | 2 | 301
- H | 48 | 0.949 | 42 | 2 | 186
I - D | - | 0.934 | 42 | 2 | 963
 | Cervinara |  |  |  | 
Threshold | Time lag [h] | Best TSS | N. of landslides | M | F
 | 24 | 0.947 | 42 | 2 | 301
 | 48 | 0.949 | 42 | 2 | 186
I - D | - | 0.934 | 42 | 2 | 963
Soil Moisture Active and Passive (SMAP), NASA
TDR probes

## Slide 9
HYDRO-METEOROLOGICAL THRESHOLD
The optimal hydro-meteorological thresholds have been identified as power-law equations in the plane
The meteorological variable is the P-event depth
The 1st hydro variable is , 0-5 cm average soil moisture
The 2st hydro variable is , 0-100 cm average soil moisture
could be derived from remote sensing, could be obtained by sensors or modelled using remote sensing input
Soil Moisture Active and Passive (SMAP), NASA
TDR probes
Giampilieri
 | Giampilieri |  |  |  | 
Threshold | Time lag [h] | Best TSS | N. of landslides | M | F
- H | 48 | 0.857 | 231 | 10 | 2431
- H | 0 | 0.947 | 231 | 1 | 1170
I - D | - | 0.720 | 231 | 33 | 3327
 | Giampilieri |  |  |  | 
Threshold | Time lag [h] | Best TSS | N. of landslides | M | F
 | 48 | 0.857 | 231 | 10 | 2431
 | 0 | 0.947 | 231 | 1 | 1170
I - D | - | 0.720 | 231 | 33 | 3327

## Slide 10
EFFECTS OF UNCERTAINTY IN SOIL MOISTURE INFORMATION
Cervinara
Giampilieri
The soil moisture data, provided by the infiltration model, have been perturbed by adding to them random errors, and the hydro-meteorological thresholds for landslide prediction have been identified, on the so obtained “non-ideal” data set, by maximization of TSS.
Error standard deviation, (m3 m-3) |  | TSS | N. of landslides | Missed Alarms | False Alarms
Cervinara |  |  |  |  | 
0 | 0 | 0.947 | 42 | 2 | 301
0.01 | 0.029 | 0.944 | 42 | 2 | 437
0.05 | 0.147 | 0.940 | 42 | 2 | 633
Giampilieri |  |  |  |  | 
0 | 0 | 0.857 | 231 | 10 | 2431
0.01 | 0.069 | 0.848 | 231 | 12 | 2435
0.05 | 0.346 | 0.687 | 231 | 28 | 4654
 |  | TSS | N. of landslides | Missed Alarms | False Alarms
Cervinara |  |  |  |  | 
0 | 0 | 0.947 | 42 | 2 | 301
0.01 | 0.029 | 0.944 | 42 | 2 | 437
0.05 | 0.147 | 0.940 | 42 | 2 | 633
Giampilieri |  |  |  |  | 
0 | 0 | 0.857 | 231 | 10 | 2431
0.01 | 0.069 | 0.848 | 231 | 12 | 2435
0.05 | 0.346 | 0.687 | 231 | 28 | 4654
The lower limit (= 0.01 m3m-3) is representative of errors of on-site TDR measurements, and the upper one (= 0.05 m3m-3) is the reported uncertainty of the currently available soil moisture retrievals from satellite radar measurements.
Soil Moisture Active and Passive (SMAP), NASA
TDR probes

## Slide 11
The results show that the improvements depend on climate, soil and geomorphologic features of the area of interest.
In the case of soils with high water storage and infiltration capacity (Cervinara case), the use of soil moisture information can significantly reduce the number of false alarms. In the case of soils with lower storage capacity and hydraulic conductivity (Giampilieri case), the improvement is even stronger, as both false alarms and missed alarms are reduced, though less robust with respect to uncertainty in soil moisture data.
This study confirms that antecedent soil moisture is an important causal, and dynamic, predisposing factor for landslide initiation, and therefore a key variable to include in shallow landslide forecasting.
Take Home Message

## Slide 12
THANK YOU FOR READING!!! FOR ANY QUESTION ASK IN CHAT
Article title:
Marino P, Peres DJ, Cancelliere A, Greco R and Bogaard TA (2020) Soil moisture information can improve shallow landslide forecasting using the hydrometeorological threshold approach. Landslides, accepted for publication. DOI: 10.1007/s10346-020-01420-8