## Slide 1
Assessment of an artificial recharge system through numerical simulations, Y. Olivares & P. Herrera
Arizona, USA
Aquifer Storage and Recovery (ASR):
1. Infiltrate water 2. Recover water
Design & operation:
low cost (A, B)
easy to build (A, B)
easy to operate (A, B)
natural filtration (A, B)
recover water (?)
FACT: Subsurface is heterogeneous
2D axisymmetric detailed numerical simulations of shallow well (B)
Question: what would be the impact of different hydro-stratigraphic units?

## Slide 2: Assessment of an artificial recharge system through numerical simulations
Yerko Olivares1 and Paulo Herrera1,2
Department of Civil Engineering, U. Técnica Federico Santa María, Chile
Deparment of Environmental Geosciences, U. Vienna, Austria

## Slide 3
Artificial Recharge (AR)
Managed Aquifer Recharge (MAR)
Aquifer Storage & Recovery (ASR)
Aquifers as reservoirs to store water
1. Infiltrate water
2. Recover water
(A)
(B)
(C)
HU 3
HU 1
HU 2
Aquifer, high K
Aquitard, low K
Design & operation:
low cost (A, B)
easy to build (A, B)
easy to operate (A, B)
natural filtration (A, B)
recover water (?)
Fact:
subsurface is heterogenous
Question:
what could be the impact of
different hydrostratigraphic
units?

## Slide 4
Arizona, USA
https://news.azpm.org/p/lastdrop/2018/8/20/135331-arizona-has-been-banking-cap-water-but-doesnt-have-a-clear-plan-to-withdraw-it/
Peru
https://agronoticias.pe/noticias/recarga-artificial-de-acuiferos-en-la-costa/
Applied since centuries in different places around the world
Modern projects have been built in recent decades to stop the decline of water levels in aquifers and/or dispose treated wastewater in different arid regions, e. g. western USA, South America, Middle East and Southeast Asia. Most of them are based on large (~1-10 km2 size) infiltration ponds.

## Slide 5
Peru
https://agronoticias.p/noticias/recarga-artificial-de-acuiferos-en-la-costa/
gravel pit
~ 60 mts
MOTIVATION:
Potential site in Santiago, Chile: heterogeneous fluvial-alluvial sediments.
Water table below 100 m depth.
Visual inspection and granulometric analyses indicate presence of quasi-horizontal hydrostratigraphic units with different characteristics.

## Slide 6
KNOWN:
K can vary by up 2-3 orders of magnitude even for homogenous sandy aquifers

## Slide 7
We performed detailed 2D (axisymmetric geometry) numerical simulations of unsaturated flow to assess the performance of an artificial recharge system composed of a single shallow well.
We consider 4 different scenarios according to the vertical sequence of 3 hydrostratigraphic units: two permeable units separated by a low permeability unit that act as a barrier (aquitard).

## Slide 8
Perched
aquifer
Injection
stops after
365 days

## Slide 9
After 1 year since injection stops, a large percentage of the injected water remains in the model domain, mainly within the initially unsaturated volume.

## Slide 10
Conclusion:
Real subsurface may be more difficult to deal with than we would like to imagine for the design of recharge systems!