## Slide 1
Drought years of 2018 and 2019 affect CO2 balance of urban forest ecosystems in the Ruhr Metropolitan Region (Germany) differently
Lutz Weihermüller
Tobias Scholz
Thomas Schmitt
Semi-natural forests
Urban greening forests
Succession forests
Let‘s start!
EGU General Assembly 2021
„Complex case studies for ecosystem responses to climate and hydrological extremes“ (BG3.17)
27.04.2021

## Slide 2
Methods & Results
Introduction
Drought years of 2018 and 2019 affect CO2 balance of urban forest ecosystems in the Ruhr Metropolitan Region (Germany) differently
Uptake
Translocation
Respiration
Study sites
Drought years 2018/2019
Conclusion
Complete balance
Research Highlights
Motivation & Objective
Methods
Results
Methods
Results
Methods
Results
Back
Implications

## Slide 3
Motivation & Objective
The history of settlement and the industrial past formed different types of temperate deciduous urban forest stands in the Ruhr Metropolitan Region in West-Germany, differing in species composition and soil characteristics:
  old-grown semi-natural forests on deep native soils,
  allochthone mixed forest stands planted in parks and on slag and slate heaps as remnants of the industrial past (urban greening forests) with limited rooting depth, and
  autochthone succession forests of birch, poplar, or willow established on industrial brownfields with loosy and coarse soils, and limited rooting depth.
CO2 balance of those forest types were investigated on eleven monitoring sites for the years 2018 and 2019, considering CO2 uptake by forest growth, CO2 translocation by litterfall, and CO2 release by soil respiration.
Both years were characterized by drought conditions, and therefore, we also studied the impact of the two years drought on CO2 balance of the different forest types.
Menu
Semi-natural forests
Urban greening forests
Succession forests

## Slide 4
Study area
Ruhr Metropolitan Region in Germany is one of the biggest agglomerations in Europe
Polycentric structure with densely populated areas, but also large amounts of green infrastructure
Area of urban forests are estimated up to 822 km² which is 23 % of total area in the agglomeration
Zoom in to study sites
Menu

## Slide 5
Investigation on CO2 balance on eleven monitoring sites
Menu
Semi-natural forests
Urban greening forests
Succession forests

## Slide 6
Semi-natural forests [click on points for site characteristics]
Menu
Old forests (> 100 a) as remnants of the traditional cultural landscape
Characterized by site-specific climax tree species like Fagus sylvatica or Quercus robur
Growing on deep native soils
Study sites
ID: RePa-Bu
Species: Fagus sylvatica
Area: 309.4 m²
Age: > 100 a
DBH: 47.7 ± 4.6 cm
Height: 39.9 ± 2.5 m
Soil: Cambisol
ID: RePa-Ah
Species: Acer pseudoplatanus
Area: 293.4 m²
Age: > 100 a
DBH: 34.6 ± 3.7 cm
Height: 28.4 ± 2.3 m
Soil: Cambisol
ID: Hert-Ei
Species: Quercus robur, Carpinus betulus
Area: 531.6 m²
Age: > 100 a
DBH: 35.7 ± 2.5 cm
Height: 21.9 ± 1.8 m
Soil: Stagnosol
ID: Hert-Bu
Species: Fagus sylvatica
Area: 623.4 m²
Age: > 100 a
DBH: 46.2 ± 4.8 cm
Height: 27.8 ± 2.7 m
Soil: Stagnosol

## Slide 7
Urban greening forests [click on points for site characteristics]
Menu
Study sites
Young or medium aged forests, planted in urban parks or on former anthropogenic sites (especially slag or slate heaps)
Mixed-species composition, mainly of intermediate tree species
Growing on thin regosols. Before planting, a topsoil on top of the anthropogenic substrates are generally added. Rooting is limited.
ID: BoHo
Species: Carpinus betulus
Area: 93.8 m²
Age: 20-30 a
DBH: 13.2 ± 0.7 cm
Height: 23.6 ± 1.2 m
Soil: Regosol
ID:BlueHa
Species: Acer pseudoplatanus
Fagus sylvatica
Quercus robur
Carpinus betulus
Area: 157.3 m²
Age: 20-30 a
DBH: 18.0 ± 1.3 cm
Height: 18.4 ± 1.1 m
Soil: Regosol
ID: ReHa-Ah
Species: Acer pseudoplatanus
Area: 82 m²
Age: 30-40 a
DBH: 14.2 ± 1.3 cm
Height: 16.4 ± 1.4 m
Soil: Regosol
ID: ReHa-Ei
Species: Quercus robur
Carpinus betulus
Acer pseudoplatanus
Tilia cordata
Area: 151.2 m²
Age: 30-40 a
DBH: 17.1 ± 1.5 cm
Height: 16.0 ± 1.1 m
Soil: Regosol

## Slide 8
Succession forests [click on points for site characteristics]
Menu
Study sites
Pioneer forests on former coal mining or steel working sites, which are neither planted nor managed
Characterized by pioneer tree species like Betula pendula, Salix spec. or Populus spec. In old stands, pioneer species are mixed with intermediate species
Growing directly on top of the anthropogenic substrates. Rooting is limited.
ID: ReHa-Bi
Species: Betula pendula
Acer pseudoplatanus
Area: 74.1 m²
Age: 60-70 a
DBH: 18.5 ± 1.7 cm
Height: 21.0 ± 2.6 m
Soil: Regosol
ID: ZeHa
Species: Betula pendula
Tilia cordata
Area: 158.1 m²
Age: 30-40 a
DBH: 9.6 ± 0.8 cm
Height: 10.8 ± 1.1 m
Soil: Regosol
ID: WePa
Species: Betula pendula
Area: 142.6 m²
Age: 30-40 a
DBH: 13.7 ± 1.0 cm
Height: 16.8 ± 1.5 m
Soil: Regosol

## Slide 9
Characteristics of the drought years 2018/2019
Menu
Experimental period (2018/2019) was much warmer and drier than typical.
Precipitation deficit of 321 mm (-37%) in 2018 and 126 mm (-15%) in 2019.
Warmer temperatures in autumn increased the length of the vegetation period about 16 days.
Precipitation | Precipitation
Long-term | 865 mm
2018 | 544 mm
2019 | 739 mm
Temperature | 
Long-term | 11.0 °C
2018 | 11.6 °C
2019 | 11.2 °C

## Slide 10
Estimating CO2 uptake in forest biomass
Menu
Measurement of Diameter at Breast Height (DBH) and tree height in April 2018/2019/2020 of each tree.
Modelling annual tree biomass depending on species, DBH and tree height, considering coarse wood, brushwood, and roots (see flowchart).
Annual changes in carbon stocks represent the CO2 uptake.
Kublin (2003): A uniform description of stem profiles. Methods and programs. BDATPro. Forstwissenschaftliches Centralblatt 122 (3): 183-200.
Kollmann (1982): Technology of wood and wood products. Volume 1. Berlin, Heidelberg (german)
Grundner & Schwappach (1952): Mass panels to determine the wood content of forest trees and stands. 10. Edition. Berlin, Heidelberg (german)
IPCC (2003): Good practice guidance for land use, land-use change and forestry. Hayama.
3.65
0.5

## Slide 11
Estimating CO2 translocation by litterfall
Menu
+
Measuring LAI weekly with Plant Canopy Analyzer + Estimating LAI with Sentinel-2 satellite images.
Collecting 30 leaf samples of each species and determine Leaf Mass Area (LMA) [g cm-2].
30 Leaf samples
Measuring leaf area (ImageJ)
Measuring dry weight after drying at 60 °C for one week
Calculating annual stand leaf dry mass (LM) [kg m-2] with maximum stand-specific LAI [m2 m-2] (LAImax) and LMA [kg m-2] weighted by species.

## Slide 12
Measuring CO2 release by soil respiration
Menu
4 measurement locations on each site.
PVC-Collar (Ø 11 cm, height 10 cm) for chamber.
Decagon soil temperature and moisture probe (5TE/5TM) in 5 cm depth beside each collar, which were read out simultaneously during respiration measurements.
Permanent data logger for soil temperature and moisture (Decagon EM50) at one location.
Weekly respiration measurements with EGM 3 Environmental Gas Monitor (Gas Chromatography-Infrared Spectroscopy) (PPSystems).
SRC-1 Soil respiration chamber (PPSystems).
2 minutes chamber closing time.

## Slide 13
CO2 uptake by forest growth
Menu
Semi-natural forests: CO2 uptake increased in 2019 in comparison to 2018.
Urban greening and succession forests: CO2 uptake decreased in 2019 in comparison to 2018.
2018
2019
Factors explaining annual differences
A = semi-natural forests; B = succession forests; C = urban greening forests

## Slide 14
Factors explaining difference in CO2 uptake
Menu
Results from CO2 uptake
Decrease in annual CO2 uptake was even larger, the smaller the effective rooting zone, the soil C stock, and the amount of plant available water was at the sites.
Effective rooting zone, soil C stock, and plant available water influence and represent, among others, the water availability for trees.

## Slide 15
LAI development at the monitoring sites
Menu
2018: Fast leaf development, where all leaves were exposed already in June, triggered by warm temperatures. Water stress induced early leaf fall in July.
2019: Forests adept to drought and build up their canopy more slowly. Leaves were fully exposed not until July. Maximum LAI was lower at all sites in comparison to 2018.
At two sites massive loss of trees due to sooty bark disease in consequence of water shortage.
Annual CO2 translocation

## Slide 16
CO2 translocation
Menu
CO2 translocation decreased at all sites in 2019 in comparison to 2018.
Decrease in annual CO2 translocation is also correlated with effective rooting zone, soil C stock, and plant available water
Leaf development
A = semi-natural forests;
B = urban greening forests;
C = succession forests
2018
2019
[kg a-1 (100 m)-2]

## Slide 17
CO2 release by soil respiration
Menu
Mean CO2 effluxes varies in a narrow range between 0.5 and 1 µmol CO2 m-2 s-1, leading annual CO2 output between 69.4 and 138.8 kg CO2 a-1 100 m-2
We found no significant difference in CO2 efflux between the sites
Factors explaining differences
A = semi-natural forests; B = urban greening forests; C = succession forests

## Slide 18
Factors explaining CO2 release by soil respiration
Menu
Soil respiration
Microbial biomass effect
CO2 efflux is even larger, the larger the amount of microbial biomass is. Therefore, the CO2 efflux from soil respiration is clearly controlled by the amount of microbial biomass
Water shortage effect
Cmik/Corg ratio represents the decomposability and accessability of C for decomposition. Therefore, CO2 efflux is even larger at sites with larger Cmik/Corg ratio. A Cmik/Corg < 1.2 % is a threshold for inhibiting conditions for decomposition activity. Only one site was above that threshold. Consequently, at nearly all sites inhibiting conditions were found. We assume, that the lack of soil water hinders access to organic matter, decreases the mobility of the microorganisms, and finally
decreases the CO2 effluxes at the sites
Temperature effect
Normally, CO2 efflux increases with soil temperature. Here, the opposite was found. We assume, that high temperatures, coupled with dry conditions, leading to thermal denaturation, which decreased the amount of microbial biomass (Cmik is negatively correlated with soil temperature (not shown)). Finally, lower amounts of Cmik leading to lower CO2 efflux (see Microbial effect).
Mean CO2 efflux is positive correlated with Cmik, representing the amount of microbial biomass, Cmik/Corg ratio, representing the decomposability and accessability of C, and negative correlated with mean soil temperature (for explanations, please click on the plus-signs in the plots)

## Slide 19
Complete CO2 balance
Menu
-7.7 %
-103.6 %
+21.7 %
+21.4 %
-107.2 %
-33.1 %
-67.1 %
-48.4 %
-17.3 %
-59.8 %
-85.0 %
A = semi-natural forests; B = succession forests; C = urban greening forests
+9.9 %
-85.0 %
-62.9 %
CO2 uptake
CO2 translocation
CO2 release
Semi-natural forests
Net CO2 uptake increased about 9.9 % in 2019 in comparison to 2018. Indeed, only two sites increased the CO2 uptake (RePa-Bu, RePa-Ah), while at the other two sites CO2 uptake decreased. The Stellario-Carpinetum Hert-Ei turned from a carbon sink in 2018 to a source in 2019 (Net CO2 release of 2.5 kg a-1 100 m-2). The site has a limited rooting zone and no access to ground water, caused by a dense Sd-horizon. Therefore, water supply depends on precipitation, which was absent during experimental period.
Urban greening forests
All sites decreased net CO2 uptake in 2019 in comparison to 2018 by 62.9 %. One site (BlueHa) turned from a carbon sink in 2018 to a source in 2019, because 45 % of all trees died in consequence of sooty bark disease, which infest mainly young sycamore trees under water stress.
Succession forests
The succession forests were CO2 sources in both drought years and even increased their CO2 release in 2019 in comparison to 2018 by 85 %. At WePa and ZeHa, we found bad growth conditions, caused by very thin, coarse and loosy soils with low plant available water. The slow forest growth faced relatively high soil respiration rates, leading to a net CO2 release in both years. On the other hand, the old birch forest ReHa-Bi is a strong carbon sink with a net CO2 uptake of 205.9 kg a-1 100 m-2 in 2018 and 170.4 kg a-1 100 m-2 in 2019.

## Slide 20
Implications
Research Highlights
Menu
In urban areas growth conditions of urban forest stands differ widely, leading to different amounts of annual CO2 sequestration, depending on the individual interaction between forest growth, litterfall, and soil respiration
The two consecutive drought years 2018/2019 decreased CO2 uptake, translocation, and respiration in the second year, but the urban forest types reacted differently on the drought
Semi-natural forests
Urban greening forests
Succession (birch) forests
Semi-natural forests on mesophilic locations were able to buffer the elevated temperatures and low precipitation and keep up the net CO2 uptake even in the second drought year. This is caused by high soil carbon content, plant available water, and a deep rooting zone, where the trees are able to access water reservoirs in deeper soil zones
In contrast, urban greening forests and semi-natural forests on more extreme locations (Stellario-Carpinetum) are more prone to droughts, because of limited rooting zones by sealed soil layers, low soil carbon content, and plant available water. Those forests drastically decreased their CO2 fixation potential in the second drought year and two sites turned from carbon sinks into sources.
Succession forests were CO2 sources in both years, because of bad growth conditions (thin, coarse, and loosy soils with low amounts of plant available water), which faced relatively high soil respiration rates.

## Slide 21
Implications
Menu
As a consequence of climate change, drought periods will increase in intensity, duration, and frequency in the following years
This study shows, that urban forest ecosystems are prone to droughts, because forests in urban areas are often limited in rooting and the water supply depends on rainwater
If the vitality of forest decrease, the provision of ecosystem services such as CO2 sequestration decreases as well
Following recommendations can be made:
  Semi-natural forests on deep native soils are able to sustain longer drought periods and keep up their CO2 fixation potential. Because of that, those forests are important for the urban carbon budget and should be preserved against other landuses
  If new urban forests are planned, practioneers should provide good growth conditions, especially a deep rooting zone and carbon rich soils, which supplies large amounts of plant available water, to ensure good vitality even under drought conditions for urban forest ecosystems
Research highlights