## Slide 2: Agenda
20 min:
Introduction to the research project RePeat
WP2: Abandoned Peatland Ecosystem Response to Secondary Succession
Field sites
Methods and Instruments
Data collection and preliminary results

## Slide 3: RePeat – Introduction to the “Danish lowland issue”
C pool
CH4
N2O
• 61 % of the total area in Denmark is used for cultivation (Danmarks Statistik, 2020)
• 7 % of the cultivated area consists of drained lowland
and emits ca. 4.8 mio. ton CO2e annually (The Danish Council on Climate Change, 2020)
• Corresponding to 6-7 % of the total national annual GHG emissions (Nielsen, O. K. et al., 2020)
Organic soils: 6-12 % OC
Peatland: > 12 % OC
Figures: Videnskab.dk
C pool
= “Lowlands” (Lavbundsjorde)

## Slide 4: RePeat – Introduction to the project
Funding: Danish Agriculture Agency: 2019 Call for climate research in agriculture
Purpose: Increase our data and knowledge on greenhouse gas emissions from organic soils managed by different practices
Research group:
  KU: Jesper R. Christiansen, Klaus S. Larsen, Lars Vesterdal, Per Gundersen and Annelie S. Nielsen
  AU: Poul Erik Lærke, Johannes Pullens and Ji Chen
Four WPs:
  WP1: Annual GHG budget on different extensification types
  WP2: Annual GHG budget on abandoned organic soils (my primary study)
  WP3: C and N pools in soil and biomass and soil-water-chemistry properties
  WP4: Modelling and improving emission factors

## Slide 5: RePeat – Project parts illustration
Figure: RePeat project group
WP1
WP2

## Slide 6: RePeat – WP2
WP2: Abandoned Peatland Ecosystem Response to Secondary Succession
Purposes and goals:
  Contribute to data collection of soil GHG emission measurements
  By measuring the total annual greenhouse gas budget of CO2 and CH4
  Estimate the annual net ecosystem exchange (NEE) of CO2 and CH4 and net carbon stock (NCS) for lowland soils
Hypothesis (H1):
By abandoning farmed peatland, over time, the land will turn into a net carbon sink through secondary succession.

## Slide 7: RePeat – WP2
WP2: Abandoned Peatland Ecosystem Response to Secondary Succession Hypothesis (H1):
By abandoning farmed peatland, over time, the land will turn into a net carbon sink through secondary succession.
+C [mass/area] (C source to the atmosphere)
+C [mass/area] (C sink to the ecosystem)
time
0
30 yr
60 yr
 (net carbon loss for eco.):
Primary by CO2 and CH4
[g C m-2 yr-1]
 (net carbon stock for eco.):
Soil and biomass
[g C m-2 yr-1]
ATM
Ecosystem

## Slide 8: Four field sites

## Slide 9: Field sites - Toftholm

## Slide 10: Field sites - Førslevgaard (rewetted 2020)
Photos: Annelie Skov Nielsen

## Slide 11: Field site setup - Instruments
10 plots x 4 field sites = 40 plots
Wsoil
Tsoil
GWLauto

## Slide 12: Methods – Instruments – Static chamber

## Slide 13: Data collection
Field campaign manual measurements:
  CO2, CH4 and H2O
  N2O (summer campaign 2021)
  Tchamber and PARchamber
  Groundwater level at each plot
  Groundwater samples for Nutrition and DOC
  Biomass (bio samples and NDVI)
  Soil core samles
Automatic measurements:
  Meteorological measures from field-installed MET-station incl. PAR
  Tsoil at each plot
  Soil moisture at each plot
  Groundwater level at each subsite
Field campaign every 3rd week at each site in entire 2021 as a minimum:
Every 3rd week
1-2 times in 2021
Data log per 1hr

## Slide 14: Preliminary results
Reco
NEE
GPP
CO2 flux [µmol m-2 h-1]
Chronosequence of peatland sites left for secondary succession
Static chamber CO2 measurements
Combined January to March 2021 data

## Slide 15: Preliminary results
Static chamber CO2 measurements - Combined January to March 2021 data
Reco vs Groundwater level GPP vs Groundwater level

## Slide 16: Thank you for your attention!

## Slide 17: References
Danmarks Statistik (2020) Danmarks landbrugsareal er stort internationalt set. Copenhagen. Available at: www.dst.dk/stattabel/868 (Accessed: 28 April 2021).
Hemes, K. S. et al. (2019) Assessing the carbon and climate benefit of restoring degraded agricultural peat soils to managed wetlands, Agricultural and Forest Meteorology. Elsevier, 268(October 2018), pp. 202–214. doi: 10.1016/j.agrformet.2019.01.017. Available at: https://www.rednueva.es/wp-content/uploads/2019/06/07-2-Hemes-et-al.-2019-AFM.pdf (Accessed: 11 March 2021).
Nielsen, O.-K. et al. (2020) Denmark’s National Inventory Report 2020: Emission Inventories 1990-2018 - Submitted under the United Nations Framework Convention on Climate Change and the Kyoto Protocol. Aarhus University, DCE - Danish Centre for Environment and Energy. Available at: http://dce2.au.dk/pub/SR372.pdf (Accessed: 11 March 2021).
The Danish Council on Climate Change (2020) Carbon rich peat soils - Proposal for a new model for effective regulation and rewetting, Copenhagen. Available at: file:///C:/Users/mpv590/Downloads/engkulstofrige_lavbundsjorder_final3_16dec20_final4%20(1).pdf (Accessed: 10 March 2021).