## Slide 1
Applied Avalanche Research in Norway
Recent advances
Avalanche formation and release
Avalanche Dynamics
Avalanche interactions
Avalanche Modelling
Please choose one of the four focus areas for more information
Author and project information

## Slide 2: Avalanche formation and release
Research highlights
Wind simulations for use in hazard zone mapping projects
Effects of forest on avalanche release probability

## Slide 3: Why wind simulations for hazard mapping?
Hazard zoning requires to decide on a fracture height for a given return period (in Norway 100, 1000 and 5000 years event)
The wind climate in a release zone plays a decisive role for the modelling scenario
Wind modelling is usually not used in this type of projects due to high costs
We try to find simplified approaches that could be implemented into standard hazard mapping projects

## Slide 4: Testing CFD wind simulations for snow distribution
Using the CFD WindSim model – developed for wind parks
  Can extract winds at different heights, use varying grid resolution both horizontally and vertically, and include terrain roughness and vegetation
  Nesting down to high resolution simulation in the area of interest is possible
Two main approaches:
  Run timeseries of wind data from one point – transferred to other location
  Run main wind directions and get a wind field for the area per direction
8 wind directions modelled by the WindSim model
  Finse – tested sensitivity to measured wind data and snow heights in undulating terrain
  Grasdalen - compared to mapped snow avalanches
Regional Weather Model (Arome) vs observed wind data at a local weather station – can be used as input?

## Slide 5: Can we use WindSim to reproduce local wind patterns?
A
B
C
2*nesting
Z = 5 m
dXY = 12m
3*nesting
Z = 3 m
dXY = 10m
WindSim can reproduce near surface wind distribution fairly well in undulating terrain (only 20-40 m terrain variation)
Test site Finse:

## Slide 6: Wind fields for main wind directions compared to observed snow distribution patterns at Finse
Input wind direction: W
Windsim

## Slide 7: WindSim to locate avalanche release areas
Windsim
Input wind direction: W
Grasdalen, western Norway

## Slide 8: Avalanche release probability
Monte-Carlo simulation
Performance function

## Slide 9: Avalanche Dynamics
Research highlights
The recent avalanche experiment at Ryggfonn
Test of model performance of maximum front velocity of major avalanches
Notes: In the section on avalanche dynamics, we want to show you some results from our recent full scale avalanche experiment at the Ryggfonn test site as well a test of model performance on maximum front velocities.

## Slide 10: The recent avalanche experiment at Ryggfonn
Video from the experiment
Alternative link

## Slide 11: Why still full-scale experiments
Although measurements of full-scale avalanches are expensive and time consuming, and they are a difficult to perform under those harsh conditions within an avalanche (and not always easy to understand), they are indispensable to gain in-depth understanding of
the flow behavior of avalanches
    velocity (longitudinal and vertical velocity profiles)
    internal forces / accelerations
    flow density
    flow height
erosion mechanism / amount / rate
impact forces / interaction with structures
  They are needed to crosscheck the scaling used in small-scale experiments, and for model development and validation.

## Slide 12: Avalanche dynamics: velocity a highly important variable
Ryggfonn observations
Comparison to various measurements
For the comparison, topography and velocity is scaled

## Slide 13: Test of model performance of maximum front velocity of major avalanches
Hazard assessment for landuse planning in snow avalanche prone areas requires, besides knowledge of return periods, the specification of expected runout distances. For a complete risk assessment, additionally, the intensity of the event, often expressed in terms of impact pressures, and the corresponding vulnerability of endangered objects are needed
To obtain dynamical parameters, such as velocity, it has become state of practice to use 2-dimensional depth integrated avalanche models like RAMMS (Christen et al. 2010) or Mot-Voellmy (Issler & Liu, 2018). However, those models still lack a thorough and documented validation - which is partly caused by the lack of sufficient avalanche data - and therefore, it requires extensive experience from practitioners to assess the model results. Mainly, the models are calibrated based on runout observation, however runout observations provide limited constraints for the validation of the empirical parameters used in common present-day numerical avalanche models.

## Slide 14: Derived from observations combined with simple block model calculations
The avalanche track
approximated
by parabola

## Slide 15: Scaling behaviour of maximum front velocity of major avalanches
Test of model performance for example
RAMMS and Mot-Voellmy
simple parabolic track
standard parameters, which however should favor long runout and high speeds

## Slide 16
HSrel [1 m, 1.5 m, 2 m]
HSC [100 m,..,2000 m]
RAMMS
MoT-Voellmy

## Slide 17: Maximum velocity along the track
RAMMS
MoT-Voellmy
Observations of major events
In addition to the drop height, steepness and initial volume are varied for the modeling.

## Slide 18: Remarks
Present-days numerical models, typically are based on the Voellmy-fluid rheology, show short comings, especially with regard to velocity predictions
Validation of avalanche models solely with runout observations is insufficient
Cross comparison of experiments is an important task to reveal scaling behaviour
Only with a thorough understanding of the dynamics of avalanches is the development of improved numerical models and their validation possible

## Slide 19: Avalanche interactions
Research highlights
Vulnerability of Norwegian buildings and persons inside
Remote sensing of snow distribution and avalanche events
Notes: In avalanche interactions we study vulnerability of Norwegian wood frame buildings against avalanches and test different remote sensing techniques to document interesting avalanche events for our research.

## Slide 20: Vulnerability of persons inside buildings
Create a database of Norwegian avalanche case histories involving buildings with persons inside
Improve/develop vulnerability curves with a damage scale
Issler et al. (2016). Vulnerability of houses and persons under avalanche impact – the avalanche at Longyearbyen on 2015-12-19
Notes: One of our goals within the research topic avalanche interaction is to better define vulnerability curves for persons inside of buildings impacted by avalanches. The figure to the left shows an example of a vulnerability curve for persons inside buildings for the avalanche in Longyearbyen in Svalbard, Norway, in 2015. We wish to continue defining these curves by including data from historical avalanches throughout Norway.
In Norway we do not have a database well suited for quickly generating vulnerability curves, as this requires some indication of degree of damage to the building, and not only a yes/no response to if buildings were impacted. The middle image shows the damage scale used for the Longyearbyen avalanche, which will be used and adapted depending on the availability of information on historical avalanche events. The image to the right shows the beginnings of our database, showing the data collected for individual avalanches, including details on effects of persons inside the buildings, and how the building fared in the avalanche. This data will be added to the vulnerability curve on the left.

## Slide 21: Vulnerability of Norwegian buildings
Model typical Norwegian wood building with OpenSeesPy
Multiple variables: flow height, building material, etc.
Favier, P. et al. (2013) A reliability assessment of physical vulnerability of reinforced concrete walls loaded by snow avalanches
NGI (2007) Vulnerability and Risk assessment for geohazards
Estimated specific loss versus impact pressure; top panel summary of the proposed vulnerability based on avalanche observations (Barboltni et al, 2004; Keylock et al, 2001; Wilhelm, 1999); bottom panel approximations derived for a failure of an exterior wall with face exposure based on (Valentine; 1998).
Notes: The second goal in within the topic of avalanche interaction is to investigate the vulnerability of wood-frame buildings impacted by avalanches. Here we plan to create a numerical model of a typical Norwegian wood-frame building with OpenSeesPy, and run simulations including variables such as avalanche flow height, impact pressure and impact direction on the structure. We also aim to model the effectiveness of improving the building material type on the strength of the structure, for example using cross laminated timber instead.
To the left you can see a presentation of estimated specific losses from increasing impact pressures from various authors. The light, or wood-frame structure is the leftmost curve, withstanding the least amount of pressure before showing loss.
To the right is an example of a simplied model showing an avalanche impacting the side of a reinforced concrete building. It is thought to take a similar approach, only with a wood frame building.

## Slide 22: Drone-based avalanche surveys
Study aim/goals
Avalanche experiment observations
Directly georeferenced 3-D models
Remote, spatially continuous snow distribution measurements in avalanche terrain using drone photogrammetry
Using precision navigation and only limited ground control

## Slide 23
Notes: Hi! I'm Sean and I'm a remote sensing specialist at the Norwegian Geotechnical Institute. On this slide we are looking at a drone survey before and after a large avalanche experiment in the Strynefjellet mountains in Norway. That's me on the left piloting the drone and on the right you can see one of the products of the survey, an orthomosaic derived from about 300 high-resolution images. 3-D surface elevation data derived from drone surveys will help avalanche experts to better map and estimate the accumulated avalanche deposit volume.

## Slide 24
Notes: To test the accuracy of our drone-based snow accumulation measurements, we independently verify control points on the ground and compare these to data mapped with and without snow cover.

## Slide 25: Avalanche modelling
Research highlights
Entrainment modelling
Modelling of flow-regime changes
Notes: Avalanche modelling aims at the development of better physically based avalanche models for the use by practitioners in avalanche consulting. Here we want to present some recent highlights from entrainment and flow-regime change modelling.

## Slide 26: Entrainment modelling
Compelling reasons for including entrainment/deposition in a state-of-the-art avalanche model:
Mass balance has important effects on avalanche dynamics and design of mitigation measures.
Impossible to achieve a model based on physical parameters instead of "fudge factors" µ, ξ.
However, most proposed entrainment models introduce yet another "fudge factor" for the entrainment rate!
Please see vPICO "Towards an Improved Parameter-Free Entrainment Model for Snow Avalanches" in CR5.2 for details.

## Slide 27: Modelling of flow-regime changes
Observed in practice:
Transition dense flow ↔ fluidized flow has decisive effect on trajectory, run-out distance and dynamic pressure.
Strongly fluidized flow correlates with light, cold snow.
Variable fraction of avalanche length is fluidized.
Practical needs:
Reliable, fast, easy-to-use model
Easy-to-follow recipe for range of input parameters
Option to include extra layer for powder-snow cloud

## Slide 28: What are the key elements of the future model?
Driving factors for fluidization:
Snow-particle collisions (granular temperature)
Escaping air from compressed snow cover
Challenge: Simplify this complex system in a meaningful way!
Rheological parameters
Avalanche density
Excess pore pressure
Avalanche speed
Snow-cover properties

## Slide 29: Authors and project information
Christian Jaedicke
Hedda Breien
Ulrik Domaas
Regula Frauenfelder
Peter Gauer
Graham Gilbert
Kjersti Gleditsch Gisnås
Sylfest Glimsdal
Håkon Heyerdahl
Dieter Issler
Henrik Langeland
Zhongqiang Liu
Kate Robinson
Sean Salazar
Katrine Mo
Frode Sandersen
The AARN project is the continuation of the NGI avalanche research legacy appointed by parliament in 1973. The project is today organised in three-year periods and is administrat-ed by the Norwegian Water and Energy Directorate (NVE).