## Slide 1
Quantum Cascade Laser absorption spectroscopy (QCLAS) of clumped 18O12C18O
Akshay Nataraj1,2, Michele Gianella1, Ivan Prokhorov1, Béla Tuzson1, Jérôme Faist2 and Lukas Emmenegger1
1 Empa, Swiss Federal Laboratories of Materials Science and Technology, 8600 Dübendorf, Switzerland 2 ETH Zurich, Institute for Quantum Electronics, 8093 Zürich, Switzerland
Wavenumber (cm-1)
Transmittance
Measured transmission spectra of CO2 isotopologues at room (red) and low (blue) temperatures.
Key results
High precision and repeatability of δ18O
Demonstration of optical clumped thermometry involving: isotope exchange reaction
EGU General Assembly 2021: Gather Online (#vEGU21), Session BG 2.2, 27 April 2021
Key components
DFB-QCL emitting at 4.3 μm driven in intermittent continuous wave (icw) mode
Cryo-cooled (150 K) segmented circular multipass cell (SC-MPC).
OPL = 6 m, P = 10 mbar
Multi-port inlet for rapid gas switching
Schematic of the optical setup.

## Slide 2
Outline
Introduction
Optical setup
Instrument performance
Optical clumped thermometry
Acknowledgements

## Slide 3
Introduction
Carbon has 2 stable (12C and 13C) and 1 radioactive (14C) isotopes
Oxygen has 3 stable isotopes (16O, 17O, 18O)
Multiply substituted or ‘clumped isotope’ species with 4 ppm relative abundance (18O12C18 O)
Quantified as deviation Δ of the isotopologue ratio 𝑅 w.r.t. random distribution 𝑅∗: 𝑅 = (1 + Δ) 𝑅∗.
Δ is independent of 𝜹.
https://dinotopes.wordpress.com/
At very high temperatures, heavier isotopes 13C and 18O will be randomly distributed
At lower temperatures, heavier isotopes 13C and 18O tend to clump together
Terminology: 16O12C16O = 626
Abundance
Molar mass [g mol-1]
Isotopologues of Carbon Dioxide

## Slide 4
Optical system
Key elements
4.3 μm DFB-QCL operated in intermittent continuous wave (icw) mode [1]
Segmented circular multipass cell (SC-MPC)[2] installed in vacuum chamber and kept at 10 mbar in a flow through mode.
Optical path length: 6 m
Vibration controlled Stirling-cooler to cool the MPC to 150 K
Temperature stabilized custom made acrylic glass housing
Automatic gas handling using multi-port Vici valve
[2]Graf, Manuel et al. “Compact, Circular, and Optically Stable Multipass Cell for Mobile Laser Absorption Spectroscopy.” Optics Letters 43 (11): 2434. https://doi.org/10.1364/OL.43.002434.
[1]Fischer, M et. al “Intermittent Operation of QC-Lasers for Mid-IR Spectroscopy with Low Heat Dissipation: Tuning Characteristics and Driving Electronics.” Optics Express 22 (6): 7014. https://doi.org/10.1364/OE.22.007014.

## Slide 5
Instrument performance
Single measurement of isotope ratio yields a precision of 0.03 ‰ for R2 and 0.05 ‰ for R1
Alternative switching between reference and sample (cycle = 400 sec) yields a precision on δ of 0.005 ‰
0.005 ‰
Isotope ratio
Allan deviation (σ)
Precision of the instrument
R1 = 12C18O2/12C16O2
R2 = 12C16O18O/12C16O2
R1
R2
τ (s)
10-5
Allan deviation (σ)
Time (s)
103
104

## Slide 6
Clumped isotope thermometry
Clumped isotope thermometer is based on measurements of three isotopologues involved in the isotope exchange reaction.
Non-equilibrated sample (red line) shows minimal fractionation (0.047 ‰) introduced by the gas handling line
Difference in the Δ12C18O2 between the reference (~ 300 ºC) and heated sample (~ 1000 ºC) is -0.37 ± 0.03 ‰.
[3] Wang, Zhengrong, et al.” Geochimica et Cosmochimica Acta 68 (23): 4779–97. https://doi.org/10.1016/j.gca.2004.05.039.
Reciprocal Temperature /10-3 K
Equilibrium constant K is related to Δ as
Expected difference in Δ12C18O2 ~ -0.39 ‰ [3]
Δ12C18O2 for non-equilibrated sample (red) and equilibrated sample (blue) at 1000 ºC
Measurement number
Δ12C18O2 ‰

## Slide 7
Acknowledgements
Philipp Scheidegger
Herbert Looser
Manuel Graf
Joachim Mohn
Funding:
  Discovery
Thanks for your attention!
Questions? Akshay.Nataraj@empa.ch, Ivan.Prokhorov@empa.ch, Michele.Gianella@empa.ch

## Slide 8
Appendix
Sample preparation unit