## Slide 1: Hydrodynamic modelling of outburst flood hazard in the Pokhara Valley, Nepal
Melanie Fischer1, Karin Lehnigk², Oliver Korup1,3, Georg Veh1, and Ariane Walz1
1Institute of Environmental Science and Geography, University of Potsdam, Germany
²Department of Geosciences, University of Massachusetts Amherst, United States
3Institute of Geosciences, University of Potsdam, Germany
Correspondence to: Melanie Fischer, melaniefischer@uni-potsdam.de

## Slide 2
International media attention in the days after the event
1st Objective: Reconstruction of the Seti Khola Flood Disaster (5th May 2012)
72 fatalities, damage to infrastructure (bridges and water supply system), estimated loss of 49.25 million NPR (c. 390,000 €)
Cascading or multihazard event along high topographic gradient
7500 m asl
1100 m asl
  Rockslide
  Lake formation
  Ice-rock avalanche
  Hyperconcentrated flood
Study Area – Pokhara Valley Overview
Watch video-footage of the event here:
https://www.youtube.com/watch?v=DR4lRcSMKRQ
And post-event footage here: https://www.youtube.com/watch?v=0znR1rm6eK4

## Slide 3
2nd Objective: Simulation of potential future events
Informed by widespread fluvial and debris-flow deposits found in the valley‘s recent and geological history
Valley fill records post-glacial to mediaeval events covering hundreds of km² (Tallakot, Ghachok, and Pokhara Formations)
Study Area – Pokhara Valley Overview
Overview of the Pokhara valley‘s topography and geology. Note the fan-shaped Pokhara Formation, the youngest alluvial depositional unit of the valley‘s sediment fill sequence (Schwanghart et al. 2016).

## Slide 4
Kaseri – a settlement of squatters – located directly on the bank of the Seti Khola at the Seti dam location
Kharapani village during and after the 2012 flood (modified after Oi et al. 2015)
Study Area – Focus Locations

## Slide 5
Methods – Hydrodynamic modelling
Steady-state models:
HEC-RAS
  One-dimensional
  25 m² resolution
  Suitable for peak discharges <10,000 m³/s
ANUGA
  Two-dimensional
  2500 m² resolution
  Suitable for peak discharges >10,000 m³/s
Data input:
  ALOS 5 m DEM
  Manning‘s n
  2012-flood-markers
  570 crosssections (field-measured and DEM-derived)
  combination of remote-sensing and field work to minimise modelling uncertainties

## Slide 6
Location: Kharapani village
Most damages and fatalities in this area
Eyewitnesses reported ice blocks within the flood
Gurung et al. (2015) estimated 8400 m³/s maximum peak discharge
HEC-RAS model:
  1D, steady state in mixed-flow regime
  8400 m³/s as flow boundary condition to test Gurung et al.‘s (2015) estimate
Results – HEC-RAS at Kharapani village location
Inundation depth [m]
Click here to start video!

## Slide 7
Results – HEC-RAS at Kharapani village location
Location: Kharapani village
Most damages and fatalities in this area
Eyewitnesses report ice blocks within the flood
Gurung et al. (2015) estimated 8400 m³/s maximum peak discharge
HEC-RAS model:
  1D, steady state in mixed-flow regime
  8400 m³/s as flow boundary condition to test Gurung et al.‘s (2015) estimate
  Simulated inundation extents in agreement with field-measured flood markers and remotely-sensed fluvial sediments
RapidEye scenes acquired before (22/03/2012, a) and after (18/10/2012, b) the May 2012 flood at Kharapani; outburst sediment extents and channel changes of the Seti Khola (c); inundation depth for a simulated peak discharge of 8400 m³/s (Gurung et al. 2015) using HEC-RAS (d).

## Slide 8
Location: Seti Dam
Densely populated settlement of squatters on lowermost terrace
SANDRP (2014) estimated 935 m³/s peak discharge and 2.15 m water level at dam
HEC-RAS model:
  1D, steady state in subcritical-flow regime
  935 m³/s as flow boundary condition to test SANDRP (2014) estimate
Results – HEC-RAS at Seti dam location
Inundation depth [m]
Click here to start video!

## Slide 9
Results – HEC-RAS at Seti dam location
RapidEye scenes acquired before (22/03/2012, a) and after (18/10/2012, b) the May 2012 flood at the Seti dam; sediment extents and channel changes of the Seti Khola (c); inundation depth for a simulated discharge of 935 m³/s (SANDRP 2014) using HEC-RAS (d).
Location: Seti Dam
Densely populated settlement of squatters on lowermost terrace
SANDRP (2014) estimated 935 m³/s peak discharge and 2.15 m water level at dam
HEC-RAS model:
  1D, steady state in subcritical-flow regime
  935 m³/s as flow boundary condition to test SANDRP (2014) estimate
  Simulated inundation extents are inconsistent with remotely-sensed fluvial sediments and reported damage

## Slide 10
Results - ANUGA models
Simulation of potential future outburst scenarios with a wide range of magnitudes
5,000 to 600,000 m³/s peak discharges
Backwater effect causing extensive flooding in tributary valleys for peak discharges >100,000 m³/s
Alluvial fan deposits may promote lateral spread of overbank flow

## Slide 11
Pokhara: a fast-growing city located in a valley prone to outburst floods!
HEC-RAS reconstructions: only partially supporting previous (empirical) assessments of the May 2012 Seti Khola Flood Disaster
Backwater effects: large events (>100,000 m³/s) could cause extensive flooding of tributary valleys for several kilometres upstream
Take Home Message

## Slide 12
Acknowledgements
A big thank you to Elisabeth Schönfeldt, Monique Fort, and Narayan Gurung for their support in the field!
This research is funded by the Deutsche Forschungsgemeinschaft (DFG) via the graduate research training group NatRiskChange (GRK 2043/1, 2043/2) at the University of Potsdam (https://www.natriskchange.de).
melaniefischer@uni-potsdam.de
@GeoMelFi1
Melanie Fischer
(https://www.researchgate.net/profile/Melanie-Fischer)
Contact me!