## Slide 1: Rapid Mapping of Landslides by Deep-Learning of Combined Optical and SAR Data
EGU General Assembly 2021 - Session NH3.6 - ‘Landslide investigation using Remote Sensing and Geophysics’ - 26 April 2021
Lorenzo Nava¹, Oriol Monserrat² and Filippo Catani³
¹University of Florence, Department of Earth Sciences, Italy (lorenzo.nava@stud.unifi.it)
²Centre Tecnològic Telecomunicacions Catalunya, Department of Remote Sensing, Spain (omonserrat@cttc.cat)
³University of Padua, Department of Geosciences, Italy (filippo.catani@unipd.it)

## Slide 2
EGU General Assembly 2021
Introduction:
Source: https:\\video.corriere.it
Source: http:\\meteoweb.eu
In the world, various natural calamities, can trigger multiple landslide events, that can occur in group of hundreds to thousands in a region, in a short time span.
Chile, in 2010 (Serey et al., 2019).
Kumamoto (Song et al., 2019) and Ecuador (Chunga et al., 2019), in 2016.
Hokkaido (Wang et al., 2019) and Lombok (Ferrario, 2019), in 2018.

## Slide 3
EGU General Assembly 2021
Method able to define the spatial activation of landslides right after a multiple event, that can be applied independently from the presence of cloud cover.
Potential and limits of convolutional neural networks (CNN) applied to SAR data to detect landslides.
Purpose of the study:

## Slide 4
EGU General Assembly 2021
Iburi sub-prefecture, Hokkaido, Japan.
Fig. 1: Localization of the study area.
Event considered:
A 6.6 Mw earthquake triggered about 7837 coseismic landslides on September 6, 2018.
Fig. 2: Coseismic landslides in the study area. (Source: Wang et al. 2019).
Study area:

## Slide 5
EGU General Assembly 2021
Sentinel-1 SAR GRD products with VV and VH polarizations, and IW acquisition mode (5 m x 20 m).
Sentinel-2 VHR RGB image (10 m x 10 m).
Digital Elevation Model (DEM) (30 m x 30 m) and slope obtained from the same.
Region and Year | Sentinel-2 | Sentinel-1
 |  | 01-09
Iburi, Hokkaido 2018 | 20-10 | 13-09
 |  | 25-09
Tab. 1: Dates of acquisition of Sentinel-2 and Sentinel-1 for the study area in Hokkaido 2018.
Multiple landslide event
Materials:

## Slide 6
EGU General Assembly 2021
Sentinel-1 SAR Layers
Topographic Layers
Input
Input
LANDSLIDE
NO LANDSLIDE
Output
Output
+
Conv2D, 3x3
MaxPool2D, 2x2
MaxPool2D, 2x2
Conv2D, 3X3
ReLU
ReLU
Rete Neurale
CNN
Supervised classification:

## Slide 7
EGU General Assembly 2021
3x3
Convolution
Max Pooling
Max Pooling
Max Pooling
3x3
Convolution
3x3
Convolution
Input
Output
Fig. 3: CNN architecture.
Fully Connected
Flatten
CNN architecture:

## Slide 8
EGU General Assembly 2021
Accuracy(%) | Precision(%) | Recall(%)
99.20 | 99.60 | 98.81
86.63 | 92.24 | 80.16
80.84 | 82.77 | 78.17
89.96 | 95.83 | 83.47
88.55 | 96.58 | 79.84
81.87 | 93.22 | 68.75
94.17 | 97.32 | 90.83
90.83 | 93.36 | 87.92
93.33 | 95.22 | 91.25
Tab. 4: Accuracy, precision and recall on the test datasets.
Tab. 2: Datasets characteristics.
Dataset Name | Band1 | Band2 | Band3
RGB | Red | Green | Blue
SSD | VV after-event | VH after-event | DEM
SSs | VV after-event | VH after-event | Slope
BAD | VV before-event | VV after-event | DEM
BAs | VV before-event | VV after-event | Slope
HHH | VH before-event | VH after-event | VH after-event
BAA | VV before-event | VV after-event | VV after-event
BAC | VV before-event | VV after-event | VV after-event - VV before-event
BAH | VV before-event | VV after-event | VH after-event
Results of test datasets:

## Slide 9
EGU General Assembly 2021
Window size: 25 m x 25 m.
Window step: 2 pixels.
Classification of the center pixel of each ROI analyzed.
Object detection - sliding window:

## Slide 10
EGU General Assembly 2021
Accuracy(%) | Precision(%) | Recall(%)
99.20 | 99.60 | 98.81
Dataset Name | Band1 | Band2 | Band3 | Band4
RGB | Red | Green | Blue | 
Landslide mapping - RGB:

## Slide 11
EGU General Assembly 2021
Accuracy(%) | Precision(%) | Recall(%)
94.17 | 97.32 | 90.83
Dataset Name | Band1 | Band2 | Band3 | Band4
BAA | VV before-event | VV after-event | VV after-event | 
Landslide mapping - baa:

## Slide 12
EGU General Assembly 2021
Accuracy(%) | Precision(%) | Recall(%)
93.33 | 95.22 | 91.25
Dataset Name | Band1 | Band2 | Band3 | Band4
BAH | VV before-event | VV after-event | VH after-event | 
Landslide mapping - baH:

## Slide 13
EGU General Assembly 2021
We verified that the developed method, using SAR data, can achieve accuracies comparable to the optical data, but it is exploitable also in presence of cloud cover.
The time spent by the model to analyze the entire study area (about 460 km ) is less than five minutes.
The next steps will be to evaluate the application of segmentation deep-learning-based methods on SAR data to define the perimeter of each individual landslide and to exploit composite images with 4+ bands, e.g., to combine RGB, SAR and topographic factors.
Conclusions:
2

## Slide 14: THANK YOU FOR YOUR ATTENTION