## Slide 1
ITRF 2014 provides periodic fits for station positions that favor the realization of better, more consistent regional continental-scale frames.
Regional subset of periodic parameters of ITRF defines a ‘periodic space’ that can be ‘inherited’ by a regional frame.
Difference in station positions with and without inheriting the periodic space from ITRF 2014 can reach ~4 mm for a continental realization in South America
Figure 2: Phasorial plots of common-modes observed in ITRF 2014 using 27 stations in Central and South America. Blue and red arrows represent the 27 common-mode components (annual and semi-annual), leaving one station out of the analysis at the time; cyan arrows represent the phasor computed by using all stations. A significant component exists in the X and Z components of annual translation. An apparent seasonal scale change is also observed for the annual component.
Realizing ITRF-Consistent Continental-Scale Geodetic Reference Frames
Figure 1: Map of the stations (continuous and campaign) used to realize POSGAR07b processed by the Scientific Processing Center – Argentina (Centro de Procesamiento Científico – Argentina) IGN. Red dots represent stations common to POSGAR, SIRGAS, and the ITRF reference frames.
Figure 3: Annual and semi-annual residuals between SP07b and ITRF 2014. a) Residuals before inheriting the periodic space of ITRF 2014. b) Same as (a) for semi-annual. c) Residuals after inheriting the seasonal terms of ITRF 2014. d) Same as (c) for semi-annual.
Demián D. Gómez, Michael G. Bevis, and Dana J. Caccamise II
For more information
Gomez.124@osu.edu