## Slide 1: The role of small wetlands for resilient ecological networks in a wetlandscape
2021. 04. 28
Bin Kim and Jeryang Park
Environmental & Ecological Complex Systems Laboratory
Department of Civil & Environmental Engineering, Hongik University, South Korea

## Slide 2: Background
Wetlands provide valuable ecosystem services
- biodiversity conservation,
- water purification,
- flood protection, etc.
Changes in habitat migration patterns of inhabiting species can occur through the change of interconnectivity between distributed wetlands according to the wetlandscape hydrology
Necessity of improving existing wetlands conservation (replacement) plan
- Focused on wetland area or number (Massachusetts inland wetland replication guidelines, Provincial wetland restoration guide (Alberta Environment), etc.)
- Underestimation of ecological benefit and importance of small wetlands
Wetlands (blue circle) of various size are connected to each other by dispersal models (e.g., heavy-tailed dispersal model) to form an ecological network in wetlandscape.

## Slide 3: Objectives
Identify the contribution of small wetlands on structure and function of ecological network
Analyzed two different scenarios in which the sum of wetland areas are similar, but their area distributions are distinct
Analyzed the multiple ecological states (based on network metrics) with change in hydro-climatic conditions
Suggest a wetlands conservation plan based on the functional role of wetlands
Ecological condition
(Sum of wetlands area)
State (<k> or E)

## Slide 4: Representations of hydrology and network
Hydrologic dynamics of wetland: Wetland-groundwater coupled model
Nodes: wetlands;
Edges: The movement path of the species; bidirectional, unweighted
Forming the edges: Probabilistically (heavy-tailed dispersal process)
Source: Leonardo et al., 2018
Source: Kim and Park, 2020

## Slide 5: Network Representation - Edge
Heavy tailed dispersal model: Describe a random walk characterized by a power law distribution (heavy tailed distribution) (Bartumeus, 2007)
Frequently occurring short movements are interspersed with rarely occurring longer movements
(Reynolds and Rhodes, 2009)

## Slide 6: Network Topology
Topological Metrics | Definition | Ecological representation
Degree (k) | The number of edges of a node | Degree is based on the idea that important nodes have the largest number of links to other nodes
Efficiency(global) () | A measure of how efficiently it exchanges information | If efficiency is high, all patches tend to be easily reachable
Betweenness centrality (BC) | The fraction of shortest paths going through a given node k : the number of shortest path from node to node : the number of these shortest path that pass node from node to node | A stepping-stone to connect the shortest path between nodes
Topological Metrics | Definition | Ecological representation
Degree (k) |  | Degree is based on the idea that important nodes have the largest number of links to other nodes
 |  | If efficiency is high, all patches tend to be easily reachable
Betweenness centrality (BC) |  | A stepping-stone to connect the shortest path between nodes

## Slide 7: Site & Data for Simulation
Location: Big Sioux Basin Ecoregion (Level IV) in South Dakota, USA
Simulation Area: 30.5 km 30.5 km
Wetland Data: 5,534 wetlands (US Fish & Wildlife Service, 2017. 10.01)
Hydro-climate Data: 2010.1 ~ 2011.12 (NOAA )
Soil data: Pre-reported in USDA
Soil :

## Slide 8: Network Simulations – Area scenario
 | Maximum area of wetlands (m2) | Hydrologically filled by each area
Sc1 | < 400 | 0
 | 400 ⁓ 1500 | 30 %
 | 1,500 ⁓ 10,000 | 73 %
 | > 10,000 | 85 %
 | d | 
Sc2 | < 400 | 70 %
 | 400 ⁓ 1500 | 70 %
 | 1,500 ⁓ 10,000 | 69.6 %
 | > 10,000 | 60 %
 | d | 
Sc3 | Maximum area of all wetlands () | 
Sc4 | Maximum area of all wetlands except small wetlands () | 
 | Maximum area of wetlands (m2) | Hydrologically filled by each area
Sc1 | < 400 | 0
 | 400 ⁓ 1500 | 30 %
 | 1,500 ⁓ 10,000 | 73 %
 | > 10,000 | 85 %
Sc2 | < 400 | 70 %
 | 400 ⁓ 1500 | 70 %
 | 1,500 ⁓ 10,000 | 69.6 %
 | > 10,000 | 60 %
Sc3 |  | 
Sc4 |  | 
• Small wetlands: Under 400 m2 of all wetlands

## Slide 9: Results: k and BC distribution
Some wetlands play important structural (k) and functional (BC) roles in ecological network. And among small wetlands, some wetlands of high importance exist.
Different wetlands have different structural and functional roles (correlation coefficient: 0.61(all wetlands), 0.57(small wetlands))

## Slide 10: Results: Node deletion
The impact that reduces the network characteristics (<k> and E) appears differently depending on the deleted node’s function (k or BC).
Removal of some small wetlands (red) also have a significant impact on network degradation.
Removal by order of high k
Removal by order of high BC
Removal by order of high BC
Removal by order of high k

## Slide 11: Results: Temporal change of <k>
<k> decreased nearly 20% (yellow) when the function of small wetlands was lost (0.8% of total wetlands area), but recovered when small wetlands were filled by rainfall (blue)
SDI (Seasonal Climate Index)

## Slide 12: Results: Temporal change of E
E decreased nearly 25% (yellow) when the function of small wetlands was lost (0.8% of total wetlands area), but recovered when small wetlands were filled by rainfall (blue)
SDI (Seasonal Climate Index)

## Slide 13: Results: All cases of change of <k> and E
Ecological states (<k> and E) have multiple regimes according to hydrologically dried wetlands (loss of function) in similar ecological condition (sum of wetlands area)
Sc1 (recover small wetlands)
Sc4 (max area except small wetlands)
Sc1 (not recover small wetlands)
Sc3 (max area of all wetlands)
Sc2 (Large wetlands decreased)
Sc1 (recover small wetlands)
Sc4 (max area except small wetlands)
Sc1 (not recover small wetlands)
Sc3 (max area of all wetlands)
Sc2 (Large wetlands decreased)

## Slide 14: Conclusions
Different impact according to wetland functions
The role in the network differs depending on the function of the wetland (k or BC), and the impact caused by the loss of function also appears differently.
Some small wetlands play an important role and also have huge impact when their functions were lost.
Find multiple ecological states following the condition of small wetlands
In the case of extremely dry season, a large decrease in network function appears.
Both network metrics (<k> and E) decreased when small wetlands lose their function (hydrologically dry).
It is necessary to consider the function of the wetlands as well as the area or number of wetlands when establishing a conservation plan

## Slide 15: Thank You
Acknowledgements
This research was supported by National Research Foundation of Korea (NRF) funded by the Ministry of Education and Ministry of Science and ICT .
(NRF-2020R1A6A3A13075479, NRF-2020M3H5A108077511)

## Slide 16: Hydrology of GIWs: Dynamic Nodes
Dynamics of water volume (W)
]
-: Mean rainfall frequency []
-: Mean rainfall depth []
-: Effective contributing area []
: Evapotranspiration = (PET) X (water surface area)
-
: Exfiltration = (exfiltration rate) X (wetted area)
-

## Slide 17: Network Representation - Edge
Model Ⅰ: Threshold distance
(deterministic approach)
Any pair of wetlands less than the threshold distance apart are connected by undirected edges
Model Ⅱ: Exponential dispersal kernel
(probabilistic approach)
The probability function for dispersal distances of inhabiting species in a wetland

## Slide 18: Probabilistic Manipulation of Bathymetry
Wetland area – p relation
PDFs of wetland depths
Statistics of the data from Hayashi and van der Kamp (2000)

## Slide 19: Estimating Power-law Exponents
Estimate the parameter for each possible choice of using the method of maximum likelihood estimators (MLEs).
()
Calculate the Kolmogorov-Smirnov goodness-of-fit which generate value of (distance between two probability distribution) and select and that gives the minimum of goodness-of-fit.
L : Log-likelihood of the data under the fitted power law