## Slide 1
Stefania Camici(1), Gabriele Giuliani(1), Luca Brocca(1), Christian Massari(1), Angelica Tarpanelli(1), Marco Restano(2), and Jérôme Benveniste(3)
Research Insititute for Geo-hydrological Protection (IRPI), National Research Council (CNR), Italy
SERCO, ESA-ESRIN, Largo Galileo Galilei, Frascati, 00044, Italy
European Space Agency, ESA-ESRIN, Largo Galileo Galilei, Frascati, 00044, Italy
2021 European General Assembly 26-30 April, 2021
26 April 2021
Global runoff estimation through a regionalized STREAM model

## Slide 2
Precipitation
Evapo-
transpiration
THE PROBLEM: MODELS
WATER BUDGET MODEL
MODEL COMPLEXITY
REPRESENTED PROCESSES
ENERGY BUDGET MODEL
Global Hydrological Models
REAL WORLD
Land Surface Models
Catchment rainfall-runoff models
Notes: runoff can be estimated through model-based approaches whose outputs can be highly model or data dependent and characterised by large uncertainties.

## Slide 3
Precipitation
Evapo-
transpiration
WATER BUDGET MODEL
MODEL COMPLEXITY
REPRESENTED PROCESSES
ENERGY BUDGET MODEL
Catchment rainfall-runoff models
Global Hydrological Models
REAL WORLD
Land Surface Models
The STREAM model is a conceptual hydrological model, alternative to existing model-based runoff estimates, for deriving runoff estimates from the ESA Climate Change Initiative, ESA CCI, soil moisture (SM) product, the Tropical Rainfall Measuring Mission, TRMM 3B42 precipitation (P) product and terrestrial water storage anomalies (TWSA) from GRACE.
SaTellite based Runoff Evaluation And Mapping (STREAM) model
Notes: Whitin the SaTellite based Runoff Evaluation And Mapping (STREAM) PROJECT, an “observational” physically-based approach, alternative to existing model-based runoff estimates, has been developed and tested for deriving daily runoff estimates by using the ESA Climate Change Initiative, ESA CCI, soil moisture (SM) product, the Tropical Rainfall Measuring Mission, TRMM 3B42 precipitation (P) product and terrestrial water storage anomalies (TWSA) from GRACE.

## Slide 4
THE MODEL CONCEPT
Slow Flow
Quick Flow
Precipitation
Rainfall+Snowfall
Terrestrial Water Storage Anomalies
Soil Moisture
Total discharge
Quick Flow +
=
Slow Flow
Upper Storage
Lower Storage
RIVER DISCHARGE IS MADE UP OF TWO COMPONENTS
Camici et al. (2021). Synergy between satellite observations of soil moisture and water storage anomalies for global runoff estimation. Geosci. Model Dev. Discuss, In review.
https://doi.org/10.5194/gmd-2020-399

## Slide 5
Parameter | Description | Module | Range Variability | Unit
Cm | degree-day coefficient | Snow | 0.1/24-3 | [-]
 | exponent of infiltration | Soil | 1-30 | [-]
T | characteristic time length | Soil | 0.01-80 | [days]
β | coefficient relationship slow runoff component and TWSA | Soil | 0.1-20 | [mm h-1]
m | exponent in the relationship between slow runoff component and TWSA | Soil | 1-15 | [-]
 | parameter of GIUH | Routing | 0.5-5.5 | [-]
C | Celerity | Routing | 1-60 | [km h-1]
D | Diffusivity | Routing | 1-30 | [km2 h-1]
Parameter | Description | Module | Range Variability | Unit
Cm | degree-day coefficient | Snow | 0.1/24-3 | [-]
 | exponent of infiltration | Soil | 1-30 | [-]
T | characteristic time length | Soil | 0.01-80 | [days]
β | coefficient relationship slow runoff component and TWSA | Soil | 0.1-20 | [mm h-1]
m | exponent in the relationship between slow runoff component and TWSA | Soil | 1-15 | [-]
 | parameter of GIUH | Routing | 0.5-5.5 | [-]
C | Celerity | Routing | 1-60 | [km h-1]
D | Diffusivity | Routing | 1-30 | [km2 h-1]
THE MODEL PARAMETERS
EIGHT PARAMETERS NEED TO BE CALIBRATED
Camici et al. (2021, GMDD, In review). doi: 10.5194/gmd-2020-399

## Slide 6
THE PROCEDURE
STREAM MODEL CALIBRATION
Discharge gauging stations
Precipitation (TMPA 3B42)
Air Temperature (in situ)
Soil Moisture (ESA CCI)
Terrestrial Water Storage Anomalies (GRACE)
Digital Elevation Model
Location of gauging station
Sub-basin delineation
Input data extraction for each sub-basin
STREAM calibration
In situ river discharge reference stations
Processing steps
Reference data
Input data
STREAM gridded runoff (0.25-degree) and river discharge at the outlet of each sub-basin
Output data

## Slide 7
THE PROCEDURE
Precipitation (TMPA 3B42)
Air Temperature (in situ)
Soil Moisture (ESA CCI)
Terrestrial Water Storage Anomalies (GRACE)
Digital Elevation Model
Location of gauging station
Sub-basin delineation
Input data extraction for each sub-basin
STREAM model regionalization
Predictors (Aridity index, basin slope, soil texture)
STREAM gridded runoff (0.25-degree) and river discharge at the outlet of each sub-basin
STREAM MODEL REGIONALIZATION
Processing steps
Reference data
Input data
Output data

## Slide 8
STREAM MODEL REGIONALIZATION
T
Variables
m
Additional relations
Aridity Index
Slope
Bulk density
Subsilt
(30-100 cm)
Predictors
Variable- Predictor Relation
THE PROCEDURE
The regionalization of STREAM parameters has been setup for Mississippi and tested for Danube river basin

## Slide 9
Kling-Gupta Index (Gupta et al., 2009)
KGE= 0.52
SATISFACTORY
MODEL PERFORMANCE
r = correlation coefficient
α1 = relative variability between observed and simulated discharge
β1 = bias normalized by the standard deviation
-∞ KGE 0.1 | 0.1 KGE 0.4 | 0.4 KGE 0.7 | 0.7 KGE 1
UNSATISFACTORY MODEL RESULTS | UNSATISFACTORY MODEL RESULTS | ACCEPTABLE/GOOD MODEL RESULTS | VERY GOOD MODEL RESULTS
UNSATISFACTORY MODEL RESULTS | UNSATISFACTORY MODEL RESULTS | ACCEPTABLE/GOOD MODEL RESULTS | VERY GOOD MODEL RESULTS
KGE= -0.30
UNSATISFACTORY
MODEL PERFORMANCE
Correlation coefficient
Relative root mean square error
KGE, R AND RRMSE SCORES
PERFORMANCE INDICES

## Slide 10
Discharge and runoff estimates have been simulated for the period 2003-2017 for two basins, Mississippi and Danube characterized by different physiographic/climatic features.
STUDY AREAS
MISSISSIPPI AND DANUBE RIVER BASINS
Notes: The study areas comprises 5 pilot areas throughout the world (Mississippi, Amazon, Niger, Danube and Murray Darling) whose characteristcs are summarized in the table within the figure.

## Slide 11: MODEL PARAMETER CALIBRATION (cal) AND REGIONALIZATION (reg)
∆ KGE = KGEcal - KGEreg
Mean (∆ KGE) = 0.46
Vicksburg
KGEcal
KGE
Mean (KGEcal) = 0.66
Vicksburg
STREAM performances are good over all the sections except downstream dams. KGE index decreases over these sections in by using regionalized model parameters
MISSISSIPPI RIVER BASIN

## Slide 12: MODEL PARAMETER CALIBRATION (cal) AND REGIONALIZATION (reg)
∆ KGE = KGEcal - KGEreg
Mean (∆ KGE) = - 0.31
Ceatal Izmail
KGEcal
KGE
Mean (KGEcal) = 0.75
Ceatal Izmail
STREAM performances are still good when the model is run by using regionalized parameters
DANUBE RIVER BASIN

## Slide 13: MODEL PARAMETER CALIBRATION (cal) AND REGIONALIZATION (reg)
KGE
Mississippi
Danubio
R
RRMSE
KGE
R
RRMSE
cal
reg
cal
reg
cal
reg
0.77
0.60
0.78
0.75
0.44
0.64
Median values
0.78
0.43
0.81
0.67
0.33
0.59
Median values
MISSISSIPPI AND DANUBE RIVER BASINS

## Slide 14
TAKE HOME MESSAGE
STREAM results demonstrate that:
A conceptual approach using satellite soil moisture, precipitation and GRACE is able to provide good performances in river discharge estimation
Regionalization of STREAM parameters provide promising results for the model implementation at global scale
Next step: runoff estimation at global scale.
@Hydrology_IRPI
http://hydrology.irpi.cnr.it
stefania.camici@irpi.cnr.it
idrologia@irpi.cnr.it

## Slide 15: Thank you for having viewed the slides
"For further information on the STREAM model, please write to: stefania.camici@ irpi.cnr.it and visit: http://hydrology.irpi.cnr.it/projects/stream and https://eo4society.esa.int/projects/stream/ for updates"
@Hydrology_IRPI
http://hydrology.irpi.cnr.it
stefania.camici@irpi.cnr.it
idrologia@irpi.cnr.it