## Slide 1: Modelling the interplay of future changes and wastewater management measures on the microbiological river water quality considering safe drinking water production
Katalin Demeter1,2†‡, Julia Derx3†‡, Jürgen Komma3, Juraj Parajka3, Jack Schijven4,5, Regina Sommer6†, Silvia Cervero-Arago6†, Gerhard Lindner6†, Christa M. Zoufal-Hruza7, Rita Linke1†, Domenico Savio8†, Simone K. Ixenmaier1†, Alexander K.T. Kirschner6,8†, Harald Kromp9, Alfred P. Blaschke3†, Andreas H. Farnleitner1,8†*
1 Institute of Chemical, Environmental and Bioscience Engineering E166/5/3, TU Wien, Austria. 2 Center for Water Resource Systems E222, TU Wien, Austria. 3 Institute of Hydraulic Engineering and Water Resources Management E222/2, TU Wien, Austria. 4 Department of Statistics, Informatics and Modelling, National Institute for Public Health and the Environment (RIVM), The Netherlands. 5 Faculty of Geosciences, Department of Earth Sciences, Utrecht University, The Netherlands. 6 Institute for Hygiene and Applied Immunology, Medical University of Vienna, Austria. 7 Division of Hygiene, Municipal Department 39, City Administration Vienna, Austria. 8 Division Water Quality and Health, Department of Pharmacology, Physiology, and Microbiology, Karl Landsteiner University of Health Sciences, Austria. 9 Vienna Water, City Administration Vienna, Austria. † Interuniversity Cooperation Centre Water & Health (www.waterandhealth.at)
vEGU 2021, Session HS2.3.5, 30/04/2021

## Slide 2: 1. The WHO concept about water safety: assessing and managing health risk
≤ health-based target at the consumer
....from the catchment to the tap: a whole system approach
berlin.de
berlin.de

## Slide 3
Schijven et al. (2015) J. Environ. Qual. 44(5)
Derx et al. (2016) J. Environ. Qual. 45(4)
Demeter, Derx, et al. (2021) Sci. Total Environ. 768
Derx et al., vPICO talk in this session (HS2.3.5)!!
Identification and characterisation of faecal pollution – catchment survey & multiparametric monitoring
Concentration of microorganisms in water – microbial fate and transport model
Deriving the required log reduction of pathogens to meet a health-based target – QMRA
2. The QMRAcatch approach

## Slide 4
3. Aims and modelling approach
Decipher the interplay among future changes and measures
Regarding their effect on the required treatment of river water for safe drinking water supply
Viral index pathogens norovirus and enterovirus (plus protozoan and bacterial: Cryptosporidium and Campylobacter)
Using an integrative modelling approach

## Slide 5
Hydrological modelling
QMRAcatch model
Faecal sources
WWTPs
CSOs
QMRA
Required treatment of river water
River flow
Hydrological model
2 regional climate models + 3 greenhouse gas emmission scenarios
River transport and mixing
River temperature
Concentration of viruses and microorganisms in river water
* Calibration: human-associated MST marker + enterovirus

## Slide 6
 | Climate change (Qriver and Triver) | Population growth (Qeffluent) | CSO prevention | Enhanced ww. treatment
Reference | - | - | - | -
No management changes | + | + | - | -
CSO prevention | + | + | + | -
Enhanced ww. treatment | + | + | - | +
Both measures | + | + | + | +
Scenarios
Scenario
Change

## Slide 7
4. Results
4.1 Required treatment of river water for safe drinking water supply

## Slide 8
4. Results
4.2 Virus loads at the study site and relative source apportionment

## Slide 9: 5. Conclusions
QMRAcatch (v1.0 Python) extended & open source
Approach applicable and code adaptable to other rivers
Data usage in modelling: 1. calibration: MST marker (abundant, source-associated) 2. validation: (index) pathogen 3. scenarios: various index pathogens for scenarios
Enhanced wastewater treatment combined with preventing CSOs had the most significant positive effect
Climate change effect:
  Negligible in “no management changes” scenario (secondary treatment at WWTPs, major source of faecal pollution: WWTPs)
  Significant in “enhanced wastewater treatment scenario” through increased CSO frequency/volumes (major source of faecal pollution: CSOs; results here not shown, please refer to Demeter, Derx 2021)

## Slide 10: Thank you for your interest!
vEGU 2021, Session HS2.3.5, 30/04/2021
References:
Demeter, K., Derx, J., Komma, J., Parajka, J., Schijven, J., Sommer, R., Cervero-Arago, S., Lindner, G., Zoufal-Hruza, C.M., Linke, R., Savio, D., Ixenmaier, S.K., Kirschner, A.K.T., Kromp, H., Blaschke, A.P. and Farnleitner, A.H. (2021) Modelling the interplay of future changes and wastewater management measures on the microbiological river water quality considering safe drinking water production. Science of the Total Environment 768, 144278.
Schijven, J. F., J. Derx, A. M. de Roda Husman, A. P. Blaschke, A. H. Farnleitner. 2015. QMRAcatch: Microbial quality simulation of water resources including infection risk assessment. J. Env. Qual. 44(5): 1491-1502
Free download of QMRAcatch (Schijven et al. 2015) at www.waterandhealth.at
QMRAcatch (v1.0 Python, Demeter et al. 2021) available on request: derx@hydro.tuwien.ac.at