## Slide 1: Impact of irrigation and soil compaction on salinization of soils in semiarid agricultural lands
Sina Maghami Nick1, Seyedmehdi Emadian1, Selen Deviren Saygın2, Muhittin Onur Akça2, Burak Demirel1, Hasan Sabri Öztürk2, Majid Sedighi4, Masoud Babaei3, and Nadim K. Copty1
1Environmental Sciences, Bogazici University, Istanbul, Turkey (sina.maghami@boun.edu.tr)
2Soil Science and Plant Nutrition, Ankara University, Ankara, Turkey
3Mechanical, Aerospace & Civil Engineering, The University of Manchester, Manchester, United Kingdom
4Chemical Engineering & Analytical Science, The University of Manchester, Manchester, United Kingdom
This work was supported by the Scientific and Technological Research Council of Turkey [Project number: TUBİTAK-118Y343] and British Council [Project number: 414693137]

## Slide 2: Columns
Constant 30°C at surface controlled
by infrared lamps

## Slide 3: Experiments
Experiment A
Saline flood irrigation
Experiment B
Experiment C
Fresh water (DI) flood irrigation
Experiment D
Fresh water (DI) drip irrigation
Saline drip irrigation
Experiment E
Fresh water (DI) flood irrigation with free drainage

## Slide 4: Flood irrigation cycles
1 litre of water (~5cm head) applied in one-go to the surface of the columns
Each phase consisted of 4-5 irrigations performed in 3-4 day gaps
Light was off during the irrigation
Soil water was extracted at 5 different heights before and after the irrigation
For the saline water phase, the water composition was same as the tank

## Slide 5: Drip irrigation cycles
250 ml of water (~1.25 cm head) is applied over 50 minutes ( 5 ml/min)
It was done for 4 consecutive days.
3 days rest
Soil water was extracted at 5 different heights before and after each 50 min cycle
For the saline water phase, the water composition was same as the tank